## Slide 1: 网络与分布式计算
Networks and Distributed Computing
Slides are adapted from those of by J.F Kurose and K.W. Ross with copyright 1996-2020 J.F Kurose and K.W. Ross, All Rights Reserved

## Slide 2: Networks and Distributed Computing
Jicheng Hu
CS, Wuhan University
jichengwhu @ 163 . com
https://github.com/network-distributed
Room E315, E-WING, Building of Computer Science
Phone (office): 027-68776033

## Slide 3: Textbook
James F. Kurose and Keith W. Ross, Computer Networking: A Top Down Approach , 8th edition. Pearson Education, 2021.
Kasun Indrasiri and Danesh Kuruppu, gRPC: Up and Running Building Cloud Native Applications with Go and Java for Docker and Kubernetes, O’Reilly, 2020
Slides of this course are adapted from J.F Kurose and K.W. Ross

## Slide 4: Some Ground Rules
To make sure that things do not get out of hand, please…
  Keep quiet in class
  Practice (via Wireshark) and coding (via VS2022 community)
  Be here
  Be here on time
Let's make this educational, academic and enjoyable.
reading
searching & research
coding

## Slide 5: Assessment for the course
Final Exam – 70 %
Course Work – 30 %
    Lab Reports – will be separately graded as a lab course
    Test / codes – 10 %
    Assignment/Quiz – 10 %
    Attendance/tutorials – 10 %

## Slide 6: Now let's begin ...

## Slide 7: Chapter 1: Introduction
Our goal:
get "feel" and terminology
more depth, detail later in course
approach:
  use Internet as example
Overview:
what's the Internet?
what's a protocol?
network edge; hosts, access net, physical media
network core: packet/circuit switching, Internet structure
performance: loss, delay, throughput
security
protocol layers, service models
history

## Slide 8: Chapter 1: outline
  1.1 What is the Internet?
  1.2 Network edge
    end systems, access networks, links
  1.3 Network core
    circuit switching, packet switching, network structure
  1.4 Delay, loss and throughput in packet-switched networks
  1.5 Protocol layers, service models
  1.6 Networks under attack: security
  1.7 History

## Slide 9: What's the Internet: "nuts and bolts" view
billions of connected computing devices:
  hosts = end systems
  running network apps
communication links
  fiber, copper, radio, satellite
  transmission rate: bandwidth
packet switches: forward packets (chunks of data)
  routers and switches
wired
links
wireless
links
router
smartphone
PC
server
wireless
laptop
mobile network
global ISP
regional ISP
home
network
institutional
network
Notes: 9

## Slide 10: "Fun" Internet-connected devices
IP picture frame
http://www.ceiva.com/
Web-enabled toaster +
weather forecaster
Internet phones
Internet
refrigerator
Slingbox: watch,
control cable TV remotely
Tweet-a-watt:
monitor energy use
sensorized,
bed
mattress
Xiaomi
aibox

## Slide 11
Internet: "network of networks"
  Interconnected ISPs
protocols control sending, receiving of messages
  e.g., TCP, IP, HTTP, Skype, 802.11
Internet standards
  RFC: Request for comments
  IETF: Internet Engineering Task Force
What's the Internet: "nuts and bolts" view
mobile network
global ISP
regional ISP
home
network
institutional
network

## Slide 12: What's the Internet: a service view
infrastructure that provides services to applications
  Web, VoIP, email, games, e-commerce, social nets, AI, …
provides programming interface to apps
  hooks that allow sending and receiving app programs to "connect" to Internet
  provides service options, analogous to postal service
mobile network
global ISP
regional ISP
home
network
institutional
network

## Slide 13: What's a protocol?
human protocols:
"what's the time?"
"I have a question"
introductions
… specific messages sent
… specific actions taken when messages received, or other events
network protocols:
machines rather than humans
all communication activity in Internet governed by protocols
protocols define format, order of messages sent and received among network entities, and actions taken on message transmission, receipt

## Slide 14
a human protocol and a computer network protocol:
Q: other human protocols?
Hi
Hi
Got the
time?
2:00
TCP connection
response
Get http://www.github.com/network-distributed
<file>
time
TCP connection
request
What's a protocol?

## Slide 15: Chapter 1: roadmap
  1.1 what is the Internet?
  1.2 network edge
    end systems, access networks, links
  1.3 network core
    packet switching, circuit switching, network structure
  1.4 delay, loss, throughput in networks
  1.5 protocol layers, service models
  1.6 networks under attack: security
  1.7 history
Notes: 15

## Slide 16: A closer look at network structure:
network edge:
  hosts: clients and servers
  servers often in data centers
access networks, physical media: wired, wireless communication links
network core:
  interconnected routers
  network of networks
mobile network
global ISP
regional ISP
home
network
institutional
network

## Slide 17: Access networks and physical media
Q: How to connect end systems to edge router?
residential access nets
institutional access networks (school, company)
mobile access networks
keep in mind:
bandwidth (bits per second) of access network?
shared or dedicated?

## Slide 18: Access network: digital subscriber line (DSL)
ISP
central office
telephone
network
DSLAM
voice, data transmitted
at different frequencies over
dedicated line to central office
  use existing telephone line to central office DSLAM
    data over DSL phone line goes to Internet
    voice over DSL phone line goes to telephone net
  < 2.5 Mbps upstream transmission rate (typically < 1 Mbps)
  < 24 Mbps downstream transmission rate (typically < 10 Mbps)
DSL
modem
splitter
DSL access
multiplexer

## Slide 19
Access network: cable network
cable
modem
splitter
…
cable headend
Channels
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
D
A
T
A
D
A
T
A
C
O
N
T
R
O
L
1
2
3
4
5
6
7
8
9
frequency division multiplexing: different channels transmitted
in different frequency bands

## Slide 20
ISP
data, TV transmitted at different
frequencies over shared cable
distribution network
cable
modem
splitter
…
cable headend
CMTS
cable modem
termination system
HFC: hybrid fiber coax
  asymmetric: up to 30Mbps downstream transmission rate, 2 Mbps upstream transmission rate
network of cable, fiber attaches homes to ISP router
  homes share access network to cable headend
  unlike DSL, which has dedicated access to central office
Access network: cable network

## Slide 21
Access network: home network
to/from headend or central office
cable or DSL modem
router, firewall, NAT
wired Ethernet (1 Gbps)
wireless access
point (54 Mbps)
wireless
devices
often combined
in single box

## Slide 22: Enterprise access networks (Ethernet)
typically used in companies, universities, etc.
  10 Mbps, 100Mbps, 1Gbps, 10Gbps transmission rates
  today, end systems typically connect into Ethernet switch
  Industrial Ethernet - the use of Ethernet in an industrial environment with protocols that provide determinism and real-time control
Ethernet
switch
institutional mail,
web servers
institutional router
institutional link to
ISP (Internet)

## Slide 23: Wireless access networks
shared wireless access network connects end system to router
  via base station aka "access point"
wireless LANs:
  within building (100 ft.)
  802.11b/g/n/ac/ax (WiFi): 11M, 54M, 450M, 1G, 4G bps transmission rate
wide-area wireless access
  provided by telco (cellular) operator, 10's km
  between 1 and 10 Mbps
  3G, 4G: LTE, 5G(10Gbps)
to Internet
to Internet
Notes: 5G网络的主要优势在于，数据传输速率远远高于以前的蜂窝网络，最高可达10Gbit/s，比当前的有线互联网要快，比先前的4G LTE蜂窝网络快100倍。另一个优点是较低的网络延迟（更快的响应时间），低于1毫秒，而4G为30-70毫秒。

## Slide 24: Host: sends packets of data
host sending function:
takes application message
breaks into smaller chunks, known as packets, of length L bits
transmits packet into access network at transmission rate R
  link transmission rate, aka link capacity, aka link bandwidth
R: link transmission rate
host
1
2
two packets,
L bits each
packet
transmission
delay
time needed to
transmit L-bit
packet into link
L (bits)
R (bits/sec)
=
=

## Slide 25: Physical media
bit: propagates between transmitter/receiver pairs
physical link: what lies between transmitter & receiver
guided media:
  signals propagate in solid media: copper, fiber, coax
unguided media:
  signals propagate freely, e.g., radio
twisted pair (TP)
two insulated copper wires
  Category 5: 100 Mbps, 1 Gbps Ethernet
  Category 6: 10Gbps
Notes: wave-guided

## Slide 26: Physical media: coax, fiber
coaxial cable:
two concentric copper conductors
bidirectional
broadband:
  multiple channels on cable
  HFC
fiber optic cable:
glass fiber carrying light pulses, each pulse a bit
high-speed operation:
  high-speed point-to-point transmission (e.g., 10’s-100’s Gbps transmission rate)
low error rate:
  repeaters spaced far apart
  immune to electromagnetic noise

## Slide 27: Physical media: radio
signal carried in electromagnetic spectrum
no physical "wire"
bidirectional
propagation environment effects:
  reflection
  obstruction by objects
  interference
radio link types:
terrestrial microwave
  e.g. up to 45 Mbps channels
LAN (e.g., WiFi)
  54 Mbps
wide-area (e.g., cellular)
  4G cellular: ~ 10 Mbps
satellite
  Kbps to 45Mbps channel (or multiple smaller channels)
  270 msec end-end delay
  geosynchronous versus low altitude

## Slide 28: Chapter 1: roadmap
  1.1 what is the Internet?
  1.2 network edge
    end systems, access networks, links
  1.3 network core
    packet switching, circuit switching, network structure
  1.4 delay, loss, throughput in networks
  1.5 protocol layers, service models
  1.6 networks under attack: security
  1.7 history
Notes: 28

## Slide 29: The network core
mesh of interconnected routers
packet-switching: hosts break application-layer messages into packets
  forward packets from one router to the next, across links on path from source to destination
  each packet transmitted at full link capacity

## Slide 30: Packet-switching: store-and-forward
takes L/R seconds to transmit (push out) L-bit packet into link at R bps
store and forward: entire packet must arrive at router before it can be transmitted on next link
one-hop numerical example:
L = 7.5 Mbits
R = 1.5 Mbps
one-hop transmission delay = 5 sec
more on delay shortly …
source
R bps
destination
1
2
3
L bits
per packet
R bps
end-end delay = 2L/R (assuming zero propagation delay)

## Slide 31: Packet Switching: queueing delay, loss
A
B
C
R = 100 Mb/s
R = 1.5 Mb/s
D
E
queue of packets
waiting for output link
queuing and loss:
if arrival rate (in bits) to link exceeds transmission rate of link for a period of time:
  packets will queue, wait to be transmitted on link
  packets can be dropped (lost) if memory (buffer) fills up
to section 1.4

## Slide 32: Two key network-core functions
forwarding: move packets from router’s input to appropriate router output
routing: determines source-destination route taken by packets
  routing algorithms
routing algorithm
local forwarding table
header value
output link
0100
0101
0111
1001
3
2
2
1
1
2
3
0111
destination address in arriving
packet’s header

## Slide 33: Alternative core: circuit switching
end-end resources allocated to, reserved for "call" between source & dest:
in diagram, each link has four circuits.
  call gets 2nd circuit in top link and 1st circuit in right link.
dedicated resources: no sharing
  circuit-like (guaranteed) performance
circuit segment idle if not used by call (no sharing)
commonly used in traditional telephone networks

## Slide 34: Circuit switching: FDM versus TDM
FDM
frequency
time
TDM
frequency
time
4 users
Example:
Notes: Two simple multiple access control techniques.
Each mobile’s share of the bandwidth is divided into portions for the uplink and the downlink. Also, possibly, out of band signaling.
As we will see, used in AMPS, GSM, IS-54/136

## Slide 35: Packet switching versus circuit switching
example:
1 Mb/s link
each user:
  100 kb/s when "active"
  active 10% of time
circuit-switching:
  10 users
packet switching:
  with 35 users, probability > 10 active at same time is less than .0004 *
packet switching allows more users to use network!
N
users
1 Mbps link
Q: how did we get value 0.0004?
Q: what happens if > 35 users ?
…..
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/

## Slide 36
great for bursty data
  resource sharing
  simpler, no call setup
excessive congestion possible: packet delay and loss
  protocols needed for reliable data transfer, congestion control
Q: How to provide circuit-like behavior?
  bandwidth guarantees needed for audio/video apps
  still an unsolved problem (chapter 7)
is packet switching a "slam dunk winner?"
Q: human analogies of reserved resources (circuit switching) versus on-demand allocation (packet-switching)?
Packet switching versus circuit switching

## Slide 37: Internet structure: network of networks
End systems connect to Internet via access ISPs (Internet Service Providers)
  residential, company and university ISPs
Access ISPs in turn must be interconnected.
  so that any two hosts can send packets to each other
Resulting network of networks is very complex
  evolution was driven by economics and national policies
Let’s take a stepwise approach to describe current Internet structure

## Slide 38: Internet structure: network of networks
Question: given millions of access ISPs, how to connect them together?
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…

## Slide 39: Internet structure: network of networks
Option: connect each access ISP to every other access ISP?
access
net
access
net
…
…
…
…
…
…
…
…
connecting each access ISP to each other directly doesn’t scale: O(N2) connections.
access
net
access
net
access
net
access
net
access
net
access
net
…
access
net
access
net
access
net
access
net
…
access
net
access
net
access
net
access
net
…

## Slide 40: Internet structure: network of networks
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
Option: connect each access ISP to one global transit ISP?
Customer and provider ISPs have economic agreement.
global ISP
Notes: Transit center: 换乘中心

## Slide 41: Internet structure: network of networks
ISP C
ISP B
ISP A
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
But if one global ISP is viable business, there will be competitors ….
access
net

## Slide 42: Internet structure: network of networks
ISP C
ISP B
ISP A
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
access
net
But if one global ISP is viable business, there will be competitors …. which must be interconnected
IXP
peering link
Internet exchange point
IXP

## Slide 43: Internet structure: network of networks
ISP C
ISP B
ISP A
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
access
net
IXP
IXP
access
net
access
net
access
net
regional net
… and regional networks may arise to connect access nets to ISPs

## Slide 44: Internet structure: network of networks
ISP C
ISP B
ISP A
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
access
net
IXP
IXP
access
net
access
net
access
net
regional net
Content provider network
… and content provider networks (e.g., Google, Microsoft, Akamai) may run their own network, to bring services, content close to end users

## Slide 45: Internet structure: network of networks
at center: small # of well-connected large networks
  "tier-1" commercial ISPs (e.g., Level 3, Sprint, AT&T, NTT), national & international coverage
  content provider network (e.g., Google): private network that connects it data centers to Internet, often bypassing tier-1, regional ISPs
IXP
IXP
IXP
Tier 1 ISP
Tier 1 ISP
Google
Regional ISP
Regional ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP

## Slide 46: Tier-1 ISP: e.g., Sprint
…
to/from customers
peering
to/from backbone
multi-home
…
…
…
…
POP: point-of-presence
Notes: Peering: 对等操作
Transit: 不对等
上网搜索两者的差异
节点(POP): A point-of-presence is a physical location where two or more types of communication devices can establish a connection
http://www.cnpaf.net/Class/p/200510/8396.html: 在因特网上，一个节点（POP）是一个从一个位置到因特网的其它部分的进入点。一个节点必然地有一个独特的因特网（IP）位址。因特网服务提供者或在线服务供应者（比如美国在线公司）有在因特网上一个或多个节点。因特网服务提供者或在线服务供应者拥有的节点的数量有时被用来衡量这些公司的规模和成长速率。 一个节点可能实际上属于通讯公司所有，因特网服务提供者可以租借其空间来提供服务。一个节点通常包含路由器，数字/模拟信号转换器，服务器，经常还有架框继电器或非同步传输模式开关。
Multi-home: 多宿

## Slide 47: Homework
ping另外一台计算机
tracert 一个服务器
申请github账户，下载相关资源https://github.com/wireshark/wireshark
作业使用markdown格式或word(强烈建议用markdown)
用github将作业提交到课代表
作业命名格式：学号_姓名.md
每次作业在一周内提交（每次课前提交上次作业）

## Slide 48: Chapter 1: roadmap
  1.1 what is the Internet?
  1.2 network edge
    end systems, access networks, links
  1.3 network core
    packet switching, circuit switching, network structure
  1.4 delay, loss, throughput in networks
  1.5 protocol layers, service models
  1.6 networks under attack: security
  1.7 history
Notes: 48
回顾第30-31张幻灯片

## Slide 49: How do loss and delay occur?
A
B
packets queue in router buffers
packet arrival rate to link (temporarily) exceeds output link capacity
packets queue, wait for turn
packet being transmitted (delay)
packets queueing (delay)
free (available) buffers: arriving packets
dropped (loss) if no free buffers

## Slide 50: Four sources of packet delay
dproc: nodal processing
check bit errors
determine output link
typically < msec
dqueue: queueing delay
time waiting at output link for transmission
depends on congestion level of router
propagation
nodal
processing
queueing
dnodal = dproc + dqueue + dtrans + dprop
A
B
transmission

## Slide 51
dtrans: transmission delay:
L: packet length (bits)
R: link bandwidth (bps)
dtrans = L/R
dprop: propagation delay:
d: length of physical link
s: propagation speed (~2x108 m/sec)
dprop = d/s
Four sources of packet delay
* Check out the Java applet for an interactive animation on trans vs. prop delay
dtrans and dprop
very different
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/
propagation
nodal
processing
queueing
dnodal = dproc + dqueue + dtrans + dprop
A
B
transmission
Notes: 51

## Slide 52: Caravan analogy
cars "propagate" at 100 km/hr
toll booth takes 12 sec to service car (bit transmission time)
car ~ bit; caravan ~ packet
Q: How long until caravan is lined up before 2nd toll booth?
time to "push" entire caravan through toll booth onto highway = 12*10 = 120 sec
time for last car to propagate from 1st to 2nd toll both: 100km/(100km/hr)= 1 hr
A: 62 minutes
toll
booth
toll
booth
ten-car
caravan
100 km
100 km

## Slide 53: Caravan analogy (more)
suppose cars now "propagate" at 1000 km/hr
and suppose toll booth now takes one min to service a car
Q: Will cars arrive to 2nd booth before all cars serviced at first booth?
A: Yes! after 7 min, first car arrives at second booth; three cars still at first booth
toll
booth
toll
booth
ten-car
caravan
100 km
100 km

## Slide 54: Queueing delay (revisited)
R: link bandwidth (bps)
L: packet length (bits)
a: average packet arrival rate
traffic intensity
= La/R
La/R ~ 0: avg. queueing delay small
La/R → 1: avg. queueing delay large
La/R > 1: more "work" arriving
than can be serviced, average delay infinite!
average queueing delay
La/R ~ 0
La/R → 1
* Check online interactive animation on queuing and loss
average cnt # of arrived packets

## Slide 55: "Real" Internet delays and routes
what do "real" Internet delay & loss look like?
traceroute program: provides delay measurement from source to router along end-end Internet path towards destination. For all i:
  sends three packets that will reach router i on path towards destination
  router i will return packets to sender
  sender times interval between transmission and reply.
3 probes
3 probes
3 probes
probe via ICMP
Notes: ICMP
Traceroute的用法为: Traceroute [options] <IP-address or domain-name> [data size]
[options]的内容有:
[-n]:显示的地址是用数字表示而不是符号
[-v]:长输出
[-p]:UDP端口设置(缺省为33434)
[-q]:设置TTL测试数目(缺省为3)
[-t]:设置测包的服务类型
[data size]:每次测试包的数据字节长度(缺省为38)

## Slide 56: "Real" Internet delays, routes
1 cs-gw (128.119.240.254) 1 ms 1 ms 2 ms
2 border1-rt-fa5-1-0.gw.umass.edu (128.119.3.145) 1 ms 1 ms 2 ms
3 cht-vbns.gw.umass.edu (128.119.3.130) 6 ms 5 ms 5 ms
4 jn1-at1-0-0-19.wor.vbns.net (204.147.132.129) 16 ms 11 ms 13 ms
5 jn1-so7-0-0-0.wae.vbns.net (204.147.136.136) 21 ms 18 ms 18 ms
6 abilene-vbns.abilene.ucaid.edu (198.32.11.9) 22 ms 18 ms 22 ms
7 nycm-wash.abilene.ucaid.edu (198.32.8.46) 22 ms 22 ms 22 ms
8 62.40.103.253 (62.40.103.253) 104 ms 109 ms 106 ms
9 de2-1.de1.de.geant.net (62.40.96.129) 109 ms 102 ms 104 ms
10 de.fr1.fr.geant.net (62.40.96.50) 113 ms 121 ms 114 ms
11 renater-gw.fr1.fr.geant.net (62.40.103.54) 112 ms 114 ms 112 ms
12 nio-n2.cssi.renater.fr (193.51.206.13) 111 ms 114 ms 116 ms
13 nice.cssi.renater.fr (195.220.98.102) 123 ms 125 ms 124 ms
14 r3t2-nice.cssi.renater.fr (195.220.98.110) 126 ms 126 ms 124 ms
15 eurecom-valbonne.r3t2.ft.net (193.48.50.54) 135 ms 128 ms 133 ms
16 194.214.211.25 (194.214.211.25) 126 ms 128 ms 126 ms
17 * * *
18 * * *
19 fantasia.eurecom.fr (193.55.113.142) 132 ms 128 ms 136 ms
traceroute: gaia.cs.umass.edu to www.eurecom.fr
3 delay measurements from
gaia.cs.umass.edu to cs-gw.cs.umass.edu
* means no response (probe lost, router not replying)
trans-oceanic
link
* Do some traceroutes from exotic countries at www.traceroute.org

## Slide 57: "Real" Internet delays, routes
1 134.79.197.131 (134.79.197.131) [AS3671] 0.599 ms
2 rtr-core2-p2p-serv01-02.slac.stanford.edu (134.79.253.253) [AS3671] 0.502 ms
3 rtr-fwcore1-trust-p2p-core1.slac.stanford.edu (134.79.254.134) [AS3671] 0.914 ms
4 rtr-core2-p2p-fwcore2-untrust.slac.stanford.edu (134.79.254.149) [AS3671] 1.366 ms
5 rtr-border2-7k-core1.slac.stanford.edu (134.79.252.181) [AS3671] 1.304 ms
6 sunncr5-ip-c-slac.slac.stanford.edu (192.68.191.233) [AS3671] 1.692 ms
7 210.25.189.141 (210.25.189.141) [AS4538] 10.957 ms
8 *
9 210.25.187.42 (210.25.187.42) [AS4538] 163.984 ms
10 210.25.187.45 (210.25.187.45) [AS4538] 163.857 ms
11 210.25.189.69 (210.25.189.69) [AS4538] 166.290 ms
12 101.4.116.81 (101.4.116.81) [AS4538] 163.201 ms
13 101.4.114.230 (101.4.114.230) [AS4538] 183.698 ms
14 wh1.cernet.net (202.112.53.82) [AS4538] 181.983 ms
15 218.197.158.253 (218.197.158.253) [AS4538] 182.566 ms
traceroute: www.slac.stanford.edu to www.whu.edu.cn

## Slide 58: Packet loss
queue (aka buffer) preceding link in buffer has finite capacity
packet arriving to full queue dropped (aka lost)
lost packet may be retransmitted by previous node, by source end system, or not at all
A
B
packet being transmitted
packet arriving to
full buffer is lost
buffer
(waiting area)
* Check out the Java applet for an interactive animation on queuing and loss

## Slide 59: Throughput
throughput: rate (bits/time unit) at which bits transferred between sender/receiver
  instantaneous: rate at given point in time
  average: rate over longer period of time
server, with
file of F bits
to send to client
link capacity
Rs bits/sec
link capacity
Rc bits/sec
server sends bits
(fluid) into pipe
pipe that can carry
fluid at rate
Rs bits/sec)
pipe that can carry
fluid at rate
Rc bits/sec)

## Slide 60: Throughput (more)
Rs < Rc What is average end-end throughput?
Rs bits/sec
Rc bits/sec
Rs > Rc What is average end-end throughput?
link on end-end path that constrains end-end throughput
bottleneck link
Rs bits/sec
Rc bits/sec

## Slide 61: Throughput: Internet scenario
per-connection end-end throughput: min(Rc,Rs,R/10)
in practice: Rc or Rs is often bottleneck
10 connections (fairly) share backbone bottleneck link R bits/sec
Rs
Rs
Rs
Rc
Rc
Rc
R
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/

## Slide 62: Chapter 1: roadmap
  1.1 what is the Internet?
  1.2 network edge
    end systems, access networks, links
  1.3 network core
    packet switching, circuit switching, network structure
  1.4 delay, loss, throughput in networks
  1.5 protocol layers, service models
  1.6 networks under attack: security
  1.7 history
Notes: 62

## Slide 63: Protocol "layers"
Networks are complex,
with many "pieces":
  hosts
  routers
  links of various media
  applications
  protocols
  hardware, software
Question:
is there any hope of organizing structure of network?
…. or at least our discussion of networks?

## Slide 64: Organization of air travel
a series of steps
ticket (purchase)
baggage (check)
gates (load)
runway takeoff
airplane routing
ticket (complain)
baggage (claim)
gates (unload)
runway landing
airplane routing
airplane routing

## Slide 65: Layering of airline functionality
layers: each layer implements a service
  via its own internal-layer actions
  relying on services provided by layer below
ticket (purchase)
baggage (check)
gates (load)
runway (takeoff)
airplane routing
departure
airport
arrival
airport
intermediate air-traffic
control centers
airplane routing
airplane routing
ticket (complain)
baggage (claim)
gates (unload)
runway (land)
airplane routing
ticket
baggage
gate
takeoff/landing
airplane routing

## Slide 66: Why layering?
dealing with complex systems:
explicit structure allows identification, relationship of complex system’s pieces
  layered reference model for discussion
modularization eases maintenance, updating of system
  change of implementation of layer’s service transparent to rest of system
  e.g., change in gate procedure doesn’t affect rest of system
layering considered harmful?

## Slide 67: Internet protocol stack
application: supporting network applications
  FTP, SMTP, HTTP
transport: process-process data transfer
  TCP, UDP
network: routing of datagrams from source to destination
  IP, routing protocols
link: data transfer between neighboring network elements
  Ethernet, 802.11 (WiFi), PPP
physical: bits "on the wire"
application
transport
network
link
physical

## Slide 68: ISO/OSI reference model
presentation: allow applications to interpret meaning of data, e.g., encryption, compression, machine-specific conventions
session: synchronization, checkpointing, recovery of data exchange
Internet stack "missing" these layers!
  these services, if needed, must be implemented in application
  needed?
application
presentation
session
transport
network
link
physical

## Slide 69: Encapsulation
source
application
transport
network
link
physical
Ht
Hn
M
segment
Ht
datagram
destination
application
transport
network
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
M
M
network
link
physical
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
Hn
M
Ht
Hn
Hl
M
router
switch
message
M
Ht
M
Hn
frame

## Slide 70: Chapter 1: roadmap
  1.1 what is the Internet?
  1.2 network edge
    end systems, access networks, links
  1.3 network core
    packet switching, circuit switching, network structure
  1.4 delay, loss, throughput in networks
  1.5 protocol layers, service models
  1.6 networks under attack: security
  1.7 history
Notes: 70

## Slide 71: Network security
field of network security:
  how bad guys can attack computer networks
  how we can defend networks against attacks
  how to design architectures that are immune to attacks
Internet not originally designed with (much) security in mind
  original vision: "a group of mutually trusting users attached to a transparent network" 
  Internet protocol designers playing "catch-up"
  security considerations in all layers!

## Slide 72: Bad guys: put malware into hosts via Internet
malware can get in host from:
  virus: self-replicating infection by receiving/executing object (e.g., e-mail attachment)
  worm: self-replicating infection by passively receiving object that gets itself executed
spyware malware can record keystrokes, web sites visited, upload info to collection site
infected host can be enrolled in botnet, used for spam. DDoS attacks

## Slide 73
Denial of Service (DoS): attackers make resources (server, bandwidth) unavailable to legitimate traffic by overwhelming resource with bogus traffic
target
1. select target
2. break into hosts around the network (see botnet)
3. send packets to target from compromised hosts
Bad guys: attack server, network infrastructure

## Slide 74: Bad guys can sniff packets
packet "sniffing":
  broadcast media (shared Ethernet, wireless)
  promiscuous network interface reads/records all packets (e.g., including passwords!) passing by
A
B
C
src:B dest:A payload
  wireshark software used for end-of-chapter labs is a (free) packet-sniffer
  https://github.com/wireshark/wireshark
Notes: promiscuous mode：混杂模式

## Slide 75: Bad guys can use fake addresses
IP spoofing: send packet with false source address
A
B
C
src:B dest:A payload
… lots more on security (throughout, Chapter 8)

## Slide 76: Chapter 1: roadmap
  1.1 what is the Internet?
  1.2 network edge
    end systems, access networks, links
  1.3 network core
    packet switching, circuit switching, network structure
  1.4 delay, loss, throughput in networks
  1.5 protocol layers, service models
  1.6 networks under attack: security
  1.7 history
Notes: 76

## Slide 77: Internet history
1961: Kleinrock - queueing theory shows effectiveness of packet-switching
1964: Baran - packet-switching in military nets
1967: ARPAnet conceived by Advanced Research Projects Agency
1969: first ARPAnet node operational
1972:
  ARPAnet public demo
  NCP (Network Control Protocol) first host-host protocol
  first e-mail program
  ARPAnet has 15 nodes
1961-1972: Early packet-switching principles

## Slide 78
1970: ALOHAnet satellite network in Hawaii
1974: Cerf and Kahn - architecture for interconnecting networks
1976: Ethernet at Xerox PARC
late70’s: proprietary architectures: DECnet, SNA, XNA
late 70’s: switching fixed length packets (ATM precursor)
1979: ARPAnet has 200 nodes
Cerf and Kahn’s internetworking principles:
  minimalism, autonomy - no internal changes required to interconnect networks
  best effort service model
  stateless routers
  decentralized control
define today’s Internet architecture
1972-1980: Internetworking, new and proprietary nets
Internet history

## Slide 79
1983: deployment of TCP/IP
1982: smtp e-mail protocol defined
1983: DNS defined for name-to-IP-address translation
1985: ftp protocol defined
1988: TCP congestion control
new national networks: CSnet, BITnet, NSFnet, Minitel
100,000 hosts connected to confederation of networks
1980-1990: new protocols, a proliferation of networks
Internet history

## Slide 80
early 1990’s: ARPAnet decommissioned
1991: NSF lifts restrictions on commercial use of NSFnet (decommissioned, 1995)
early 1990s: Web
  hypertext [Bush 1945, Nelson 1960’s]
  HTML, HTTP: Berners-Lee
  1994: Mosaic, later Netscape
  late 1990’s: commercialization of the Web
late 1990’s – 2000’s:
more killer apps: instant messaging, P2P file sharing
network security to forefront
est. 50 million host, 100 million+ users
backbone links running at Gbps
1990, 2000’s: commercialization, the Web, new apps
Internet history

## Slide 81
2005-present
~5B devices attached to Internet (2016)
  smartphones and tablets
aggressive deployment of broadband access
increasing ubiquity of high-speed wireless access
emergence of online social networks:
  Facebook: ~ one billion users
service providers (Google, Microsoft) create their own networks
  bypass Internet, providing "instantaneous" access to search, video content, email, etc.
e-commerce, universities, enterprises running their services in "cloud" (e.g., Amazon EC2)
Internet history

## Slide 82: Introduction: summary
covered a "ton" of material!
Internet overview
what's a protocol?
network edge, core, access network
  packet-switching versus circuit-switching
  Internet structure
performance: loss, delay, throughput
layering, service models
security
history
you now have:
context, overview, "feel" of networking
more depth, detail to follow!

## Slide 83
Chapter 1 Additional Slides

## Slide 84
Transport (TCP/UDP)
Network (IP)
Link (Ethernet)
Physical
application
(www browser,
email client)
application
OS
packet
capture
(pcap)
packet
analyzer
copy of all Ethernet frames sent/received

## Slide 85: Homework
课本第一章习题任意选做3道
下一次课为实验课, 请先从 github.com/network-distributed 上下载相关资料并预习