## Slide 1: Chapter 4 Network Layer: The Data Plane
Slides are adapted from those of by J.F Kurose and K.W. Ross with copyright 1996-2020 J.F Kurose and K.W. Ross, All Rights Reserved

## Slide 2: Network Layer Data Plane: our goals
understand principles behind network layer services, focusing on data plane:
  network layer service models
  forwarding versus routing
  generalized forwarding
  how a router works
  Internet architecture
instantiation, implementation in the Internet
  IP protocol
  NAT, middleboxes

## Slide 3: Network Layer Data Plane: roadmap
Network layer: overview
  data plane
  control plane
What’s inside a router
  input ports, switching, output ports
  buffer management, scheduling
IP: the Internet Protocol
  datagram format
  addressing
  network address translation
  IPv6
Generalized Forwarding, SDN
  Match+action
  OpenFlow: match+action in action
Middleboxes
Notes: SDN: software defined network
What Is OpenFlow: Key Takeaways
OpenFlow is one of the first software-defined networking (SDN) standards and defined the communication protocol between SDN controllers and the forwarding plane of networking devices.
Benefits include its programmability, centralized intelligence, and how it abstracts network architecture.
The original concept began at Stanford University in 2008 but has since been managed by the Open Networking Foundation.

## Slide 4
4.1 Overview of Network layer
4.2 What's inside a router
4.3 IP: Internet Protocol
4.4 Generalized Forward
4.5 Middleboxes
Chapter 4 Network Layer
- The Data Plane
Network Layer - the data plane
Notes: SDN: software defined network

## Slide 5
4.1 Overview of Network layer
  data plane
  control plane
4.2 What's inside a router
4.3 IP: Internet Protocol
4.4 Generalized Forward
4.5 Middleboxes
Chapter 4 Network Layer
- The Data Plane
Network Layer - the data plane

## Slide 6: Network layer
packet in network layer
transport segment from sending to receiving host
  on sending side encapsulates segments into datagrams
  on receiving side, delivers segments to transport layer
network layer protocols in every Internet device:
  host, router
routers:
  examine header fields in all IP datagrams passing through it
  move datagrams from input ports to output ports to transfer datagrams along end-end path
application
transport
network
data link
physical
application
transport
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
4.1 Overview
Notes: Strictly speaking, ethernet switches are networking devices, not Internet devices.

## Slide 7: Two key network-layer functions
network-layer functions:
forwarding: move packets from router's input to appropriate router output
routing: determine route taken by packets from source to destination
  routing algorithms
analogy: taking a trip
forwarding: process of getting through single interchange
routing: process of planning trip from source to destination
4.1 Overview

## Slide 8: Network layer: data plane, control plane
Data plane
local, per-router function
determines how datagram arriving on router input port is forwarded to router output port
forwarding function
Control plane
global(network-wide) logic
determines how datagram is routed among routers along end-end path from source host to destination host
two control-plane approaches:
  traditional routing algorithms: implemented in routers
  software-defined networking (SDN): implemented in (remote) servers
1
2
3
0111
values in arriving
packet header
4.1 Overview

## Slide 9: Per-router control plane
Routing
Algorithm
Individual routing algorithm components in each and every router interact in the control plane
data
plane
control
plane
1
2
0111
values in arriving
packet header
3
4.1 Overview
determine end-to-end route
determine how to forward per-router

## Slide 10: Logically centralized control plane
data
plane
control
plane
A distinct (typically remote) controller interacts with local control agents (CAs)
Remote Controller
CA
CA
CA
CA
CA
1
2
0111
3
values in arriving
packet header
4.1 Overview

## Slide 11: Network service model
Q: What service model for "channel" transporting datagrams from sender to receiver?
example services for individual datagrams:
guaranteed delivery
guaranteed delivery with less than 40 msec delay
example services for a flow of datagrams:
in-order datagram delivery
guaranteed minimum bandwidth to flow
restrictions on changes in inter-packet spacing
4.1 Overview
4.1.2 Network service model
network characteristics defined by end-2-end packet transfer
small jitter

## Slide 12: Network layer service models:
Congestion
feedback
no (inferred via loss)
no congestion
no congestion
yes
no
Network
Architecture
Internet
ATM
ATM
ATM
ATM
Internet
Internet
Service
Model
best effort
CBR
VBR
ABR
UBR
Intserv
Guaranteed
(RFC 1633)
Diffserv
(RFC 2475)
Bandwidth
none
constant
rate
guaranteed
rate
guaranteed
minimum
none
yes
possible
Loss
no
yes
yes
no
no
yes
possibly
Order
no
yes
yes
yes
yes
yes
possibly
Timing
no
yes
yes
no
no
yes
no
Guarantees ?
4.1 Overview
4.1.2 Network service model
Asynchronous
Transfer Mode
No guarantees on:
  successful datagram delivery to destination
  timing or order of delivery
  bandwidth available to end-end flow
Internet “best effort” service model
Notes: ATM (Asynchronous Transfer Mode) : 异步传输模式，信元(cell)交换
未定比特速率（UBR：Unspecified Bit Rate）：对传输速率没有指定，但可靠性要求很高，即所谓"尽力传输"（Best Effort），用于局域网仿真（LAN Emulation）。
不变比特速率（CBR：Constant Bit Rate）：有固定的带宽（速率）要求，适用实时的话音和视频信号传输。
可用比特速率（ABR：Available Bit Rate）：只需指定峰值（Peak）和谷值（Minimum）信元速率，应用不多。
可变比特速率（VBR：Variable Bit Rate）：允许随时可变的带宽，但必须指定峰值带宽、最大突发数据长度和必须维持的最低速率。
Integrated services or IntServ is an architecture that specifies the elements to guarantee quality of service (QoS) on networks. IntServ can for example be used to allow video and sound to reach the receiver without interruption.
Differentiated services or DiffServ is a computer networking architecture that specifies a simple and scalable mechanism for classifying and managing network traffic and providing quality of service (QoS) on modern IP networks. DiffServ can, for example, be used to provide low-latency to critical network traffic such as voice or streaming media while providing simple best-effort service to non-critical services such as web traffic or file transfers.

## Slide 13: Reflections on best-effort service
simplicity of mechanism has allowed Internet to be widely deployed adopted
sufficient provisioning of bandwidth allows performance of real-time applications (e.g., interactive voice, video) to be “good enough” for “most of the time”
replicated, application-layer distributed services (datacenters, content distribution networks) connecting close to clients’ networks, allow services to be provided from multiple locations
congestion control of “elastic” services helps
It’s hard to argue with success of best-effort service model
4.1 Overview

## Slide 14
4.1 Overview of Network layer
4.2 What's inside a router
4.3 IP: Internet Protocol
4.4 Generalized Forward
4.5 Middleboxes
Chapter 4 Network Layer
- The Data Plane
Network Layer - the data plane
Notes: SDN: software defined network

## Slide 15
4.1 Overview of Network layer
4.2 What's inside a router
4.3 IP: Internet Protocol
4.4 Generalized Forward
4.5 Middleboxes
Chapter 4 Network Layer
- The Data Plane
Network Layer - the data plane
Notes: SDN: software defined network

## Slide 16: Router architecture overview
high-speed
switching
fabric
routing
processor
router input ports
router output ports
forwarding data plane (hardware) operates in nanosecond timeframe
routing, management control plane (software)
operates in millisecond timeframe
high-level view of generic router architecture:
4.2 What's inside a router
decentralized switching:
forwarding decisions can be made locally, at each input port
forwarding
table
Notes: femtosecond: 飞秒 —— one quadrillionth, or one millionth of one billionth, of a second
picosecond: 皮秒 —— one trillionth, or one millionth of one millionth of a second
nanosecond：纳秒 —— one billionth of a second
microsecond: 微秒 —— one millionth of a second
millisecond: 毫秒 —— one thousandth of a second

## Slide 17: Input port functions
switch
fabric
line
termination
link
layer
protocol
(receive)
lookup,
forwarding
queueing
decentralized switching:
using header field values, lookup output port using forwarding table in input port memory ("match plus action")
goal: complete input port processing at 'line speed'
queuing: if datagrams arrive faster than forwarding rate into switch fabric
physical layer:
bit-level reception
data link layer:
e.g., Ethernet
see chapter 6
4.2 What's inside a router
4.2.1 Input Port Processing and Destination-Based Forwarding
Notes: line termination: 线路端接

## Slide 18: Input port functions
line
termination
link
layer
protocol
(receive)
lookup,
forwarding
queueing
decentralized switching:
using header field values, lookup output port using forwarding table in input port memory ("match plus action")
destination-based forwarding: forward based only on destination IP address (traditional)
generalized forwarding: forward based on any set of header field values
physical layer:
bit-level reception
data link layer:
e.g., Ethernet
see chapter 6
switch
fabric
4.2 What's inside a router
4.2.1 Input Port Processing and Destination-Based Forwarding

## Slide 19: Destination-based forwarding
Destination Address Range
11001000 00010111 00010000 00000000
through
11001000 00010111 00010111 11111111
11001000 00010111 00011000 00000000
through
11001000 00010111 00011000 11111111
11001000 00010111 00011001 00000000
through
11001000 00010111 00011111 11111111
otherwise
Link Interface
0
1
2
3
Q: but what happens if ranges don't divide up so nicely?
forwarding table
4.2 What's inside a router
4.2.1 Input Port Processing and Destination-Based Forwarding

## Slide 20: Longest prefix matching
Destination Address Range
11001000 00010111 00010*** *********
11001000 00010111 00011000 *********
11001000 00010111 00011*** *********
otherwise
DA: 11001000 00010111 00011000 10101010
examples:
DA: 11001000 00010111 00010110 10100001
which interface?
which interface?
longest prefix matching
Link interface
0
1
2
3
4.2 What's inside a router
when looking for forwarding table entry for given destination address, use longest address prefix that matches destination address.
4.2.1 Input Port Processing and Destination-Based Forwarding
wildcard

## Slide 21: Longest prefix matching
we'll see why longest prefix matching is used shortly, when we study addressing
longest prefix matching: often performed using ternary content addressable memories (TCAMs)
  content addressable: present address to TCAM: retrieve address in one clock cycle, regardless of table size
  Cisco Catalyst: can up ~1M routing table entries in TCAM
4.2 What's inside a router
4.2.1 Input Port Processing and Destination-Based Forwarding
Notes: 三态内容可寻址存储器(Ternary Content Address Memory)

## Slide 22: Switching fabrics
transfer packet from input buffer to appropriate output buffer
switching rate: rate at which packets can be transfer from inputs to outputs
  often measured as multiple of input/output line rate
  N inputs: switching rate N times line rate desirable
three types of switching fabrics
memory
memory
bus
crossbar
4.2 What's inside a router
4.2.2 Switching

## Slide 23: Switching via memory
first generation routers:
traditional computers with switching under direct control of CPU
packet copied to system's memory
speed limited by memory bandwidth (2 bus crossings per datagram)
input
port
(e.g.,
Ethernet)
memory
output
port
(e.g.,
Ethernet)
system bus
4.2 What's inside a router
4.2.2 Switching

## Slide 24: Switching via a bus
datagram from input port memory to output port memory via a shared bus
bus contention: switching speed limited by bus bandwidth
32 Gbps bus, Cisco 5600: sufficient speed for access and enterprise routers
bus
4.2 What's inside a router
4.2.2 Switching
Notes: bus contention (总线竞争)

## Slide 25: Switching via interconnection network
overcome bus bandwidth limitations
banyan networks, crossbar, other interconnection nets initially developed to connect processors in multiprocessor
advanced design: fragmenting datagram into fixed length cells, switch cells through the fabric.
Cisco 12000: switches 60 Gbps through the interconnection network
Huawei 8000 series: 400G – 4Tbps
crossbar
4.2 What's inside a router
4.2.2 Switching
interconnection net
8x8 multistage switch
built from smaller-sized switches
Notes: banyan network 榕树网

## Slide 26: Switching via interconnection network
scaling, using multiple switching “planes” in parallel:
  speedup, scaleup via parallelism
fabric plane 0
. . .
. . .
fabric plane 1
. . .
. . .
fabric plane 2
. . .
. . .
fabric plane 3
. . .
. . .
fabric plane 4
. . .
. . .
fabric plane 5
. . .
. . .
fabric plane 6
. . .
. . .
fabric plane 7
. . .
. . .
Cisco CRS router:
  basic unit: 8 switching planes
  each plane: 3-stage interconnection network
  up to 100’s Tbps switching capacity
4.2 What's inside a router
Notes: multi-stage interconnection: 多级互连

## Slide 27: Input port queuing
If switch fabric slower than input ports combined queueing may occur at input queues
  queueing delay and loss due to input buffer overflow!
Head-of-the-Line (HOL) blocking: queued datagram at front of queue prevents others in queue from moving forward
output port contention:
only one red datagram can be transferred. lower red packet is blocked
switch
fabric
one packet time later: green packet experiences HOL blocking
switch
fabric
4.2 What's inside a router
4.2.4 Where Does Queuing Occur?

## Slide 28: Output ports
buffering required when datagrams arrive from fabric faster than the transmission rate
  Drop policy: which datagrams to drop if no free buffers?
scheduling discipline chooses among queued datagrams for transmission
line
termination
link
layer
protocol
(send)
switch
fabric
datagram
buffer
queueing
This slide in HUGELY important!
Datagram (packets) can be lost due to congestion, lack of buffers
Priority scheduling – who gets best performance, network neutrality
4.2 What's inside a router
4.2.4 Where Does Queuing Occur?

## Slide 29: Output port queueing
buffering when arrival rate via switch exceeds output line speed
queueing (delay) and loss due to output port buffer overflow!
at t, packets more
from input to output
one packet time later
switch
fabric
switch
fabric
4.2 What's inside a router
4.2.4 Where Does Queuing Occur?

## Slide 30: How much buffering?
RFC 3439 rule of thumb: average buffering equal to "typical" RTT (say 250 msec) times link capacity C
  e.g., C = 10 Gpbs link: 2.5 Gbit buffer
recent recommendation: with N flows, buffering equal to
4.2 What's inside a router
4.2.4 Where Does Queuing Occur?
but too much buffering can increase delays (particularly in home routers)
  long RTTs: poor performance for realtime apps, sluggish TCP response
  recall delay-based congestion control: “keep bottleneck link just full enough (busy) but no fuller”

## Slide 31: Buffer Management
buffer management:
drop: which packet to add, drop when buffers are full
  tail drop: drop arriving packet
  priority: drop/remove on priority basis
line
termination
link
layer
protocol
(send)
switch
fabric
datagram
buffer
queueing
scheduling
marking: which packets to mark to signal congestion (ECN, RED)
R
queue
(waiting area)
packet
arrivals
packet
departures
link
(server)
Abstraction: queue
R
4.2 What's inside a router

## Slide 32: Packet Scheduling: FCFS
packet scheduling: deciding which packet to send next on link
  first come, first served
  priority
  round robin
  weighted fair queueing
FCFS: packets transmitted in order of arrival to output port
also known as: First-in-first-out (FIFO)
real world examples?
queue
(waiting area)
packet
arrivals
packet
departures
link
(server)
Abstraction: queue
R
4.2 What's inside a router

## Slide 33: Scheduling mechanisms
scheduling: choose next packet to send on link
FIFO (first in first out) scheduling: send in order of arrival to queue
  real-world example?
  discard policy: if packet arrives to full queue: who to discard?
    tail drop: drop arriving packet
    priority: drop/remove on priority basis
    random: drop/remove randomly
queue
(waiting area)
packet
arrivals
packet
departures
link
(server)
4.2 What's inside a router
4.2.5 Packet Scheduling

## Slide 34: Scheduling policies: priority
priority scheduling:
arriving traffic classified, queued by class
  any header fields can be used for classification
high priority queue
(waiting area)
low priority queue
(waiting area)
arrivals
classify
departures
link
(server)
1
3
2
4
5
5
5
2
2
1
1
3
3
4
4
arrivals
departures
packet in service
4.2 What's inside a router
4.2.5 Packet Scheduling
send packet from highest priority queue that has buffered packets
  FCFS within priority class

## Slide 35: Scheduling policies: round robin
Round Robin (RR) scheduling:
arriving traffic classified, queued by class
  any header fields can be used for classification
4.2 What's inside a router
4.2.5 Packet Scheduling
classify
arrivals
departures
link
R
server cyclically, repeatedly scans class queues, sending one complete packet from each class (if available) in turn

## Slide 36: Scheduling policies: weighted fair queueing
Weighted Fair Queuing (WFQ):
generalized Round Robin
each class gets weighted amount of service in each cycle
minimum bandwidth guarantee (per-traffic-class)
4.2 What's inside a router
4.2.5 Packet Scheduling
classify
arrivals
departures
link
Notes: 加权公平队列

## Slide 37: Homework this week
Problems of Chapter 4:
P1
P4
P6
P9
Network Layer - the data plane

## Slide 38
4.1 Overview of Network layer
4.2 What's inside a router
4.3 IP: Internet Protocol
4.4 Generalized Forward
4.5 Middleboxes
Chapter 4 Network Layer
- The Data Plane
Network Layer - the data plane
Notes: SDN: software defined network

## Slide 39
4.1 Overview of Network layer
4.2 What's inside a router
4.3 IP: Internet Protocol
  datagram format
  fragmentation
  IPv4 addressing
  network address translation
  IPv6
4.4 Generalized Forward
4.5 Middleboxes
Chapter 4 Network Layer
- The Data Plane
Network Layer - the data plane
Notes: SDN: software defined network

## Slide 40
4.1 Overview of Network layer
4.2 What's inside a router
4.3 IP: Internet Protocol
  datagram format
  fragmentation
  IPv4 addressing
  network address translation
  IPv6
4.4 Generalized Forward
4.5 Middleboxes
Chapter 4 Network Layer
- The Data Plane
Network Layer - the data plane
Notes: SDN: software defined network

## Slide 41
TELNET
HTTP
FTP
SMTP
DNS
RIP
SNMP
DHCP
TCP
UDP
IP
ICMP
OSPF
ARP
RARP
application layer
transport
layer
network
layer
The Internet Hourglass
link
layer
ethernet
802.11
SONET
ATM
4.3 IP: Internet Protocol

## Slide 42: The Internet network layer
forwarding
table
host, router network layer functions:
routing protocols
path selection
RIP, OSPF, BGP
IP protocol
addressing conventions
datagram format
packet handling conventions
ICMP protocol
error reporting
router "signaling"
transport layer: TCP, UDP
link layer
physical layer
network
layer
4.3 IP: Internet Protocol
3 major protocols
in network layer

## Slide 43: IPv4 datagram format
Maximum length: 64K bytes
Typically: 1500 bytes or less
ver
length
32 bits
data
(variable length,
typically a TCP
or UDP segment)
16-bit identifier
header
checksum
time to
live
32 bit source IP address
type of
service
flgs
fragment
offset
upper
layer
32 bit destination IP address
options (if any)
head.
len
IP protocol version
number
header length
(bytes)
upper layer protocol
to deliver payload to
total datagram
length (bytes)
for
fragmentation/
reassembly
max number
remaining hops
(decremented at
each router)
e.g. timestamp,
record route
taken, specify
list of routers
to visit.
how much overhead?
20 bytes of TCP
20 bytes of IP
= 40 bytes + app layer overhead
4.3 IP: Internet Protocol
4.3.1 IPv4 Datagram Format
measured in units of eight-byte blocks
"type" of data
diffserv (0:5)
ECN (6:7)

## Slide 44: IP fragmentation, reassembly
network links have MTU (max.transfer size) - largest possible link-level frame
  different link types, different MTUs
large IP datagram divided ("fragmented") within net
  one datagram becomes several datagrams
  "reassembled" only at final destination
  IP header bits used to identify, order related fragments
fragmentation:
in: one large datagram
out: 3 smaller datagrams
reassembly
…
…
4.3 IP: Internet Protocol
4.3.2 IPv4 Datagram Fragmentation
ethernet
MTU = 1500

## Slide 45: IP fragmentation, reassembly
ID
=x
offset
=0
fragflag
=0
length
=4000
ID
=x
offset
=0
fragflag
=1
length
=1500
ID
=x
offset
=185
fragflag
=1
length
=1500
ID
=x
offset
=370
fragflag
=0
length
=1040
one large datagram becomes
several smaller datagrams
example:
4000 byte datagram
MTU = 1500 bytes
1480 bytes in data field
offset = 1480/8
4.3 IP: Internet Protocol
4.3.2 IPv4 Datagram Fragmentation
measured in units of eight-byte blocks
 | length(byte) | Data length(byte) | FF | offset
ori. datagram | 4000 | 3980 | 0 | 0
segment 1 | 1500 | 1480 | 1 | 0
segment 2 | 1500 | 1480 | 1 | 185
segment 3 | 1040 | 1020 | 0 | 370

## Slide 46
4.1 Overview of Network layer
4.2 What's inside a router
4.3 IP: Internet Protocol
  datagram format
  fragmentation
  IPv4 addressing
  network address translation
  IPv6
4.4 Generalized Forward
4.5 Middleboxes
Chapter 4 Network Layer
- The Data Plane
Network Layer - the data plane
Notes: SDN: software defined network

## Slide 47
4.1 Overview of Network layer
4.2 What's inside a router
4.3 IP: Internet Protocol
  datagram format
  fragmentation
  IPv4 addressing
  network address translation
  IPv6
4.4 Generalized Forward
4.5 Middleboxes
Chapter 4 Network Layer
- The Data Plane
Network Layer - the data plane
Notes: SDN: software defined network

## Slide 48: IPv4 addressing: introduction
IP address: 32-bit identifier for host or router interface
interface: connection between host/router and physical link
  router typically has multiple interfaces
  host typically has one or two interfaces (e.g., wired Ethernet, wireless 802.11)
IP addresses associated with each interface
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.1 = 11011111 00000001 00000001 00000001
223
1
1
1
4.3 IP: Internet Protocol
4.3.3 IPv4 Addressing
dotted-decimal notation
binary notation
subnet
subnet
subnet

## Slide 49: IPv4 addressing: introduction
Q: how are interfaces actually connected?
A: we'll learn about that in chapter 6, 7.
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
A: wired Ethernet interfaces connected by Ethernet switches
A: wireless WiFi interfaces connected by WiFi base station
For now: don't need to worry about how one interface is connected to another (with no intervening router)
4.3 IP: Internet Protocol
4.3.3 IPv4 Addressing

## Slide 50: Subnets
what's a subnet ?
  device interfaces with same subnet part of IP address
  can physically reach each other without intervening router
IP address:
  subnet part: common high order bits
  host part: remaining low order bits
network consisting of 3 subnets
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.9
223.1.3.2
223.1.3.1
subnet
223.1.1.2
223.1.3.27
223.1.2.2
223.1.2.1
4.3 IP: Internet Protocol
4.3.3 IPv4 Addressing
switch
AP

## Slide 51: Subnets
recipe for defining subnets
to determine the subnets
  detach each interface from its host or router
  creating islands of isolated networks
each isolated network is called a subnet
subnet mask: /24
(high order 24 bits define subnet)
223.1.1.0/24
223.1.2.0/24
223.1.3.0/24
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.9
223.1.3.2
223.1.3.1
subnet
223.1.1.2
223.1.3.27
223.1.2.2
223.1.2.1
4.3 IP: Internet Protocol
4.3.3 IPv4 Addressing

## Slide 52: Subnets
How many?
Which ones?
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.2
223.1.2.1
223.1.2.6
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.2
223.1.7.0
223.1.7.1
223.1.8.0
223.1.8.1
223.1.9.1
223.1.9.2
4.3 IP: Internet Protocol
4.3.3 IPv4 Addressing

## Slide 53: IPv4 addressing: CIDR
CIDR: Classless InterDomain Routing
  subnet portion of address of arbitrary length
  address format: a.b.c.d/x, where x is # bits in subnet portion of address
11001000 00010111 00010000 00000000
subnet
part
host
part
200.23.16.0/23
4.3 IP: Internet Protocol
4.3.3 IPv4 Addressing
prefix
dotted-decimal form
Notes: 无类别域间路由 CIDR (pronounced like “cider” [ˈsaɪdrɚ])

## Slide 54: IP addresses: how to get one?
Q: How does a host get IP address?
hard-coded by system admin in a config file
  Windows: control-panel->network->configuration->tcp/ip->properties
  UNIX: /etc/rc.config
DHCP: Dynamic Host Configuration Protocol: dynamically get address from a DHCP server
  "plug-and-play"
4.3 IP: Internet Protocol
4.3.3 IPv4 Addressing
That’s actually two questions:
Q: How does a host get IP address within its network (host part of address)?
Q: How does a network get IP address for itself (network part of address)?

## Slide 55: DHCP: Dynamic Host Configuration Protocol
goal: host dynamically obtains IP address from network server when it "joins" a network
  can renew its lease on address in use
  allows reuse of addresses (only hold address while connected/"on")
  support for mobile users who join/leave network
DHCP overview:
  host broadcasts "DHCP discover" msg [optional]
  DHCP server responds with "DHCP offer" msg [optional]
  host requests IP address: "DHCP request" msg
  DHCP server sends address: "DHCP ack" msg
4.3 IP: Internet Protocol
4.3.3 IPv4 Addressing
Server: UDP Port 67
Client: UDP Port 68

## Slide 56: DHCP client-server scenario
223.1.1.0/24
223.1.2.0/24
223.1.3.0/24
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.9
223.1.3.2
223.1.3.1
223.1.1.2
223.1.2.2
223.1.2.1
DHCP server
223.1.2.5
4.3 IP: Internet Protocol
4.3.3 IPv4 Addressing
arriving DHCP client needs
address in this network
Typically, DHCP server will be co-located in router, serving all subnets to which router is attached
223.1.3.27

## Slide 57: DHCP client-server scenario
DHCP server: 223.1.2.5
arriving
client
DHCP discover
src : 0.0.0.0, 68
dest.: 255.255.255.255,67
yiaddr: 0.0.0.0
transaction ID: 654
DHCP offer
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 654
lifetime: 3600 secs
DHCP request
src: 0.0.0.0, 68
dest:: 255.255.255.255, 67
yiaddrr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs
DHCP ACK
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs
Broadcast: is there a DHCP server out there?
Broadcast: I'm a DHCP server! Here's an IP address you can use
Broadcast: OK. I'll take that IP address!
Broadcast: OK. You've got that IP address!
4.3 IP: Internet Protocol
4.3.3 IPv4 Addressing
The two steps above can be skipped “if a client remembers and wishes to reuse a previously allocated network address” [RFC 2131]

## Slide 58: DHCP: more than IP addresses
DHCP can return more than just allocated IP address on subnet:
  address of first-hop router for client
  name and IP address of DNS sever
  network mask (indicating network versus host portion of address)
4.3 IP: Internet Protocol
4.3.3 IPv4 Addressing

## Slide 59: DHCP: example
connecting laptop needs its IP address, addr of first-hop router, addr of DNS server: use DHCP
router with DHCP
server built into
router
DHCP request encapsulated in UDP, encapsulated in IP, encapsulated in 802.1 Ethernet
Ethernet frame broadcast (dest: FFFFFFFFFFFF) on LAN, received at router running DHCP server
Ethernet demuxed to IP demuxed, UDP demuxed to DHCP
168.1.1.1
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
4.3 IP: Internet Protocol
4.3.3 IPv4 Addressing

## Slide 60: DHCP: example
DHCP server formulates DHCP ACK containing client's IP address, IP address of first-hop router for client, name & IP address of DNS server
encapsulated DHCP server reply forwarded to client, demuxing up to DHCP at client
router with DHCP
server built into
router
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
client now knows its IP address, name and IP address of DNS server, IP address of its first-hop router
4.3 IP: Internet Protocol
4.3.3 IPv4 Addressing

## Slide 61: DHCP: Wireshark output (home LAN)
Message type: Boot Reply (2)
Hardware type: Ethernet
Hardware address length: 6
Hops: 0
Transaction ID: 0x6b3a11b7
Seconds elapsed: 0
Bootp flags: 0x0000 (Unicast)
Client IP address: 192.168.1.101 (192.168.1.101)
Your (client) IP address: 0.0.0.0 (0.0.0.0)
Next server IP address: 192.168.1.1 (192.168.1.1)
Relay agent IP address: 0.0.0.0 (0.0.0.0)
Client MAC address: Wistron_23:68:8a (00:16:d3:23:68:8a)
Server host name not given
Boot file name not given
Magic cookie: (OK)
Option: (t=53,l=1) DHCP Message Type = DHCP ACK
Option: (t=54,l=4) Server Identifier = 192.168.1.1
Option: (t=1,l=4) Subnet Mask = 255.255.255.0
Option: (t=3,l=4) Router = 192.168.1.1
Option: (6) Domain Name Server
Length: 12; Value: 445747E2445749F244574092;
IP Address: 68.87.71.226;
IP Address: 68.87.73.242;
IP Address: 68.87.64.146
Option: (t=15,l=20) Domain Name = "hsd1.ma.comcast.net."
reply
Message type: Boot Request (1)
Hardware type: Ethernet
Hardware address length: 6
Hops: 0
Transaction ID: 0x6b3a11b7
Seconds elapsed: 0
Bootp flags: 0x0000 (Unicast)
Client IP address: 0.0.0.0 (0.0.0.0)
Your (client) IP address: 0.0.0.0 (0.0.0.0)
Next server IP address: 0.0.0.0 (0.0.0.0)
Relay agent IP address: 0.0.0.0 (0.0.0.0)
Client MAC address: Wistron_23:68:8a (00:16:d3:23:68:8a)
Server host name not given
Boot file name not given
Magic cookie: (OK)
Option: (t=53,l=1) DHCP Message Type = DHCP Request
Option: (61) Client identifier
Length: 7; Value: 010016D323688A;
Hardware type: Ethernet
Client MAC address: Wistron_23:68:8a (00:16:d3:23:68:8a)
Option: (t=50,l=4) Requested IP Address = 192.168.1.101
Option: (t=12,l=5) Host Name = "nomad"
Option: (55) Parameter Request List
Length: 11; Value: 010F03062C2E2F1F21F92B
1 = Subnet Mask; 15 = Domain Name
3 = Router; 6 = Domain Name Server
44 = NetBIOS over TCP/IP Name Server
……
request
4.3 IP: Internet Protocol
4.3.3 IPv4 Addressing

## Slide 62: IP addresses: how to get one?
Q: how does network get subnet part of IP addr?
A: gets allocated portion of its provider ISP's address space
ISP's block 11001000 00010111 00010000 00000000 200.23.16.0/20
4.3 IP: Internet Protocol
4.3.3 IPv4 Addressing
Internet Corporation for Assigned Names and Numbers (ICANN)
ISP can then allocate out its address space in 8 blocks:
Organization 0 11001000 00010111 00010000 00000000 200.23.16.0/23
Organization 1 11001000 00010111 00010010 00000000 200.23.18.0/23
Organization 2 11001000 00010111 00010100 00000000 200.23.20.0/23
... ….. …. ….
Organization 7 11001000 00010111 00011110 00000000 200.23.30.0/23

## Slide 63: Hierarchical addressing: route aggregation
"Send me anything
with addresses
beginning
200.23.16.0/20"
200.23.16.0/23
200.23.18.0/23
200.23.30.0/23
Fly-By-Night-ISP
Organization 0
Organization 7
Internet
Organization 1
ISPs-R-Us
"Send me anything
with addresses
beginning
199.31.0.0/16"
200.23.20.0/23
Organization 2
.
.
.
.
.
.
hierarchical addressing allows efficient advertisement of routing
information:
4.3 IP: Internet Protocol
4.3.3 IPv4 Addressing
Notes: 路由聚合
路由摘要（route summarization）
Fly by night: 不可信

## Slide 64: Hierarchical addressing: more specific routes
Organization 1 moves from Fly-By-Night-ISP to ISPs-R-Us
ISPs-R-Us now advertises a more specific route to Organization 1
"Send me anything
with addresses
beginning
200.23.16.0/20"
200.23.16.0/23
200.23.30.0/23
Fly-By-Night-ISP
Organization 0
Organization 7
Internet
200.23.20.0/23
Organization 2
.
.
.
.
.
.
4.3 IP: Internet Protocol
4.3.3 IPv4 Addressing
longest prefix matching
enabling route aggregation
of organization 1
200.23.18.0/23
Organization 1
200.23.18.0/23
Organization 1
“or 200.23.18.0/23”
ISPs-R-Us
"Send me anything
with addresses
beginning 199.31.0.0/16”

## Slide 65: IP addressing: last words...
Q: how does an ISP get block of addresses?
A: ICANN: Internet Corporation for Assigned
Names and Numbers http://www.icann.org/
    allocates IP addresses, through 5 regional internet registries (RIRS)
      RIRS may then allocate to local registries
    manages DNS root zone, including delegation of individual TLD (.com, .edu , …) management
    assigns domain names, resolves disputes
4.3 IP: Internet Protocol
4.3.3 IPv4 Addressing
https://aso.icann.org/advisory-council/regional-internet-registries-rirs/
Q: are there enough 32-bit IP addresses?
    ICANN allocated last chunk of IPv4 addresses to RIRS in 2011
    NAT (next) helps IPv4 address space exhaustion
    IPv6 has 128-bit address space
"Who the hell knew how much address space we needed?" Vint Cerf (reflecting on decision to make IPv4 address 32 bits long)

## Slide 66
4.1 Overview of Network layer
4.2 What's inside a router
4.3 IP: Internet Protocol
  datagram format
  fragmentation
  IPv4 addressing
  network address translation
  IPv6
4.4 Generalized Forward
4.5 Middleboxes
Chapter 4 Network Layer
- The Data Plane
Network Layer - the data plane
Notes: SDN: software defined network

## Slide 67
4.1 Overview of Network layer
4.2 What's inside a router
4.3 IP: Internet Protocol
  datagram format
  fragmentation
  IPv4 addressing
  network address translation
  IPv6
4.4 Generalized Forward
4.5 Middleboxes
Chapter 4 Network Layer
- The Data Plane
Network Layer - the data plane
Notes: SDN: software defined network

## Slide 68: NAT: network address translation
10.0.0.1
10.0.0.2
10.0.0.3
10.0.0.4
local network
(e.g., home network)
10.0.0/24
138.76.29.7
rest of
Internet
datagrams with source or
destination in this network
have 10.0.0/24 address for
source, destination (as usual)
all datagrams leaving local
network have same single source NAT IP address: 138.76.29.7, but different source port numbers
4.3 IP: Internet Protocol
4.3.4 Network Address Translation (NAT)
NAT: all devices in local network share just one IPv4 address as far as outside world is concerned
Notes: 网络地址转换

## Slide 69: NAT: network address translation
motivation: local network uses just one IP address as far as outside world is concerned:
    range of addresses not needed from ISP: just one IP address for all devices
    can change addresses of devices in local network without notifying outside world
    can change ISP without changing addresses of devices in local network
    devices inside local net not explicitly addressable, visible by outside world (a security plus)
4.3 IP: Internet Protocol
4.3.4 Network Address Translation (NAT)

## Slide 70: NAT: network address translation
implementation: NAT router must (transparently):
    outgoing datagrams: replace (source IP address, port #) of every outgoing datagram to (NAT IP address, new port #)
    remote clients/servers will respond using (NAT IP address, new port #) as destination addr
    remember (in NAT translation table) every (source IP address, port #) to (NAT IP address, new port #) translation pair
    incoming datagrams: replace (NAT IP address, new port #) in dest fields of every incoming datagram with corresponding (source IP address, port #) stored in NAT table
4.3 IP: Internet Protocol
4.3.4 Network Address Translation (NAT)

## Slide 71: NAT: network address translation
10.0.0.1
10.0.0.2
10.0.0.3
S: 10.0.0.1, 3345
D: 128.119.40.186, 80
1
10.0.0.4
138.76.29.7
1: host 10.0.0.1
sends datagram to
128.119.40.186, 80
NAT translation table
WAN side addr LAN side addr
138.76.29.7, 5001 10.0.0.1, 3345
…… ……
S: 128.119.40.186, 80
D: 10.0.0.1, 3345
4
S: 138.76.29.7, 5001
D: 128.119.40.186, 80
2
2: NAT router
changes datagram
source addr from
10.0.0.1, 3345 to
138.76.29.7, 5001,
updates table
S: 128.119.40.186, 80
D: 138.76.29.7, 5001
3
3: reply arrives
dest. address:
138.76.29.7, 5001
4: NAT router
changes datagram
dest addr from
138.76.29.7, 5001 to 10.0.0.1, 3345
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/
4.3 IP: Internet Protocol
4.3.4 Network Address Translation (NAT)
private IP
public IP

## Slide 72: NAT: network address translation
16-bit port-number field:
  60,000 simultaneous connections with a single LAN-side address!
NAT has been controversial:
  routers should only process up to layer 3
  address shortage should be solved by IPv6
  violates end-to-end argument
    port # manipulation by network-layer device
    NAT possibility must be taken into account by app designers, e.g., P2P applications
  NAT traversal: what if client wants to connect to server behind NAT?
  But NAT is here to stay:
  extensively used in home and institutional nets, 4G/5G mobile networks
4.3 IP: Internet Protocol
4.3.4 Network Address Translation (NAT)
RFC 5389
Notes: NAT traversal [trəˈvərs(ə)l] 穿透

## Slide 73
4.1 Overview of Network layer
4.2 What's inside a router
4.3 IP: Internet Protocol
  datagram format
  fragmentation
  IPv4 addressing
  network address translation
  IPv6
4.4 Generalized Forward
4.5 Middleboxes
Chapter 4 Network Layer
- The Data Plane
Network Layer - the data plane
Notes: SDN: software defined network

## Slide 74
4.1 Overview of Network layer
4.2 What's inside a router
4.3 IP: Internet Protocol
  datagram format
  fragmentation
  IPv4 addressing
  network address translation
  IPv6
4.4 Generalized Forward
4.5 Middleboxes
Chapter 4 Network Layer
- The Data Plane
Network Layer - the data plane
Notes: SDN: software defined network

## Slide 75: IPv6: motivation
initial motivation: 32-bit IPv4 address space would be completely allocated.
additional motivation:
  header format helps speed processing/forwarding: 40-byte fixed length header
  header changes to facilitate QoS (flows)
IPv6 initiated mid-1990’s
  Slow transition: 25 years later: 25% Google clients, use IPv6, 1/3 US government domains IPv6-enabled
IPv6 datagram format:
  fixed-length 40 byte header
  no fragmentation allowed
4.3 IP: Internet Protocol
ver
length
32 bits
data
(variable length,
typically a TCP
or UDP segment)
16-bit identifier
header
checksum
time to
live
32 bit source IP address
head.
len
type of
service
flgs
fragment
offset
upper
layer
32 bit destination IP address
options (if any)

## Slide 76: IPv6 datagram format
data
payload len
next hdr
hop limit
flow label
pri
ver
32 bits
4.3 IP: Internet Protocol
traffic class
priority: identify priority
among datagrams in flow
128 bit
IPv6 addresses
flow label: identify datagrams in same "flow." (concept of "flow" not well defined).
next header: identify upper layer protocol for data
Notes:
Payload length, hop limit as in IPv4 (TTL)
no checksum (to speed processing at routers, must recalculate at each hop due to change of TTL)
no options (available as upper layer, next-header protocol)
source address
(128 bits)
destination address
(128 bits)

## Slide 77: Other changes from IPv4
checksum: removed entirely to reduce processing time at each hop
options: allowed, but outside of header, indicated by "Next Header" field
ICMPv6: new version of ICMP
  additional message types, e.g. "Packet Too Big"
  multicast group management functions
4.3 IP: Internet Protocol

## Slide 78: Transition from IPv4 to IPv6
not all routers can be upgraded simultaneously
  no "flag days"
  how will network operate with mixed IPv4 and IPv6 routers?
tunneling: IPv6 datagram carried as payload in IPv4 datagram among IPv4 routers("packet within a packet")
  tunneling used extensively in other contexts (4G/5G)
IPv4 source, dest addr
IPv4 header fields
IPv4 datagram
IPv6 datagram
IPv4 payload
UDP/TCP payload
IPv6 source dest addr
IPv6 header fields
4.3 IP: Internet Protocol

## Slide 79: Tunneling and encapsulation
4.3 IP: Internet Protocol
Ethernet connecting two IPv6 routers:
Ethernet connects two IPv6 routers
A
B
IPv6
IPv6
E
F
IPv6
IPv6
Link-layer frame
IPv6 datagram
The usual: datagram as payload in link-layer frame
A
B
IPv6
IPv6/v4
E
F
IPv6/v4
IPv6
IPv4 network
IPv4 network connecting two IPv6 routers

## Slide 80: Tunneling and encapsulation
4.3 IP: Internet Protocol
Ethernet connecting two IPv6 routers:
Ethernet connects two IPv6 routers
A
B
IPv6
IPv6
E
F
IPv6
IPv6
IPv4 tunnel connecting two IPv6 routers
IPv4 tunnel
connecting IPv6 routers
A
B
IPv6
E
F
IPv6
Link-layer frame
IPv6 datagram
The usual: datagram as payload in link-layer frame
IPv4 datagram
IPv6 datagram
tunneling: IPv6 datagram as payload in a IPv4 datagram
IPv6/v4
IPv6/v4

## Slide 81: Tunneling
flow: X
src: A
dest: F
data
A-to-B:
IPv6
flow: X
src: A
dest: F
data
src:B
dest: E
B-to-C:
IPv6 inside
IPv4
E-to-F:
IPv6
flow: X
src: A
dest: F
data
D-to-E:
IPv6 inside
IPv4
flow: X
src: A
dest: F
data
src:B
dest: E
physical view:
A
B
IPv6
IPv6/v4
E
IPv6/v4
IPv6
F
C
D
logical view:
IPv4 tunnel
connecting IPv6 routers
E
IPv6/v4
IPv6
F
A
B
IPv6
IPv6/v4
IPv4
IPv4
4.3 IP: Internet Protocol
Note source and destination addresses!

## Slide 82: IPv6: adoption
Google: ~30% of clients access services via IPv6
NIST: 1/3 of all US government domains are IPv6 capable
Long (long!) time for deployment, use
  25 years and counting!
  think of application-level changes in last 25 years: WWW, Facebook, streaming media, telepresence, metaverse, GPT …
  Why?
4.3 IP: Internet Protocol
http://www.gov.cn/zhengce/zhengceku/2020-03/23/content_5494661.htm
http://www.gov.cn/zhengce/2017-11/26/content_5242389.htm
Notes: National Institute of Standards and Technology
https://fedv6-deployment.antd.nist.gov/

## Slide 83
4.1 Overview of Network layer
4.2 What's inside a router
4.3 IP: Internet Protocol
4.4 Generalized Forward
4.5 Middleboxes
Chapter 4 Network Layer
- The Data Plane
Network Layer - the data plane
Notes: SDN: software defined network

## Slide 84
4.1 Overview of Network layer
4.2 What's inside a router
4.3 IP: Internet Protocol
4.4 Generalized Forward
  match
  action
  OpenFlow examples of match-plus-action in action
4.5 Middleboxes
Chapter 4 Network Layer
- The Data Plane
Network Layer - the data plane
https://www.sdnctc.com/
Notes: SDN: software defined network

## Slide 85
Generalized Forwarding and SDN
Review: Each router contains a forwarding table that is computed and distributed by a logically centralized routing controller
4.4 Generalized Forward and SDN
data
plane
control
plane
Remote Controller
CA
CA
CA
CA
CA
1
2
0111
3
values in arriving
packet header
local forwarding table
header counter action
flow
local flow table

## Slide 86
Review and Overview: Forwarding
4.4 Generalized Forward and SDN
1
2
0111
3
values in arriving
packet header
Eeach router contains a forwarding table
forwarding table
  Routing(destination-based forwarding): forwarding by dest. IP address
  Switching: forwarding by local destination MAC address

## Slide 87
Generalized Forwarding: match plus action
4.4 Generalized Forward and SDN
1
2
0111
3
values in arriving
packet header
Eeach router contains a forwarding table (broad term: flow table)
  generalized forwarding: forwarding/(taking action) by flow
    many header fields can determine action (may use any of the info within the packet)
    many action possible: drop/copy/modify/log packet
forwarding table
(broad term: flow table)
  Routing(destination-based forwarding): forwarding by dest. IP address
  Switching: forwarding by local destination MAC address

## Slide 88: Flow table abstraction
flow: defined by header fields(in link-, network-, transport-layer fields)
generalized forwarding: simple packet-handling rules
  Match: pattern values in packet header fields
  Actions: for matched packet: drop, forward, modify, matched packet or send matched packet to controller
  Priority: disambiguate overlapping patterns
  Counters: #bytes and #packets
4.4 Generalized Forward and SDN
Router’s flow table (computed and distributed by controller) define router’s match+action rules
Flow table
match
action
Notes: disambiguate [ˌdɪsæmˈbɪɡjuˌet] vt. 消除…的歧义

## Slide 89: Flow table abstraction
flow: defined by header fields
generalized forwarding: simple packet-handling rules
  Match: pattern values in packet header fields
  Actions: for matched packet: drop, forward, modify, matched packet or send matched packet to controller
  Priority: disambiguate overlapping patterns
  Counters: #bytes and #packets
4.4 Generalized Forward and SDN
Flow table
match
action
1
2
3
4
* : wildcard
src=10.1.2.3, dest=*.*.*.* send to controller
src=1.2.*.*, dest=*.*.*.* drop
src = *.*.*.*, dest=3.4.*.* forward(2)
Notes: disambiguate [ˌdɪsæmˈbɪɡjuˌet] vt. 消除…的歧义

## Slide 90: OpenFlow: Flow Table Entries
4.4 Generalized Forward and SDN
Rule
Action
Stats
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP/UDP
sport
TCP/UDP
dport
Forward packet to port(s)
Encapsulate and forward to controller
Drop packet
Send to normal processing pipeline
Modify Fields
Packet + byte counters
Link layer
Network layer
Transport layer
Ingress
Port
Notes: The ingress port refers to the input port at the packet switch on which a packet is received.
  Ingress Port: Incoming Port, Input Port, Switch Port
  Egress Port: Exiting Port, Output Port
Now I’ll describe the API that tries to meet these goals.
90

## Slide 91
OpenFlow: Examples
Destination-based forwarding:
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Action
*
*
*
*
*
51.6.0.8
*
*
*
port 6
IP datagrams destined to IP address 51.6.0.8 should be forwarded to router output port 6
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Forward
*
*
*
*
*
*
*
*
22
drop
Firewall:
do not forward (block) all datagrams destined to TCP port 22 (ssh port #)
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Forward
*
*
*
*
128.119.1.1
*
*
*
*
drop
do not forward (block) all datagrams sent by host 128.119.1.1
4.4 Generalized Forward and SDN
Notes: Port 22: ssh

## Slide 92
Destination-based layer 2 (switch) forwarding:
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Action
*
*
*
*
*
*
*
*
port 3
OpenFlow: Examples
layer 2 frames with dst MAC address 22:A7:23:11:E1:02 should be forwarded to output port 3
22:A7:23:
11:E1:02
4.4 Generalized Forward and SDN
Source-based layer 2 (switch) forwarding:
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Action
*
*
*
*
*
*
*
*
port 3
layer 2 frames from MAC address 22:A7:23:11:E1:02 should be forwarded to output port 3
22:A7:23:
11:E1:02

## Slide 93: OpenFlow abstraction
Router
  match: longest destination IP prefix
  action: forward out a link
Switch
  match: destination MAC address
  action: forward or flood
Firewall
  match: IP addresses and TCP/UDP port numbers
  action: permit or deny
NAT
  match: IP address and port
  action: rewrite address and port
match+action: abstraction unifies different kinds of devices
4.4 Generalized Forward and SDN
≈ broadcast
Notes: flood: 广播

## Slide 94: OpenFlow example
orchestrated tables can create
network-wide behavior:
datagrams from hosts h5 and h6 should be sent to h3 or h4, via s1 and from there to s2
4.4 Generalized Forward and SDN
Host h1
10.1.0.1
Host h2
10.1.0.2
Host h4
10.2.0.4
Host h3
10.2.0.3
Host h5
10.3.0.5
s1
s2
s3
1
2
3
4
1
2
3
4
1
2
3
4
Host h6
10.3.0.6
controller

## Slide 95: OpenFlow example
IP Src = 10.3.*.*
IP Dst = 10.2.*.*
forward(3)
match
action
ingress port = 2
IP Dst = 10.2.0.3
ingress port = 2
IP Dst = 10.2.0.4
forward(3)
match
action
forward(4)
ingress port = 1
IP Src = 10.3.*.*
IP Dst = 10.2.*.*
forward(4)
match
action
Host h1
10.1.0.1
Host h2
10.1.0.2
Host h4
10.2.0.4
Host h3
10.2.0.3
Host h5
10.3.0.5
s1
s2
s3
1
2
3
4
1
2
3
4
1
2
3
4
Host h6
10.3.0.6
controller
4.4 Generalized Forward and SDN
orchestrated tables can create
network-wide behavior:
datagrams from hosts h5 and h6 should be sent to h3 or h4, via s1 and from there to s2

## Slide 96: Generalized forwarding: summary
“match plus action” abstraction: match bits in arriving packet header(s) in any layers, take action
  matching over many fields (link-, network-, transport-layer)
  local actions: drop, forward, modify, or send matched packet to controller
  “program” network-wide behaviors
simple form of “network programmability”
  programmable, per-packet “processing”
  historical roots: active networking
  today: more generalized programming:
P4 (see p4.org).
4.4 Generalized Forward and SDN
Notes: Programming Protocol-independent Packet Processors (P4) is a domain-specific language for network devices, specifying how data plane devices (switches, NICs, routers, filters, etc.) process packets.

## Slide 97
4.1 Overview of Network layer
4.2 What's inside a router
4.3 IP: Internet Protocol
4.4 Generalized Forward
4.5 Middleboxes
Chapter 4 Network Layer
- The Data Plane
Network Layer - the data plane
4.5 Middleboxes
Notes: SDN: software defined network

## Slide 98: Middleboxes
Enabled by:
programmable local actions: generalized match+action forwarding
software-defined networking: (logically) centralized control, configuration management often in private or public cloud
  network functions virtualization (NFV): boxes with programmable networking, computation, storage
“white box” SDN, NFV hardware: networking, computation, storage
"any intermediary box performing functions apart from normal, standard functions of an IP router on the data path between a source host and destination host"
Middlebox (RFC 3234)
flow monitoring/inspection & control/management
vs
packet switch & forward
4.5 Middleboxes
Notes: Network Functions Virtualization

## Slide 99: Middleboxes everywhere!
enterprise
network
national or global ISP
datacenter
network
NAT: home, cellular, institutional
Firewalls, IDS/IPS: corporate, institutional, service providers, ISPs
Load balancers: corporate, service provider, data center, mobile nets
Caches: service provider, mobile, CDNs
Application-specific: service providers, institutional, CDN
4.5 Middleboxes

## Slide 100: Middleboxes
initially: proprietary (closed) hardware solutions
move towards “whitebox” hardware implementing open API
  move away from proprietary hardware solutions
  programmable local actions via match + action
  move towards innovation/differentiation in software
SDN: (logically) centralized control and configuration management often in private/public cloud
network functions virtualization (NFV): programmable services over white box networking, computation, storage
4.5 Middleboxes

## Slide 101: The IP hourglass
IP
TCP
UDP
HTTP
SMTP
QUIC
DASH
RTP
…
Ethernet
WiFi
Bluetooth
PPP
PDCP
…
copper radio fiber
Internet’s “thin waist”:
one network layer protocol: IP
must be implemented by every (billions) of Internet-connected devices
many protocols in physical, link, transport, and application layers
4.5 Middleboxes

## Slide 102: The IP hourglass, at middle age
IP
TCP
UDP
HTTP
SMTP
QUIC
DASH
RTP
…
Ethernet
WiFi
Bluetooth
PPP
PDCP
…
copper radio fiber
Internet’s middle age “love handles”?
middleboxes, operating inside the network
NAT
NFV
Firewalls
caching
4.5 Middleboxes

## Slide 103: Architectural Principles of the Internet
“Many members of the Internet community would argue that there is no architecture, but only a tradition, which was not written down for the first 25 years (or at least not by the IAB). However, in very general terms, the community believes that
RFC 1958
the goal is connectivity, the tool is the Internet Protocol, and the intelligence is end to end rather than hidden in the network.”
Three cornerstone beliefs:
simple connectivity
IP protocol: that narrow waist
intelligence, complexity at network edge
4.5 Middleboxes

## Slide 104: The end-end argument
some network functionality (e.g., reliable data transfer, congestion) can be implemented in network, or at network edge
end-end implementation of reliable data transfer
application
transport
network
data link
physical
application
transport
network
data link
physical
application
transport
network
data link
physical
application
transport
network
data link
physical
network
link
physical
network
link
physical
network
link
physical
network
link
physical
network
link
physical
network
link
physical
hop-by-hop (in-network) implementation of reliable data transfer
4.5 Middleboxes

## Slide 105: The end-end argument
“The function in question can completely and correctly be implemented only with the knowledge and help of the application standing at the end points of the communication system. Therefore, providing that questioned function as a feature of the communication system itself is not possible. (Sometimes an incomplete version of the function provided by the communication system may be useful as a performance enhancement.)
We call this line of reasoning against low-level function implementation the “end-to-end argument.”
Saltzer, Reed, Clark 1984
some network functionality (e.g., reliable data transfer, congestion) can be implemented in network, or at network edge
4.5 Middleboxes

## Slide 106: Where’s the intelligence?
4.5 Middleboxes
20th century phone net:
intelligence/computing at network switches
Internet (pre-2005)
intelligence, computing at edge
Internet (post-2005)
programmable network devices
intelligence, computing, massive application-level infrastructure at edge
Notes: The 20th century phone network had dumb network endpoints, really by definition. The end points were rotary phones that maybe only your parents and grandparents remember; they weren’t computers. They really were dumb devices, and therefore the phone network had programmable switches that were quite smart. All functionality – well, all of the intelligence - was implemented within the network. It HAD to be. The end systems could not do anything more than send digits and send audio signals.
When the Internet came along, the endpoints and the switches were both programmable computers. So where to put the complexity? RFC 1958 – the architectural principles of the Internet RFC - that says “intelligence is end to end rather than hidden in the network.” That puts the intelligence clearly at the edge, like we see here. And that’s possible because the edge devices are smart; they’re programmable. Well that’s the diagram as I remember it 20 years ago.
And in the 20 years since, as we see the rise of middleboxes and SDN, we’re now seeing intelligence (in software) layered on top of “dumb” whiteboxes within the network. So I might add a brain here today. And with datacenters and content distribution networks, we see even smarter and more sophisticated application-level infrastructure being connected at points within the network. So now there are clearly much much bigger, much more computationally intensive and complex, endpoints if you will in today’s Internet

## Slide 107
Overview of Network layer:
  data plane
  control plane
What's inside a router
IP: Internet Protocol
  datagram format
  fragmentation
  IPv4 addressing
  network address translation
  IPv6
Chapter 4 summary
Generalized Forward and SDN
  match plus action
  OpenFlow example
Network Layer - the data plane

## Slide 108: Homework this week
Problems of Chapter 4:
P11
P17
Lab: https://www.github.com/network-whu/lab/
  7.Wireshark_IP.docx
  Hand-in: add to your lab report, in a separate chapter
Network Layer - the data plane