## Slide 1: Chapter 3 Transport Layer
Slides are adapted from those of by J.F Kurose and K.W. Ross with copyright 1996-2022 J.F Kurose and K.W. Ross, All Rights Reserved

## Slide 2: Chapter 3 Transport Layer
our goals:
understand principles behind transport layer services:
  multiplexing, demultiplexing
  reliable data transfer
  flow control
  congestion control
learn about Internet transport layer protocols:
  UDP: connectionless transport
  TCP: connection-oriented reliable transport
  TCP congestion control

## Slide 3
3.1 transport-layer services
3.2 multiplexing and demultiplexing
3.3 connectionless transport: UDP
3.4 principles of reliable data transfer
3.5 connection-oriented transport: TCP
3.6 principles of congestion control
3.7 TCP congestion control
3.8 Evolution of Transport-Layer Functionality
Chapter 3 Transport Layer
Transport Layer
3.1 transport-layer services

## Slide 4: Transport services and protocols
provide logical communication between app processes running on different hosts
transport protocols run in end systems
  send side: breaks app messages into segments, passes to network layer
  rcv side: reassembles segments into messages, passes to app layer
Two transport protocols available to internet apps
  TCP, UDP
3.1 transport-layer services
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
application
transport
network
data link
physical
application
transport
network
data link
physical
logical end-end transport
Notes: segment: 报文段

## Slide 5: Transport vs. network layer
Alibaba sending shipments to customers:
hosts = courier station
processes = shipper/consignee
app messages = shipment in express package
transport protocol = couriers demux to consignee
network-layer protocol = express delivery service
express delivery analogy:
3.1 transport-layer services
courier station
courier station
Notes: 快递小哥：delivery guy, delivery man, delivery boy, courier

## Slide 6: Transport vs. network layer
network layer: logical communication between hosts
transport layer: logical communication between processes
  relies on, enhances, network layer services
Alibaba sending shipments to customers:
hosts = courier station
processes = shipper/consignee
app messages = shipment in express package
transport protocol = couriers demux to consignee
network-layer protocol = express delivery service
express delivery analogy:
3.1 transport-layer services

## Slide 7: Transport Layer Actions
physical
link
network (IP)
application
physical
link
network (IP)
application
transport
Sender:
app. msg
is passed an application-layer message
determines segment header fields values
creates segment
passes segment to IP
transport
Th
Th
app. msg
3.1 transport-layer services

## Slide 8: Transport Layer Actions
physical
link
network (IP)
application
physical
link
network (IP)
application
transport
transport
Receiver:
app. msg
extracts application-layer message
checks header values
receives segment from IP
Th
app. msg
demultiplexes message up to application via socket
3.1 transport-layer services

## Slide 9: Internet transport-layer protocols
reliable, in-order delivery (TCP)
  congestion control
  flow control
  connection setup
unreliable, unordered delivery: UDP
  no-frills extension of "best-effort" IP
services not available:
  delay guarantees
  bandwidth guarantees
application
transport
network
data link
physical
application
transport
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
logical end-end transport
3.1 transport-layer services

## Slide 10
3.1 transport-layer services
3.2 multiplexing and demultiplexing
3.3 connectionless transport: UDP
3.4 principles of reliable data transfer
3.5 connection-oriented transport: TCP
3.6 principles of congestion control
3.7 TCP congestion control
3.8 Evolution of Transport-Layer Functionality
Chapter 3 Transport Layer
Transport Layer

## Slide 11: Multiplexing/demultiplexing
process
socket
use header info to deliver
received segments to correct
socket
demultiplexing at receiver:
handle data from multiple
sockets, add transport header (later used for demultiplexing)
multiplexing at sender:
transport
application
physical
link
network
P2
P1
transport
application
physical
link
network
P4
transport
application
physical
link
network
P3
3.2 multiplexing and demultiplexing

## Slide 12: How demultiplexing works
host receives IP datagrams
  each datagram has source IP address, destination IP address
  each datagram carries one transport-layer segment
  each segment has source, destination port number
host uses IP addresses & port numbers to direct segment to appropriate socket
source port #
dest port #
32 bits
application
data
(payload)
other header fields
TCP/UDP segment format
3.2 multiplexing and demultiplexing

## Slide 13: Connectionless demultiplexing
recall: created socket has host-local port #:
when host receives UDP segment:
  checks destination port # in segment
  directs UDP segment to socket with that port #
recall: when creating datagram to send into UDP socket, must specify
  destination IP address
  destination port #
IP datagrams with same dest. port #, but different source IP addresses and/or source port numbers will be directed to same socket at dest
3.2 multiplexing and demultiplexing
DatagramSocket mySocket1 =
newDatagramSocket（12534）；

## Slide 14: Connectionless demux: example
DatagramSocket serverSocket
= new DatagramSocket (6428);
transport
application
physical
link
network
P3
transport
application
physical
link
network
P1
transport
application
physical
link
network
P4
DatagramSocket mySocket1 = new DatagramSocket (5775);
DatagramSocket mySocket2 = new DatagramSocket (9157);
source port: 9157
dest port: 6428
source port: 6428
dest port: 9157
source port: ?
dest port: ?
source port: ?
dest port: ?
3.2 multiplexing and demultiplexing
host A
host B
host C

## Slide 15: Connection-oriented demux
TCP socket identified by 4-tuple:
  source IP address
  source port number
  dest IP address
  dest port number
demux: receiver uses all four values (4-tuple) to direct segment to appropriate socket
server may support many simultaneous TCP sockets:
  each socket identified by its own 4-tuple
  each socket associated with a different connecting client
3.2 multiplexing and demultiplexing
？
not really

## Slide 16: Connection-oriented demux: example
transport
application
physical
link
network
P1
transport
application
physical
link
P4
transport
application
physical
link
network
P2
source IP,port: A,9157
dest IP, port: B,80
source IP,port: B,80
dest IP,port: A,9157
host: IP address A
host: IP address C
network
P6
P5
P3
source IP,port: C,5775
dest IP,port: B,80
source IP,port: C,9157
dest IP,port: B,80
three segments, all destined to IP address: B,
dest port: 80 are demultiplexed to different sockets
server: IP address B
3.2 multiplexing and demultiplexing

## Slide 17: Connection-oriented demux: example
transport
application
physical
link
network
P3
transport
application
physical
link
transport
application
physical
link
network
P2
source IP,port: A,9157
dest IP, port: B,80
source IP,port: B,80
dest IP,port: A,9157
host: IP address A
host: IP address C
server: IP address B
network
P3
source IP,port: C,5775
dest IP,port: B,80
source IP,port: C,9157
dest IP,port: B,80
P4
threaded server
3.2 multiplexing and demultiplexing

## Slide 18: Summary
Multiplexing, demultiplexing: based on segment, datagram header field values
UDP: demultiplexing using destination port number (only)
TCP: demultiplexing using 4-tuple: source and destination IP addresses, and port numbers
Multiplexing/demultiplexing happen at all layers
3.2 multiplexing and demultiplexing

## Slide 19
3.1 transport-layer services
3.2 multiplexing and demultiplexing
3.3 connectionless transport: UDP
3.4 principles of reliable data transfer
3.5 connection-oriented transport: TCP
3.6 principles of congestion control
3.7 TCP congestion control
3.8 Evolution of Transport-Layer Functionality
Chapter 3 Transport Layer
Transport Layer

## Slide 20: UDP: User Datagram Protocol [RFC 768]
"no frills," "bare bones" Internet transport protocol
"best effort" service, UDP segments may be:
  lost
  delivered out-of-order to app
connectionless:
  no handshaking between UDP sender, receiver
  each UDP segment handled independently of others
3.3 connectionless transport: UDP
no connection establishment (which can add RTT delay)
simple: no connection state at sender, receiver
small header size
no congestion control:
  UDP can blast away as fast as desired
  can function in the face of congestion
why is there a UDP?

## Slide 21: UDP: User Datagram Protocol [RFC 768]
UDP use:
  streaming multimedia apps (loss tolerant, rate sensitive)
  DNS
  SNMP
  HTTP/3
reliable transfer over UDP:
  add needed reliability at application layer
  add congestion control at application layer
  application-specific error recovery!
  approach taken in HTTP/3
  google QUIC over HTTP/3
3.3 connectionless transport: UDP
https://datatracker.ietf.org/doc/rfc9114/
Notes: SNMP：simple network management protocol, application layer

## Slide 22: UDP: segment header
source port #
dest port #
32 bits
application
data
(payload)
UDP segment format
length
checksum
3.3 connectionless transport: UDP
length, in bytes of UDP segment, including header
data to/from application layer

## Slide 23: UDP checksum
Goal: detect "errors" (e.g., flipped bits) in transmitted segment
3.3 connectionless transport: UDP
Transmitted: 5 6 11
Received: 4 6 11
1st number
2nd number
sum
receiver-computed
checksum
sender-computed
checksum (as received)
=

## Slide 24: UDP checksum
sender:
treat contents of UDP segment (including header fields and IP addresses) as sequence of 16-bit integers
checksum: addition (one's complement sum) of segment contents
sender puts checksum value into UDP checksum field
receiver:
compute checksum of received segment
check if computed checksum equals checksum field value:
  NO - error detected
  YES - no error detected. But maybe errors nonetheless? More later ….
Goal: detect "errors" (e.g., flipped bits) in transmitted segment
3.3 connectionless transport: UDP
https://www.rfc-editor.org/rfc/rfc1071
Notes: one's complement sum 反码加法，需要加上进位；
two's complement sum 补码加法，丢弃进位进位；

## Slide 25: Internet checksum: example
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/
3.3 connectionless transport: UDP
example: add two 16-bit integers
sum
checksum
Note: when adding numbers, a carryout from the most significant bit needs to be added to the result
1 1 1 0 0 1 1 0 0 1 1 0 0 1 1 0
1 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1
1 1 0 1 1 1 0 1 1 1 0 1 1 1 0 1 1
wraparound
1 0 1 1 1 0 1 1 1 0 1 1 1 1 0 0
0 1 0 0 0 1 0 0 0 1 0 0 0 0 1 1
flip, invert, toggle
Notes: Kurose and Ross forgot to say anything about wrapping the carry of the MSB and adding it to low order bit
wrapped around
carry, carryout: 进位

## Slide 26: Internet checksum: weak protection!
example: add two 16-bit integers
sum
checksum
1 1 1 0 0 1 1 0 0 1 1 0 0 1 1 0
1 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1
1 1 0 1 1 1 0 1 1 1 0 1 1 1 0 1 1
wraparound
1 0 1 1 1 0 1 1 1 0 1 1 1 1 0 0
0 1 0 0 0 1 0 0 0 1 0 0 0 0 1 1
0 1
1 0
Even though numbers have changed (bit flips), no change in checksum!
3.3 connectionless transport: UDP

## Slide 27
3.1 transport-layer services
3.2 multiplexing and demultiplexing
3.3 connectionless transport: UDP
3.4 principles of reliable data transfer
3.5 connection-oriented transport: TCP
3.6 principles of congestion control
3.7 TCP congestion control
3.8 Evolution of Transport-Layer Functionality
Chapter 3 Transport Layer
Transport Layer

## Slide 28: Principles of reliable data transfer
important in application, transport, link layers
  top-10 list of important networking topics!
3.4 principles of reliable data transfer
sending
process
data
data
reliable channel
receiver
process
transport
layer
application
layer
Notes: characteristics of unreliable channel will determine complexity of reliable data transfer protocol (rdt)

## Slide 29: Principles of reliable data transfer
important in application, transport, link layers
  top-10 list of important networking topics!
3.4 principles of reliable data transfer
sending
process
data
data
reliable channel
receiver
process
transport
layer
application
layer
Notes: characteristics of unreliable channel will determine complexity of reliable data transfer protocol (rdt)

## Slide 30: Principles of reliable data transfer
important in application, transport, link layers
  top-10 list of important networking topics!
3.4 principles of reliable data transfer
sending
process
data
data
reliable channel
receiver
process
transport
layer
application
layer
Notes: characteristics of unreliable channel will determine complexity of reliable data transfer protocol (rdt)

## Slide 31: Principles of reliable data transfer
3.4 principles of reliable data transfer
sending
process
data
data
reliable channel
receiver
process
transport
layer
application
layer
unreliable channel
(a) reliable service abstraction
(b) reliable service implementation
network
layer
important in application, transport, link layers
  top-10 list of important networking topics!
Notes: characteristics of unreliable channel will determine complexity of reliable data transfer protocol (rdt)

## Slide 32: Principles of reliable data transfer
(a) reliable service abstraction
3.4 principles of reliable data transfer
sending
process
data
data
reliable channel
receiver
process
transport
layer
application
layer
unreliable channel
data
data
reliable data
transfer protocol
(sender side)
reliable data
transfer protocol
(receiver side)
rdt_send ( )
deliver_data ( )
udt_send ( )
rdt_rcv ( )
network
layer
important in application, transport, link layers
  top-10 list of important networking topics!
Complexity of reliable data transfer protocol will depend (strongly) on characteristics of unreliable channel (lose, corrupt, reorder data?)
sending
process
data
data
receiver
process
(b) reliable service implementation
Sender, receiver do not know the “state” of each other, e.g., was a message received?
unless communicated via a message
Notes: characteristics of unreliable channel will determine complexity of reliable data transfer protocol (rdt)
Here’s a point of view to keep in mind – it’s easy for US to look at sender and receiver together and see what is happening. OH – that message sent was lost.
But think about it say from senders POV How does the sender know if its transmitted message over the unreliable channel got though?? ONLY if receiver somehow signals to the sender that it was received.
The key point here is that one side does NOT know what is going on at the other side – it’s as if there’s a curtain between them. Everything they know about the other can ONLY be learned by sending/receiving messages.
Sender process wants to make sure a segment got through. But it can just somehow magically look through curtain to see if receiver got it. It will be up to the receiver to let the sender KNOW that it (the receiver) has correctly received the segment.
How will the sender and receiver do that – that’s the PROTOCOL.
Before starting to develop a protocol, let’s look more closely at the interface (the API if you will)

## Slide 33: Reliable data transfer protocol (rdt): interfaces
sender
side
receiver
side
rdt_send(): called from above, (e.g., by app.). Passed data to
deliver to receiver upper layer
udt_send(): called by rdt,
to transfer packet over
unreliable channel to receiver
rdt_rcv(): called when packet arrives on rcv-side of channel
deliver_data(): called by rdt to deliver data to upper
3.4 principles of reliable data transfer
implementation of rdt reliable data transfer protocol
implementation of rdt reliable data
transfer protocol
rdt_send ( )
deliver_data ( )
udt_send ( )
rdt_rcv ( )
unreliable channel
data
receiving
process
sending
process
data
Bi-directional communication over unreliable channel
data
packet
data
Header
data
Header

## Slide 34: Reliable data transfer: getting started
we'll:
incrementally develop sender, receiver sides of reliable data transfer protocol (rdt)
consider only unidirectional data transfer
  but control info will flow on both directions!
use finite state machines (FSM) to specify sender, receiver
state
1
state
2
event causing state transition
actions taken on state transition
state: when in this "state" next state uniquely determined by next event
event
actions
3.4 principles of reliable data transfer
Notes: actions: maybe several actions taken, or maybe only one action

## Slide 35: rdt1.0: reliable transfer over a reliable channel
underlying channel perfectly reliable
  no bit errors
  no loss of packets
separate FSMs for sender, receiver:
  sender sends data into underlying channel
  receiver reads data from underlying channel
sender
receiver
3.4 principles of reliable data transfer
Wait for call from above
packet = make_pkt(data)
udt_send(packet)
rdt_send(data)
extract (packet,data)
deliver_data(data)
Wait for call from below
rdt_rcv(packet)

## Slide 36: rdt2.0: channel with bit errors
underlying channel may flip bits in packet
  checksum (e.g., Internet checksum) to detect bit errors
the question: how to recover from errors?
3.4 principles of reliable data transfer
How do humans recover from "errors"
during conversation?
Repeat whenever there is a “pardon”
How do humans recover from “errors” during conversation?
Notes: Acknowledge 确认

## Slide 37: rdt2.0: channel with bit errors
underlying channel may flip bits in packet
  checksum (e.g., Internet checksum) to detect bit errors
the question: how to recover from errors?
  acknowledgements (ACKs): receiver explicitly tells sender that pkt received OK
  negative acknowledgements (NAKs): receiver explicitly tells sender that pkt had errors
  sender retransmits pkt on receipt of NAK
3.4 principles of reliable data transfer
How do humans recover from "errors"
during conversation?
Repeat whenever there is a “pardon”
stop and wait
sender sends one packet, then waits for receiver response
Notes: Acknowledge 确认

## Slide 38: rdt2.0: channel with bit errors
underlying channel may flip bits in packet
  checksum (e.g., Internet checksum) to detect bit errors
the question: how to recover from errors:
  acknowledgements (ACKs): receiver explicitly tells sender that pkt received OK
  negative acknowledgements (NAKs): receiver explicitly tells sender that pkt had errors
  sender retransmits pkt on receipt of NAK
new mechanisms in rdt2.0 (beyond rdt1.0):
  error detection
  feedback: control messages (ACK,NAK) from receiver → sender
3.4 principles of reliable data transfer
How do humans recover from "errors"
during conversation?
Repeat whenever there is a “pardon”
Notes: Acknowledge 确认

## Slide 39: rdt2.0: FSM specification
3.4 principles of reliable data transfer
Wait for call from above
udt_send(sndpkt)
rdt_rcv(rcvpkt) && isNAK(rcvpkt)
Wait for ACK or NAK
udt_send(NAK)
rdt_rcv(rcvpkt) && corrupt(rcvpkt)
Wait for call from below
extract(rcvpkt,data)
deliver_data(data)
udt_send(ACK)
rdt_rcv(rcvpkt) && notcorrupt(rcvpkt)
snkpkt = make_pkt(data, checksum)
udt_send(sndpkt)
rdt_send(data)
rdt_rcv(rcvpkt) && isACK(rcvpkt)
L
sender
receiver

## Slide 40: rdt2.0: FSM specification
3.4 principles of reliable data transfer
Wait for call from above
udt_send(sndpkt)
rdt_rcv(rcvpkt) && isNAK(rcvpkt)
Wait for ACK or NAK
udt_send(NAK)
rdt_rcv(rcvpkt) && corrupt(rcvpkt)
Wait for call from below
snkpkt = make_pkt(data, checksum)
udt_send(sndpkt)
rdt_send(data)
rdt_rcv(rcvpkt) && isACK(rcvpkt)
L
sender
receiver
Note: "state" of receiver (did the receiver get my message correctly?) isn’t known to sender unless somehow communicated from receiver to sender
that’s why we need a protocol!

## Slide 41: rdt2.0: operation with no errors
Wait for call from above
snkpkt = make_pkt(data, checksum)
udt_send(sndpkt)
extract(rcvpkt,data)
deliver_data(data)
udt_send(ACK)
rdt_rcv(rcvpkt) &&
notcorrupt(rcvpkt)
rdt_rcv(rcvpkt) && isACK(rcvpkt)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
isNAK(rcvpkt)
udt_send(NAK)
rdt_rcv(rcvpkt) &&
corrupt(rcvpkt)
Wait for ACK or NAK
Wait for call from below
rdt_send(data)
L
3.4 principles of reliable data transfer
sender
receiver

## Slide 42: rdt2.0: error scenario
Wait for call from above
snkpkt = make_pkt(data, checksum)
udt_send(sndpkt)
extract(rcvpkt,data)
deliver_data(data)
udt_send(ACK)
rdt_rcv(rcvpkt) &&
notcorrupt(rcvpkt)
rdt_rcv(rcvpkt) && isACK(rcvpkt)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
isNAK(rcvpkt)
udt_send(NAK)
rdt_rcv(rcvpkt) &&
corrupt(rcvpkt)
Wait for ACK or NAK
Wait for call from below
rdt_send(data)
L
3.4 principles of reliable data transfer
receiver
sender

## Slide 43: rdt2.0 has a fatal flaw!
what happens if ACK/NAK corrupted?
sender doesn't know what happened at receiver!
can't just retransmit: possible duplicate
handling duplicates:
sender retransmits current pkt if ACK/NAK corrupted
sender adds sequence number to each pkt
receiver discards (doesn't deliver up) duplicate pkt
stop and wait
sender sends one packet,
then waits for receiver
response
3.4 principles of reliable data transfer

## Slide 44: rdt2.1: sender, handles garbled ACK/NAKs
3.4 principles of reliable data transfer
Wait for call 0 from above
Wait for ACK or NAK 0
sndpkt = make_pkt(0, data, checksum)
udt_send(sndpkt)
rdt_send(data)
udt_send(sndpkt)
rdt_rcv(rcvpkt) && (corrupt(rcvpkt) || isNAK(rcvpkt) )
sndpkt = make_pkt(1, data, checksum)
udt_send(sndpkt)
rdt_send(data)
udt_send(sndpkt)
rdt_rcv(rcvpkt) && (corrupt(rcvpkt) ||
isNAK(rcvpkt) )
Wait for
call 1 from above
Wait for ACK or NAK 1
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt)
L
rdt_rcv(rcvpkt) && notcorrupt(rcvpkt) && isACK(rcvpkt)
L
Notes: garbley gook
gobbledygook

## Slide 45: rdt2.1: receiver, handles garbled ACK/NAKs
3.4 principles of reliable data transfer
Wait for
0 from below
rdt_rcv(rcvpkt) && notcorrupt(rcvpkt)
&& has_seq1(rcvpkt)
extract(rcvpkt,data)
deliver_data(data)
sndpkt = make_pkt(ACK, chksum)
udt_send(sndpkt)
Wait for
1 from below
rdt_rcv(rcvpkt) && notcorrupt(rcvpkt)
&& has_seq0(rcvpkt)
extract(rcvpkt,data)
deliver_data(data)
sndpkt = make_pkt(ACK, chksum)
udt_send(sndpkt)
sndpkt = make_pkt(NAK, chksum)
udt_send(sndpkt)
rdt_rcv(rcvpkt) && (corrupt(rcvpkt)
rdt_rcv(rcvpkt) &&
not corrupt(rcvpkt) &&
has_seq0(rcvpkt)
sndpkt = make_pkt(ACK, chksum)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
not corrupt(rcvpkt) &&
has_seq1(rcvpkt)
sndpkt = make_pkt(ACK, chksum)
udt_send(sndpkt)
rdt_rcv(rcvpkt) && (corrupt(rcvpkt)
sndpkt = make_pkt(NAK, chksum)
udt_send(sndpkt)

## Slide 46: rdt2.1: discussion
sender:
seq # added to pkt
two seq. #s (0,1) will suffice. Why?
must check if received ACK/NAK corrupted
twice as many states
  state must "remember" whether "expected" pkt should have seq # of 0 or 1
receiver:
must check if received packet is duplicate
  state indicates whether 0 or 1 is expected pkt seq #
note: receiver can not know if its last ACK/NAK received OK at sender
3.4 principles of reliable data transfer

## Slide 47: rdt2.2: a NAK-free protocol
same functionality as rdt2.1, using ACKs only
instead of NAK, receiver sends ACK for last pkt received OK
  receiver must explicitly include seq # of pkt being ACKed
duplicate ACK at sender results in same action as NAK: retransmit current pkt
3.4 principles of reliable data transfer
As we will see, TCP uses this approach to be NAK-free

## Slide 48: rdt2.2: sender, receiver fragments
Wait for call 0 from above
sndpkt = make_pkt(0, data, checksum)
udt_send(sndpkt)
rdt_send(data)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
( corrupt(rcvpkt) ||
isACK(rcvpkt,1) )
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt,0)
Wait for ACK
0
sender FSM
fragment
rdt_rcv(rcvpkt) && notcorrupt(rcvpkt)
&& has_seq1(rcvpkt)
extract(rcvpkt,data)
deliver_data(data)
sndpkt = make_pkt(ACK1, chksum)
udt_send(sndpkt)
Wait for
0 from below
rdt_rcv(rcvpkt) &&
(corrupt(rcvpkt) ||
has_seq1(rcvpkt))
udt_send(sndpkt)
receiver FSM
fragment
L
3.4 principles of reliable data transfer

## Slide 49: rdt3.0: channels with errors and loss
timeout
new assumption: underlying channel can also lose packets (data, ACKs)
  checksum, seq. #, ACKs, retransmissions will be of help … but not enough
approach: sender waits "reasonable" amount of time for ACK
retransmits if no ACK received in this time
if pkt (or ACK) just delayed (not lost):
  retransmission will be duplicate, but seq. #'s already handles this
  receiver must specify seq # of pkt being ACKed
requires countdown timer
3.4 principles of reliable data transfer
How do humans handle lost sender-to-receiver words in conversation?

## Slide 50: rdt3.0 sender
3.4 principles of reliable data transfer
Wait for ACK0
sndpkt = make_pkt(0, data, checksum)
udt_send(sndpkt)
start_timer
rdt_send(data)
Wait for
call 1 from above
sndpkt = make_pkt(1, data, checksum)
udt_send(sndpkt)
start_timer
rdt_send(data)
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt,0)
stop_timer
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt,1)
stop_timer
udt_send(sndpkt)
start_timer
timeout
Wait for
call 0 from above
Wait for ACK1
L
rdt_rcv(rcvpkt)
rdt_rcv(rcvpkt) &&
( corrupt(rcvpkt) ||
isACK(rcvpkt,1) )
L
rdt_rcv(rcvpkt)
L
rdt_rcv(rcvpkt) &&
( corrupt(rcvpkt) ||
isACK(rcvpkt,0) )
udt_send(sndpkt)
start_timer
timeout
L

## Slide 51: rdt3.0 in action
sender
receiver
rcv pkt1
rcv pkt0
send ack0
send ack1
send ack0
rcv ack0
send pkt0
send pkt1
rcv ack1
send pkt0
rcv pkt0
pkt0
pkt0
pkt1
ack1
ack0
ack0
(a) no loss
sender
receiver
rcv pkt1
rcv pkt0
send ack0
send ack1
send ack0
rcv ack0
send pkt0
send pkt1
rcv ack1
send pkt0
rcv pkt0
pkt0
pkt0
ack1
ack0
ack0
(b) packet loss
pkt1
X
loss
pkt1
timeout
resend pkt1
3.4 principles of reliable data transfer

## Slide 52: rdt3.0 in action
rcv pkt1
send ack1
(detect duplicate)
pkt1
sender
receiver
rcv pkt1
rcv pkt0
send ack0
send ack1
send ack0
rcv ack0
send pkt0
send pkt1
rcv ack1
send pkt0
rcv pkt0
pkt0
pkt0
ack1
ack0
ack0
(c) ACK loss
ack1
X
loss
pkt1
timeout
resend pkt1
rcv pkt1
send ack1
(detect duplicate)
pkt1
sender
receiver
rcv pkt1
send ack0
rcv ack0
send pkt1
send pkt0
rcv pkt0
pkt0
ack0
(d) premature timeout/ delayed ACK
pkt1
timeout
resend pkt1
ack1
send ack1
(ignore)
rcv ack1
pkt1
ack1
send pkt0
rcv ack1
pkt0
rcv pkt0
send ack0
ack0
3.4 principles of reliable data transfer

## Slide 53: Performance of rdt3.0
rdt3.0 is correct, but performance stinks
e.g.: 1 Gbps link, 15 ms prop. delay, 8000 bit packet:
  time to transmit packet into channel:
  Usender: utilization – fraction of time sender busy sending
  if RTT=30 msec, 1KB pkt every 30 msec: 33kB/sec thruput over 1 Gbps link
network protocol limits use of physical resources!
Dtrans =
L
R
8000 bits
10 9 bits/sec
=
=
8 microsecs
3.4 principles of reliable data transfer
Notes: ms: millisecond 毫秒 = 0.001 second
microsecond微秒=0.000001 second
1/(30+1000/1024) * 1000 = 33 kB/s

## Slide 54: rdt3.0: stop-and-wait operation
first packet bit transmitted, t = 0
sender
receiver
RTT
last packet bit transmitted, t = L / R
first packet bit arrives
last packet bit arrives, send ACK
ACK arrives, send next
packet, t = RTT + L / R
3.4 principles of reliable data transfer

## Slide 55: Pipelined protocols
pipelining: sender allows multiple, "in-flight", yet-to-be-acknowledged pkts
  range of sequence numbers must be increased
  buffering at sender and/or receiver
two generic forms of pipelined protocols: go-Back-N, selective repeat
3.4 principles of reliable data transfer

## Slide 56: Pipelining: increased utilization
first packet bit transmitted, t = 0
sender
receiver
RTT
last bit transmitted, t = L / R
first packet bit arrives
last packet bit arrives, send ACK
ACK arrives, send next
packet, t = RTT + L / R
last bit of 2nd packet arrives, send ACK
last bit of 3rd packet arrives, send ACK
3-packet pipelining increases utilization by a factor of 3!
3.4 principles of reliable data transfer
81

## Slide 57: Pipelined protocols: overview
Go-back-N:
sender can have up to N unacked packets in pipeline
receiver only sends cumulative ack
  doesn't ack packet if there's a gap
sender has timer for oldest unacked packet
  when timer expires, retransmit all unacked packets
Selective Repeat:
sender can have up to N unack'ed packets in pipeline
rcvr sends individual ack for each packet
sender maintains timer for each unacked packet
  when timer expires, retransmit only that unacked packet
3.4 principles of reliable data transfer

## Slide 58: Go-Back-N: sender
k-bit seq # in pkt header
"window" of up to N, consecutive unack'ed pkts allowed
3.4 principles of reliable data transfer
already
ack’ed
sent, not yet ack’ed
usable, not yet sent
not usable
Window size
N
nextseqnum
cumulative ACK： ACK(n): ACKs all pkts up to, including seq # n
  may receive duplicate ACKs (see receiver)
  on receiving ACK(n): move window forward to begin at n+1
timer for oldest in-flight pkt
timeout(n): retransmit packet n and all higher seq # pkts in window
send_base

## Slide 59: Go-Back-N: receiver
ACK-only: always send ACK for correctly-received packet so far, with highest in-order seq #
  may generate duplicate ACKs
  need only remember rcv_base
on receipt of out-of-order packet:
  can discard (don’t buffer) or buffer: an implementation decision
  re-ACK pkt with highest in-order seq #
rcv_base
received and ACKed
Out-of-order: received but not ACKed
Not received
Receiver view of sequence number space:
…
…
3.4 principles of reliable data transfer
Notes: Note – we’ll skip the Go-Back-N FSM specification (actually it’s simple)

## Slide 60: Go-Back-N: sender extended FSM
3.4 principles of reliable data transfer
Wait
start_timer
udt_send(sndpkt[base])
udt_send(sndpkt[base+1])
…
udt_send(sndpkt[nextseqnum-1])
timeout
rdt_send(data)
if (nextseqnum < base+N) {
sndpkt[nextseqnum] = make_pkt(nextseqnum,data,chksum)
udt_send(sndpkt[nextseqnum])
if (base == nextseqnum)
start_timer
nextseqnum++
}
else
refuse_data(data)
base = getacknum(rcvpkt)+1
If (base == nextseqnum)
stop_timer
else
start_timer
rdt_rcv(rcvpkt) &&
notcorrupt(rcvpkt)
base=1
nextseqnum=1
rdt_rcv(rcvpkt)
&& corrupt(rcvpkt)
L
L

## Slide 61: Go-Back-N : receiver extended FSM
ACK-only: always send ACK for correctly-received pkt with highest in-order seq #
  may generate duplicate ACKs
  need only remember expectedseqnum
out-of-order pkt:
  discard (don't buffer): no receiver buffering!
  re-ACK pkt with highest in-order seq #
3.4 principles of reliable data transfer
Wait
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& hasseqnum(rcvpkt,expectedseqnum)
extract(rcvpkt,data)
deliver_data(data)
sndpkt = make_pkt(expectedseqnum,ACK,chksum)
udt_send(sndpkt)
expectedseqnum++
udt_send(sndpkt)
any other event
expectedseqnum=1
sndpkt =
make_pkt(expectedseqnum,ACK,chksum)
L

## Slide 62: Go-Back-N in action
send pkt0
send pkt1
send pkt2
send pkt3
(wait)
sender
receiver
receive pkt0, send ack0
receive pkt1, send ack1
receive pkt3, discard,
(re)send ack1
rcv ack0, send pkt4
rcv ack1, send pkt5
pkt 2 timeout
send pkt2
send pkt3
send pkt4
send pkt5
X
loss
receive pkt4, discard,
(re)send ack1
receive pkt5, discard,
(re)send ack1
rcv pkt2, deliver, send ack2
rcv pkt3, deliver, send ack3
rcv pkt4, deliver, send ack4
rcv pkt5, deliver, send ack5
ignore duplicate ACK
0 1 2 3 4 5 6 7 8
sender window (N=4)
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
3.4 principles of reliable data transfer

## Slide 63: Selective repeat
receiver individually acknowledges all correctly received pkts
  buffers pkts, as needed, for eventual in-order delivery to upper layer
sender times-out/retransmits individually for unACKed packets
  sender maintains timer for each unACKed pkt
sender window
  N consecutive seq #'s
  limits seq #s of sent, unACKed pkts
3.4 principles of reliable data transfer
Notes: An important mechanism of GBN was the use of the cumulative acknowledgements, and as we mentioned, cumulative ACKs are used in TCP
An alternate ACK mechanism would be for the receiver to individually acknowledge specific packets as they are received. This mechanism is at the heart of the Selective repeat protocol.

## Slide 64: Selective repeat: sender, receiver windows
nextseqnum
3.4 principles of reliable data transfer
already
ack’ed
sent, not yet ack’ed
usable, not yet sent
not usable
Window size
N
send_base
Window size
N
not usable
expected, not yet received
out of order (buffered) but already ack’ed
acceptable
(within window)
(b) receiver view of sequence numbers
rcv_base
(a) sender view of sequence numbers

## Slide 65: Selective repeat
data from above:
if next available seq # in window, send pkt
timeout(n):
resend pkt n, restart timer
ACK(n) in [sendbase,sendbase+N]:
mark pkt n as received
if n smallest unACKed pkt, advance window base to next unACKed seq #
sender
pkt n in [rcvbase, rcvbase+N-1]
send ACK(n)
out-of-order: buffer
in-order: deliver (also deliver buffered, in-order pkts), advance window to next not-yet-received pkt
pkt n in [rcvbase-N,rcvbase-1]
ACK(n)
otherwise:
ignore
receiver
3.4 principles of reliable data transfer
Notes: If the packet is in order, its data will be delivered, as will any buffered data that can now be delivered in order

## Slide 66: Selective Repeat in action
send pkt0
send pkt1
send pkt2
send pkt3
(wait)
sender
receiver
send pkt2
(but not 3,4,5)
X
loss
pkt 2 timeout
sender window (N=4)
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
rcv ack0, send pkt4
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
rcv ack1, send pkt5
receive pkt0, send ack0
receive pkt1, send ack1
receive pkt3, buffer,
send ack3
record ack3 arrived
receive pkt4, buffer,
send ack4
receive pkt5, buffer,
send ack5
rcv pkt2; deliver pkt2,
pkt3, pkt4, pkt5; send ack2
Q: what happens when ack2 arrives?
3.4 principles of reliable data transfer

## Slide 67: Selective repeat: a dilemma
example:
seq #'s: 0, 1, 2, 3
window size=3
receiver window
(after receipt)
sender window
(after receipt)
0 1 2 3 0 1 2
0 1 2 3 0 1 2
0 1 2 3 0 1 2
pkt0
pkt1
pkt2
0 1 2 3 0 1 2
pkt0
timeout
retransmit pkt0
0 1 2 3 0 1 2
0 1 2 3 0 1 2
0 1 2 3 0 1 2
X
X
X
will accept packet
with seq number 0
(b) oops!
0 1 2 3 0 1 2
0 1 2 3 0 1 2
0 1 2 3 0 1 2
pkt0
pkt1
pkt2
0 1 2 3 0 1 2
pkt0
0 1 2 3 0 1 2
0 1 2 3 0 1 2
0 1 2 3 0 1 2
X
will accept packet
with seq number 0
0 1 2 3 0 1 2
pkt3
(a) no problem
receiver can't see sender side.
receiver behavior identical in both cases!
something's (very) wrong!
receiver sees no difference in two scenarios!
duplicate data accepted as new in (b)
Q: what relationship between seq # size and window size to avoid problem in (b)?
3.4 principles of reliable data transfer

## Slide 68: Additional slide for python environment
Find out the installation position of your python, say “C:\Python39", add it to the global environment variable PATH
Run the command cmd as an Administrator
In the command line input "python -m pip install -U pip" and enter to run the command to upgrade python installation package
Run the command "pip install -i http://mirrors.aliyun.com/pypi/simple matplotlib" to install matplot library into your python invironment
Other alternative mirror sites:
  https://pypi.mirrors.ustc.edu.cn/simple
  https://pypi.douban.com/simple
  https://pypi.mirrors.opencas.cn/simple
Transport Layer
https://learn.microsoft.com/en-us/visualstudio/python/tutorial-working-with-python-in-visual-studio-step-00-installation?view=vs-2022

## Slide 69: Homework Week 7
Problems of Chapter 3:
P3
P4
Coding
Use python to implement the Internet checksum
deadline: Tuesday, Week 9
use matplotlib
Transport Layer

## Slide 70
3.1 transport-layer services
3.2 multiplexing and demultiplexing
3.3 connectionless transport: UDP
3.4 principles of reliable data transfer
3.5 connection-oriented transport: TCP
3.6 principles of congestion control
3.7 TCP congestion control
3.8 Evolution of Transport-Layer Functionality
Chapter 3 Transport Layer
Transport Layer

## Slide 71
3.1 transport-layer services
3.2 multiplexing and demultiplexing
3.3 connectionless transport: UDP
3.4 principles of reliable data transfer
3.5 connection-oriented transport: TCP
    segment structure
    reliable data transfer
    flow control
    connection management
3.6 principles of congestion control
3.7 TCP congestion control
3.8 Evolution of Transport-Layer Functionality
Transport Layer
Chapter 3 Transport Layer

## Slide 72: TCP: Overview RFCs: 793,1122,2018,5681,7323
cumulative ACKs
full duplex data:
  bi-directional data flow in same connection
  MSS: maximum segment size
connection-oriented:
  handshaking (exchange of control msgs) initializes sender, receiver state before data exchange
flow controlled:
  sender will not overwhelm receiver
point-to-point:
  one sender, one receiver
reliable, in-order byte stream:
  no "message boundaries"
pipelined:
  TCP congestion and flow control set window size
3.5 connection-oriented transport: TCP
Notes: Link layer MTU : Maximum Transmission Unit
Typical MSS is 1460 bytes

## Slide 73
3.1 transport-layer services
3.2 multiplexing and demultiplexing
3.3 connectionless transport: UDP
3.4 principles of reliable data transfer
3.5 connection-oriented transport: TCP
    segment structure
    reliable data transfer
    flow control
    connection management
3.6 principles of congestion control
3.7 TCP congestion control
Transport Layer
Chapter 3 Transport Layer

## Slide 74: TCP segment structure
IP header
IP data
TCP header
TCP data
source port #
dest port #
32 bits
application
data
(variable length)
sequence number
acknowledgement number
receive window
Urg data pointer
checksum
F
S
R
P
A
U
head
len
not
used
options (variable length)
URG: urgent data
(generally not used)
ACK: ACK #
valid
PSH: push data now
(generally not used)
RST, SYN, FIN:
connection estab
(setup, teardown
commands)
# bytes
rcvr willing
to accept (rwnd)
counting by bytes of data
(not segments!)
Internet
checksum
(as in UDP)
3.5 connection-oriented transport: TCP
HLEN
4
RSVD
4
URG
ACK
PSH
RST
SYN
FIN
Flag field
ECE
CWR
CWR & ECE:
Explicit congestion
Notification (3.7.2)
CWR
ECE
data sent by application into TCP socket
urgent data (generally not used)
flow
control
Notes: https://kb.clavister.com/317180249/explicit-congestion-notification---ecn-ece-cwe-ns-ect-ce
CWR (Congestion Window Reduced)
Congestion Encountered （CE）
ECE - Echo of Congestion Encountered - starts being set in TCP packets when "CE" is seen
CWR - Congestion Window Reduced = "OK, I saw your ECE, you can turn it off now"

## Slide 75: TCP seq. numbers, ACKs
sequence numbers:
  byte stream "number" of first byte in segment's data
acknowledgements:
  seq # of next byte expected from other side
  cumulative ACK
Q: how receiver handles out-of-order segments
A: TCP spec doesn't say, up to implementor
source port #
dest port #
sequence number
acknowledgement number
checksum
rwnd
urg pointer
incoming segment to sender
A
sent
ACKed
sent, not-yet ACKed
("in-flight")
usable
but not
yet sent
not
usable
window size
N
  sender sequence number space
source port #
dest port #
sequence number
acknowledgement number
checksum
rwnd
urg pointer
outgoing segment from sender
3.5 connection-oriented transport: TCP
outgoing segment from receiver

## Slide 76: TCP seq. numbers, ACKs
3.5 connection-oriented transport: TCP
host ACKs receipt of echoed ‘C’
host ACKs receipt of‘C’, echoes back ‘C’
simple telnet scenario
Host B
Host A
User types‘C’
Seq=42, ACK=79, data = ‘C’
Seq=79, ACK=43, data = ‘C’
Seq=43, ACK=80
Notes: The key thing to note here is that the ACK number (43) on the B-to-A segment is one more than the sequence number (42) on the A-to-B segment that triggered that ACK
Similarly, the ACK number (80) on the last A-to-B segment is one more than the sequence number (79) on the B-to-A segment that triggered that ACK

## Slide 77: TCP round trip time, timeout
Q: how to set TCP timeout value?
longer than RTT
  but RTT varies
too short: premature timeout, unnecessary retransmissions
too long: slow reaction to segment loss
Q: how to estimate RTT?
SampleRTT: measured time from segment transmission until ACK receipt
  ignore retransmissions
SampleRTT will vary, want estimated RTT "smoother"
  average several recent measurements, not just current SampleRTT
3.5 connection-oriented transport: TCP

## Slide 78: TCP round trip time, timeout
EstimatedRTT = (1- )*EstimatedRTT + *SampleRTT
exponential weighted moving average (EWMA)
influence of past sample decreases exponentially fast
typical value:  = 0.125
RTT (milliseconds)
RTT: gaia.cs.umass.edu to fantasia.eurecom.fr
sampleRTT
EstimatedRTT
time (seconds)
3.5 connection-oriented transport: TCP
Notes: Samples oscillate up and down, fluctuate around the mean value.
This is how TCP re-computes the estimated RTT each time a new SampleRTT is taken.
The process is known as an exponentially weighted moving average, shown by the equation here.
<say it>
Where alpha reflects the influence of the most recent measurements on the estimated RTT; a typical value of alpha used in implementations is .125
The graph at the bottom show measured RTTs between a host in the Massachusetts and a host in France, as well as the estimated, “smoothed” RTT

## Slide 79: TCP round trip time, timeout
timeout interval: EstimatedRTT plus "safety margin"
  large variation in EstimatedRTT： want a larger safety margin
estimate SampleRTT deviation from EstimatedRTT:
DevRTT = (1-)*DevRTT +
*|SampleRTT-EstimatedRTT|
(typically,  = 0.25)
TimeoutInterval = EstimatedRTT + 4*DevRTT
estimated RTT
"safety margin"
3.5 connection-oriented transport: TCP
Notes: Given this value of the estimated RTT, TCP computes the timeout interval to be the estimated RTT plus a “safety margin”
And the intuition is that if we are seeing a large variation in SAMPLERTT – the RTT estimates are fluctuating a lot - then we’ll want a larger safety margin
So TCP computes the Timeout interval to be the Estimated RTT plus 4 times a measure of deviation in the RTT.
The deviation in the RTT is computed as the eWMA of the difference between the most recently measured SampleRTT from the Estimated RTT

## Slide 80
3.1 transport-layer services
3.2 multiplexing and demultiplexing
3.3 connectionless transport: UDP
3.4 principles of reliable data transfer
3.5 connection-oriented transport: TCP
    segment structure
    reliable data transfer
    flow control
    connection management
3.6 principles of congestion control
3.7 TCP congestion control
Transport Layer
Chapter 3 Transport Layer

## Slide 81: TCP reliable data transfer
TCP creates process-to-process reliable transfer of segments on top of IP’s unreliable host-to-host delivery of IP datagram
  pipelining of segments
  cumulative acks
  single retransmission timer
retransmissions triggered by:
  duplicate acks
  timeout events
let's initially consider simplified TCP sender:
  ignore duplicate acks
  ignore flow control, congestion control
3.5 connection-oriented transport: TCP

## Slide 82: TCP sender events (simplified) :
event: data rcvd from app
create segment with seq #
seq # is byte-stream number of first data byte in segment
start timer if not already running
  think of timer as for oldest unACKed segment
  expiration interval: TimeOutInterval
event: timeout
retransmit segment that caused timeout
restart timer
event: ACK rcvd
if ACK acknowledges previously unACKed segments
  update what is known to be ACKed
  start timer if there are still unACKed segments
3.5 connection-oriented transport: TCP
Notes: Given these details of TCP sequence numbers, acks, and timers, we can now describe the big picture view of how the TCP sender and receiver operate
You can check out FSMs in book; let’s just give an English text description here and let’s start with the sender.

## Slide 83: TCP ACK generation Recommendation [RFC 5681]
event at receiver
arrival of in-order segment with
expected seq #. All data up to
expected seq # already ACKed
arrival of in-order segment with
expected seq #. One other
segment has ACK pending
arrival of out-of-order segment
higher-than-expect seq. # .
Gap detected
arrival of segment that
partially or completely fills gap
TCP receiver action
delayed ACK. Wait up to 500ms
for next segment. If no next segment,
send ACK
immediately send single cumulative
ACK, ACKing both in-order segments
immediately send duplicate ACK,
indicating seq. # of next expected byte
immediate send ACK, provided that
segment starts at lower end of gap
3.5 connection-oriented transport: TCP
Notes: duplicate ACK: 冗余ACK，ACK复本
Rather than immediately ACKnowledge this segment, many TCP implementations will wait for half a second for another in-order segment to arrive, and then generate a single cumulative ACK for both segments – thus decreasing the amount of ACK traffic. The arrival of this second in-order segment and the cumulative ACK generation that covers both segments is the second row in this table.

## Slide 84: TCP: retransmission scenarios
3.5 connection-oriented transport: TCP
lost ACK scenario
Host B
Host A
Seq=92, 8 bytes of data
Seq=92, 8 bytes of data
ACK=100
X
ACK=100
timeout
premature timeout
Host B
Host A
Seq=92, 8
bytes of data
ACK=120
timeout
ACK=100
ACK=120
SendBase=100
SendBase=120
SendBase=120
Seq=92, 8 bytes of data
Seq=100, 20 bytes of data
SendBase=92
send cumulative
ACK for 120
Notes: To cement our understanding of TCP reliability, let’s look at a few retransmission scenarios
In the first case a TCP segments is transmitted and the ACK is lost, and the TCP timeout mechanism results in another copy of being transmitted and then re-ACKed a the sender
In the second example two segments are sent and acknowledged, but there is a premature timeout for the first segment, which is retransmitted. Note that when this retransmitted segment is received, the receiver has already received the first two segments, and so resends a cumulative ACK for both segments received so far, rather than an ACK for just this first segment.

## Slide 85: TCP: retransmission scenarios
3.5 connection-oriented transport: TCP
cumulative ACK covers for earlier lost ACK
Host B
Host A
Seq=92, 8 bytes of data
Seq=120, 15 bytes of data
Seq=100, 20 bytes of data
X
ACK=100
ACK=120
Notes: And in this last example, two segments are again transmitted, the first ACK is lost but the second ACK, a cumulative ACK arrives at the sender, which then can transmit a third segment, knowing that the first two have arrived, even though the ACK for the first segment was lost

## Slide 86: TCP fast retransmit
time-out period often relatively long:
  long delay before resending lost packet
detect lost segments via duplicate ACKs.
  sender often sends many segments back-to-back
  if segment is lost, there will likely be many duplicate ACKs. , so treat three duplicate ACKs in a row as a segment loss indicator
if sender receives 3 ACKs for same data
("triple duplicate resend unACKed segment with smallest seq #
  likely that unACKed segment lost, so don't wait for timeout
TCP fast retransmit
("triple duplicate ACKs"),
3.5 connection-oriented transport: TCP
X
fast retransmit after sender
receipt of triple duplicate ACK
Host B
Host A
Seq=92, 8 bytes of data
ACK=100
timeout
ACK=100
ACK=100
ACK=100
Seq=100, 20 bytes of data
Seq=100, 20 bytes of data
Notes: Let’s wrap up our study of TCP reliability by discussing an optimization to the original TCP known as TCP fast retransmit,
Take a look at this example on the right where 5 segments are transmitted and the second segment is lost. In this case the TCP receiver sends an ACK 100 acknowledging the first received segment.
When the third segment arrives at the receiver, the TCP receiver sends another ACK 100 since the second segment has not arrived. And similarly for the 4th and 5th segments to arrive.
Now what does the sender see? The sender receives the first ACK 100 it has been hoping for, but then three additional duplicate ACK100s arrive. The sender knows that somethings’ wrong – it knows the first segment arrived at the receiver but three later arriving segments at the receiver – the ones that generated the three duplicate ACKs – we received correctly but were not in order. That is, that there was a missing segment at the receiver when each of the three duplicate ACK were generated.
With fast retransmit, the arrival of three duplicate ACK causes the sender to retransmit its oldest unACKed segment, without waiting for a timeout event. This allows TCP to recover more quickly from what is very likely a loss event
specifically that the second segment has been lost, since three higher -numbered segments were received

## Slide 87
3.1 transport-layer services
3.2 multiplexing and demultiplexing
3.3 connectionless transport: UDP
3.4 principles of reliable data transfer
3.5 connection-oriented transport: TCP
    segment structure
    reliable data transfer
    flow control
    connection management
3.6 principles of congestion control
3.7 TCP congestion control
Transport Layer
Chapter 3 Transport Layer

## Slide 88: TCP flow control
application
process
TCP socket
receiver buffers
TCP
code
IP
code
receiver protocol stack
Q: What happens if network layer delivers data faster than application layer removes data from socket buffers?
Network layer delivering IP datagram payload into TCP socket buffers
from sender
Application removing data from TCP socket buffers
3.5 connection-oriented transport: TCP
Notes: (Presuming an intro)
Before diving into the details of TCP flow control, let’s first get the general context and motivate the need for flow control.
This diagram shows a typical transport-layer implementation
A segment is brought up the protocol stack to the transport layer, and the segment’s payload is removed from the segment and written INTO socket buffers.
How does data get taken OUT of socket buffers? By applications performing socket reads, as we learned in Chapter 2.
And so the question is “What happens if network layer delivers data faster than an application-layer process removes data from socket buffers?”

## Slide 89: TCP flow control
3.5 connection-oriented transport: TCP
Q: What happens if network layer delivers data faster than application layer removes data from socket buffers?
application
process
TCP socket
receiver buffers
TCP
code
IP
code
receiver protocol stack
Network layer delivering IP datagram payload into TCP socket buffers
from sender
Application removing data from TCP socket buffers
no one can drink from a firehose
Notes: Let’s watch a video of what happens when things arrive way too fast to be processed.
Another human analogy showing the need for flow control is the saying – to use some English slang - “no one can drink from a firehose”
Flow control is a mechanism to the calamity of a receiver being over-run by a sender that is sending too fast – it allows the RECEIVER to explicitly control the SENDER so sender won’t overflow receiver’s buffer by transmitting too much, too fast

## Slide 90: TCP flow control
application
process
TCP socket
receiver buffers
TCP
code
IP
code
application
OS
receiver protocol stack
application copying/
removing data from
TCP socket buffers ….
… slower than TCP
receiver is delivering
(sender is sending)
from sender
receiver controls sender, so sender won't overflow receiver's buffer by transmitting too much, too fast
flow control
3.5 connection-oriented transport: TCP
Q: What happens if network layer delivers data faster than application layer removes data from socket buffers?
Network layer delivering IP datagram payload into TCP socket buffers
zero-copy
Notes: A short introduction to zero-copy

## Slide 91: TCP flow control
TCP receiver "advertises" free buffer space by including rwnd value in TCP header of receiver-to-sender segments
  RcvBuffer size set via socket options (typical default is 4096 bytes)
  many operating systems autoadjust RcvBuffer
sender limits amount of unACKed ("in-flight") data to receiver's rwnd value
guarantees receive buffer will not overflow
buffered data
free buffer space
rwnd
RcvBuffer
TCP segment payloads
to application process
TCP
receiver-side buffering
3.5 connection-oriented transport: TCP
source port #
dest port #
application
data
(variable length)
sequence number
acknowledgement number
receive window
Urg data pointer
checksum
F
S
R
P
A
U
head
len
not
used
options (variable length)
ECE
CWR
Notes: Here’s how TCP implement flow control. The basic idea is simple – the receiver informs the sender how much free buffer space there is, and the sender is limited to send no more than this amount of data. That the value of RWND in the diagram to the right.
This information is carried from the receiver to the sender in the “receiver advertised window” (do a PIP of header) in the TCP header, and the value will change as the amount of free buffer space fluctuates over time.

## Slide 92
3.1 transport-layer services
3.2 multiplexing and demultiplexing
3.3 connectionless transport: UDP
3.4 principles of reliable data transfer
3.5 connection-oriented transport: TCP
    segment structure
    reliable data transfer
    flow control
    connection management
3.6 principles of congestion control
3.7 TCP congestion control
Transport Layer
Chapter 3 Transport Layer

## Slide 93: TCP Connection Management
before exchanging data, sender/receiver "handshake":
agree to establish connection (each knowing the other willing to establish connection)
agree on connection parameters (e.g., starting seq #s)
connection state: ESTAB
connection variables:
  seq # client-to-server
  server-to-client
  rcvBuffer size
  at server, client
application
network
connection state: ESTAB
connection variables:
  seq # client-to-server
  server-to-client
  rcvBuffer size
  at server, client
application
network
Socket clientSocket =
newSocket("hostname","port number");
Socket connectionSocket = welcomeSocket.accept();
3.5 connection-oriented transport: TCP
Notes: The other TCP topic we’ll want to consider here is that of “connection management”
The TCP sender and receiver have a number of pieces of shared state that they must establish before actually communication
FIRST they must both agree that they WANT to communicate with each other
Secondly there are connection parameters – the initial sequence number and the initial receiver-advertised buffer space that they’ll want to agree on
This is done via a so-called handshake protocol – the client reaching out to the server, and the server answering back.
And before diving into the TCP handshake protocol, let’s first consider the problem of handshaking, of establishing shared state.

## Slide 94: Agreeing to establish a connection
Q: will 2-way handshake always work in network?
variable delays
retransmitted messages (e.g. req_conn(x)) due to message loss
message reordering
can't "see" other side
2-way handshake:
Let's talk
OK
ESTAB
ESTAB
choose x
req_conn(x)
ESTAB
ESTAB
acc_conn(x)
3.5 connection-oriented transport: TCP
Notes: Here’s an example of a two way handshake. Alice reaches out to Bob and say’s “let’s talk” and Bob says OK, and they start their conversation
For a network protocol, the equivalent protocol would be a client sending a “request connection” message saying ”let’s talk, the initial sequence number is x”
And the server would respond with a message ”I accept your connect x”
And the question we want to ask ourselves is <talk through>
Will this work? Let’s look at a few scenarios…

## Slide 95: 2-way handshake scenarios
Q: will 2-way handshake always work in network?
variable delays
retransmitted messages (e.g. req_conn(x)) due to message loss
message reordering
can't "see" other side
3.5 connection-oriented transport: TCP
connection
x completes
choose x
req_conn(x)
ESTAB
ESTAB
acc_conn(x)
data(x+1)
accept
data(x+1)
ACK(x+1)
No problem!

## Slide 96: 2-way handshake scenarios
failure scenarios:
retransmit
req_conn(x)
ESTAB
req_conn(x)
Problem: half open connection!
(no client!)
client terminates
server
forgets x
connection
x completes
retransmit
req_conn(x)
ESTAB
req_conn(x)
data(x+1)
retransmit
data(x+1)
accept
data(x+1)
Problem: dup data accepted!
choose x
req_conn(x)
ESTAB
ESTAB
acc_conn(x)
client terminates
ESTAB
choose x
req_conn(x)
ESTAB
acc_conn(x)
data(x+1)
accept
data(x+1)
connection
x completes
server
forgets x
3.5 connection-oriented transport: TCP
practical technique: login thread

## Slide 97: TCP 3-way handshake
SYNbit=1, Seq=x
choose init seq num, x
send TCP SYN msg
ESTAB
SYNbit=1, Seq=y
ACKbit=1; ACKnum=x+1
choose init seq num, y
send TCP SYNACK
msg, acking SYN
ACKbit=1, ACKnum=y+1
received SYNACK(x)
indicates server is live;
send ACK for SYNACK;
this segment may contain
client-to-server data
received ACK(y)
indicates client is live
SYN SENT
ESTAB
SYN RCVD
client state
LISTEN
server state
LISTEN
3.5 connection-oriented transport: TCP
Notes: TCP’s three way handshake, that operates as follows
Let’s say the client and server both create a TCP socket as we learned about in Chapter 2 and enter the LISTEN state
The client then connects to the server sending a SYN message with a sequence number x (SYN Message is an TCP Segment with SYN but set in the header – you might want to go back and review the TCP segment format!)
The server is waiting for a connection, and receives the SYN message enters the SYN received state (NOT the established state and sends a SYN ACK message back.
Finally the client sends an ACK message to the server, and when the server receiver this enters the ESTABLished state. This is when the application process would see the return from the wait on the socket accept() call

## Slide 98: TCP: closing a connection
client, server each close their side of connection
  send TCP segment with FIN bit = 1
respond to received FIN with ACK
  on receiving FIN, ACK can be combined with own FIN
simultaneous FIN exchanges can be handled
3.5 connection-oriented transport: TCP
Connection Teardown
2 x 2-way handshake
A
B
Fin
FinAck
Fin
FinAck
two pairs of two-way handshakes
Notes: All good things must come to an end, and that’s true for a TCP connection as well.
And of course there’s a protocol for one side to gracefully close of a TCP connection using a FIN message, to which the other side sends a FINACK message and waits around a bit to respond to any retransmitted FIN messages before timing out.

## Slide 99: Homework Week 8
Problems of Chapter 3:
P26
P27
Lab: https://www.github.com/network-whu/lab/
  5.Wireshark_UDP.docx
  Hand-in: add to your lab report, in a separate chapter
Transport Layer

## Slide 100
3.1 transport-layer services
3.2 multiplexing and demultiplexing
3.3 connectionless transport: UDP
3.4 principles of reliable data transfer
3.5 connection-oriented transport: TCP
3.6 principles of congestion control
3.7 TCP congestion control
3.8 Evolution of Transport-Layer Functionality
Chapter 3 Transport Layer
Transport Layer

## Slide 101: Principles of congestion control
congestion:
informally: "too many sources sending too much data too fast for network to handle"
manifestations:
  packet loss (buffer overflow at routers)
  long delays (queueing in router buffers)
different from flow control!
a top-10 problem!
3.6 principles of congestion control
congestion control: too many senders, sending too fast
flow control: one sender too fast for one receiver
Notes: manifestation – 表现形式
Throughput measures the rate at which messages and data arrive at their destination
Goodput, only measures the throughput of the original data.

## Slide 102: Causes/costs of congestion: scenario 1
3.6 principles of congestion control
Simplest scenario:
maximum per-connection throughput: R/2
Host A
Host B
throughput: lout
large delays as arrival rate lin approaches capacity R/2
Q: What happens as arrival rate lin approaches R/2?
original data: lin
R
two flows
one router, infinite buffers
input, output link capacity: R
infinite shared output link buffers
R
no retransmissions needed
R/2
delay
lin
R/2
R/2
lout
lin
throughput:

## Slide 103: Causes/costs of congestion: scenario 2
one router, finite buffers
sender retransmission of timed-out packet
  application-layer input = application-layer output: lin = lout
  transport-layer input includes retransmissions : l′in ≧ lin
finite shared output link buffers
Host A
lin : original data
Host B
lout
l'in: original data, plus retransmitted data
3.6 principles of congestion control

## Slide 104: Causes/costs of congestion: scenario 2
idealization: perfect knowledge
sender sends only when router buffers available
R/2
R/2
lout
lin
3.6 principles of congestion control
finite shared output link buffers
lin : original data
lout
l'in: original data, plus retransmitted data
copy
free buffer space!
Host B
Host A

## Slide 105: Causes/costs of congestion: scenario 2
Idealization: some perfect knowledge
packets can be lost (dropped at router) due to full buffers
sender knows when packet has been dropped: only resends if packet known to be lost
3.6 principles of congestion control
lin : original data
lout
l'in: original data, plus retransmitted data
copy
no buffer space!
Host B
Host A
when sending at R/2, some packets are needed retransmissions
lin
R/2
lout
throughput:
R/2
“wasted” capacity due to retransmissions

## Slide 106: Causes/costs of congestion: scenario 2
Idealization: some perfect knowledge
packets can be lost (dropped at router) due to full buffers
sender knows when packet has been dropped: only resends if packet known to be lost
3.6 principles of congestion control
lin : original data
lout
l'in: original data, plus retransmitted data
free buffer space!
Host B
Host A
R/2
R/2
l'in
lout
when sending at R/2, some packets are retransmissions but asymptotic goodput is still R/2 (why?)
Notes: goodput: effective throughput

## Slide 107: Causes/costs of congestion: scenario 2
3.6 principles of congestion control
lin
l'in
copy
free buffer space!
timeout
Host B
Realistic scenario: un-needed duplicates
packets can be lost, dropped at router due to full buffers – requiring retransmissions
but sender times can time out prematurely, sending two copies, both of which are delivered
Host A
when sending at R/2, some packets are retransmissions, including needed and un-needed duplicates, that are delivered!
“wasted” capacity due to un-needed retransmissions
lin
R/2
lout
throughput:
R/2

## Slide 108: Causes/costs of congestion: scenario 2
"costs" of congestion:
more work (retrans) for given "goodput"
unneeded retransmissions: link carries multiple copies of pkt
  decreasing goodput
3.6 principles of congestion control
Realistic scenario: un-needed duplicates
packets can be lost, dropped at router due to full buffers – requiring retransmissions
but sender times can time out prematurely, sending two copies, both of which are delivered
when sending at R/2, some packets are retransmissions, including needed and un-needed duplicates, that are delivered!
“wasted” capacity due to un-needed retransmissions
lin
R/2
lout
throughput:
R/2
Notes: goodput: 有效吞吐量, achievable throughput

## Slide 109: Causes/costs of congestion: scenario 3
four senders
multi-hop paths
timeout/retransmit
Q: what happens as and increase ?
finite shared output link buffers
Host A
lout
Host B
Host C
Host D
lin : original data
l'in: original data, plus retransmitted data
A: as red increases, all arriving blue pkts at upper queue are dropped, blue throughput g 0
3.6 principles of congestion control
R3
R1
R2
R4

## Slide 110: Causes/costs of congestion: scenario 3
another "cost" of congestion:
when packet dropped, any "upstream" transmission capacity used for that packet was wasted!
C/2
C/2
lout
3.6 principles of congestion control
Notes: upstream: 上游

## Slide 111: Causes/costs of congestion: insights
upstream transmission capacity / buffering wasted for packets lost downstream
delay increases as capacity approached
un-needed duplicates further decreases effective throughput
loss/retransmission decreases effective throughput
throughput can never exceed capacity

## Slide 112: Approaches towards congestion control
End-end congestion control:
no explicit feedback from network
congestion inferred from observed loss, delay
data
data
ACKs
ACKs
approach taken by TCP

## Slide 113: Approaches towards congestion control
TCP ECN, ATM, DECbit protocols
data
data
ACKs
ACKs
explicit congestion info
Network-assisted congestion control:
routers provide direct feedback to sending/receiving hosts with flows passing through congested router
may indicate congestion level or explicitly set sending rate
Notes: Explicit Congestion Notification

## Slide 114
3.1 transport-layer services
3.2 multiplexing and demultiplexing
3.3 connectionless transport: UDP
3.4 principles of reliable data transfer
3.5 connection-oriented transport: TCP
3.6 principles of congestion control
3.7 TCP congestion control
3.8 Evolution of Transport-Layer Functionality
Chapter 3 Transport Layer
Transport Layer

## Slide 115: TCP congestion control: additive increase multiplicative decrease
approach: sender increases transmission rate (window size, cwnd), probing for usable bandwidth, until loss occurs, then decrease sending rate on loss event
  Additive Increase: increase cwnd by 1 MSS every RTT until loss detected
  Multiplicative Decrease: cut cwnd in half after loss
cwnd: TCP sender
congestion window size
AIMD saw tooth
behavior: probing
for bandwidth
additively increase window size …
…. until loss occurs (then cut window in half)
time
3.7 TCP congestion control
AIMD
Maximum Segment Size
"AIMD"
also known as "congestion avoidance"

## Slide 116: TCP Congestion Control: details
sender limits transmission:
cwnd is dynamically adjusted in response to observed network congestion (implementing TCP congestion control)
TCP sending rate:
roughly: send cwnd bytes, wait RTT for ACKS, then send more bytes
last byte
ACKed
sent, not-yet ACKed
("in-flight")
cwnd
last byte sent
sender sequence number space
bytes/sec
3.7 TCP congestion control
available but not used

## Slide 117: TCP Slow Start
when connection begins, increase rate exponentially until first loss event:
  initially cwnd = 1 MSS
  double cwnd every RTT
  done by incrementing cwnd for every ACK received
summary: initial rate is slow but ramps up exponentially fast
Host A
one segment
Host B
RTT
time
two segments
four segments
3.7 TCP congestion control

## Slide 118: TCP: detecting, reacting to loss
loss indicated by timeout:
  cwnd set to 1 MSS;
  window then grows exponentially (as in slow start) to threshold, then grows linearly
loss indicated by 3 duplicate ACKs: TCP RENO
  dup ACKs indicate network capable of delivering some segments
  cwnd is cut in half window then grows linearly
TCP Tahoe always sets cwnd to 1 (timeout or 3 duplicate acks)
3.7 TCP congestion control
Notes: 慢启动
拥塞避免模式
快恢复

## Slide 119: TCP: from slow start to congestion avoidance
Q: when should the exponential increase switch to linear?
A: when cwnd gets to 1/2 of its value before timeout.
3.7 TCP congestion control
Implementation:
variable ssthresh
on loss event, ssthresh is set to 1/2 of cwnd just before loss event
X

## Slide 120: Summary: TCP Congestion Control
timeout
ssthresh = cwnd/2
cwnd = 1 MSS
dupACKcount = 0
retransmit missing segment
L
cwnd > ssthresh
congestion
avoidance
cwnd = cwnd + MSS (MSS/cwnd)
dupACKcount = 0
transmit new segment(s), as allowed
.
new ACK
dupACKcount++
duplicate ACK
fast
recovery
cwnd = cwnd + MSS
transmit new segment(s), as allowed
duplicate ACK
ssthresh= cwnd/2
cwnd = ssthresh + 3
retransmit missing segment
dupACKcount == 3
timeout
ssthresh = cwnd/2
cwnd = 1
dupACKcount = 0
retransmit missing segment
ssthresh= cwnd/2
cwnd = ssthresh + 3
retransmit missing segment
dupACKcount == 3
cwnd = ssthresh
dupACKcount = 0
New ACK
slow
start
timeout
ssthresh = cwnd/2
cwnd = 1 MSS
dupACKcount = 0
retransmit missing segment
cwnd = cwnd+MSS
dupACKcount = 0
transmit new segment(s), as allowed
new ACK
dupACKcount++
duplicate ACK
L
cwnd = 1 MSS
ssthresh = 64 KB
dupACKcount = 0
New
ACK!
New
ACK!
New
ACK!
3.7 TCP congestion control

## Slide 121: TCP throughput
avg. TCP thruput as function of window size, RTT?
  ignore slow start, assume always data to send
W: window size (measured in bytes) where loss occurs
  avg. window size (# in-flight bytes) is ¾ W
  avg. thruput is 3/4W per RTT
W
W/2
avg TCP thruput =
3
4
W
RTT
bytes/sec
3.7 TCP congestion control

## Slide 122: TCP CUBIC
Is there a better way than AIMD to “probe” for usable bandwidth?
Insight/intuition:
  Wmax: sending rate at which congestion loss was detected
  congestion state of bottleneck link probably (?) hasn’t changed much
  after cutting rate/window in half on loss, initially ramp to to Wmax faster, but then approach Wmax more slowly
3.7 TCP congestion control
Wmax
Wmax/2
classic TCP
TCP CUBIC - higher throughput in this example
Notes: TCP Congestion Control Algorithms Comparison
TCP congestion control and avoidance algorithms (CCAs) are an important connection tuning consideration, especially with high bandwidth/high latency broadband networks. Below is a list of the most commonly used algorithms that all aim to improve the traditional TCP congestion control algorithm as defined in RFC 2581. The algorithms have continued to evolve over the years, and are listed in below in loose chronological order, with their advantages and shortcomings. Current recommendations are in the last section of the article.
There are generally three types of CCAs based on how they detect network congestion to control the congestion window (cwnd) buffer:
loss-based - algorithms respond to packet loss to determine congestion and change the buffer. Most CCAs use this metric, including TCP Reno, New-Reno and CUBIC.
delay-based - algorithms like TCP Vegas that use variations of latency (RTT) to determine congestion and change the buffer size.
model-based - modern algorithms like BBR use combination of factors to determine congestion, they are both rate-based and delay-based, introduce packet pacing, etc. BBRv2 also uses packet loss for the model, BBRv1 does not.
TCP Reno (1986)
Traditional TCP congestion control used by older OSes. Reno uses slow start, congestion avoidance, and fast retransmit triggered by triple duplicate ACKs. Reno uses packet loss to detect network congestion. It cannot distinguish between random errors and congestion loss, so it can overreact to random packet loss. Similar to TCP Tahoe algorithm of the same era.
TCP Vegas (1994)
Emphasizes packet delay, rather than packet loss, as a signal to determine the rate at which to send packets. Unlike TCP-Reno which detects congestion only after it has happened via packet drops, TCP-Vegas detects congestion based on increasing RTT values of the packets in the connection, detecting congestion in the network before packet loss occurs.
TCP Vegas tends to limit throughput with very small RTT values, and overruns the connection in large RTT values. TCP Vegas does not co-exist well with other congestion control algorithms because it is the fastest to detect congestion and throttle the connection, before other algorithms that use packet loss as the main indication.
TCP New-Reno (1999)
[RFC 6582], obsoletes [RFC 3782]
New-Reno improves retransmissions compared to TCP Reno during fast recovery. New-Reno is able to detect multiple lost packets. The only problem with this algorithm mistakes some TCP reordering by more than 3 sequence numbers.
SACK (Selective Acknowledgements) is an extension to TCP Reno and New-Reno that helps with detection of multiple lost packets, and retransmission of more than one lost packet per RTT. SACK TCP acknowledges segments selectively, rather than cumulatively.
TCP Westwood (TCPW, 2001)
Westwood is a modification of TCP Reno optimized for lossy networks. It works well with wireless networks, the improvement is most significant in wireless networks with lossy links. TCPW is also not very sensitive to random packet loss, while TCP Reno is equally sensitive to random loss and congestion loss and cannot discriminate between them.
The key innovative idea in TCP Westwood is to measure the bandwidth used by the connection via monitoring the rate of returning ACKs at the sender side. This allows for faster recovery of the connection than TCP Reno. The TCP Westwood mechanism is particularly effective over wireless links where sporadic losses due to radio channel problems are often misinterpreted as a symptom of congestion by other congestion algorithms and thus lead to an unnecessary TCP window reduction.
TCP BIC (2004)
The Binary Increase Congestion (BIC) control is optimized congestion control algorithm for high speed/high latency networks. BIC has a unique congestion window algorithm which uses a binary search algorithm in an attempt to find the largest congestion window that will last the maximum amount of time. BIC was used by default in Linux kernels 2.6.8 through 2.6.18, before CUBIC became the default.
TCP CUBIC (2007)
CUBIC is one of the most popular congestion control/avoidance algorithms currently in use. It is used by default in Linux kernels after 2.6.19, it is also the default in later Windows 10 builds, and Windows Server 2019.
CUBIC is a less aggressive and more systematic derivative of BIC, in which the window is a cubic function of time since the last packet loss. There are two components to TCP window growth. In the first part the window ramps up quickly to the size as it was before the packet loss occurred. After the first part, there is a delay allowing enough time for the network to stabilize. After this delay, the second part of CUBIC probes for more bandwidth, slowly at first then very rapidly.
CTCP (Compound TCP, 2006)
CTCP is a Microsoft algorithm that was introduced as part of the Windows Vista and Window Server 2008 TCP stack. It is designed to aggressively adjust the sender's congestion window to optimize TCP for connections with large bandwidth-delay products and large receive window sizes. CTCP attempts to maximize throughput on these types of connections by monitoring delay variations and packet loss. CTCP also ensures that its behavior does not negatively impact other TCP connections. It is also available for some Linux kernels as a patch, for Windows XP and Windows Server 2003 via a hotfix.
Notes: CTCP was the default congestion control protocol for Windows 8/10, 2008 Server. This default has changed to CUBIC in more recent builds of Windows 10 and Windows 2019 Server.
CTCP may perform slightly better than CUBIC with VoIP, and possibly gaming in combination with ECN. CUBIC performs a bit better for pure throughput when there is no excessive network congestion.
TCP LEDBAT (2010)
RFC 6817
Low Extra Delay Background Transport (LEDBAT) is an algorithm that uses changes in one-way delay measurements to limit congestion. It is designed to for use by background bulk-transfer applications to be less aggressive than competing flows, limiting interference with the network performance of competing data streams. It is a way to transfer data in the background quickly, consuming unused bandwidth without clogging the network and without interfering with other TCP connections.
TCP BBR (2016)
Bottleneck Bandwidth and Round-trip propagation time (BBR) is a modern congestion control and avoidance algorithm. It was initially developed at Google in 2016, and a second version with some changes was introduced in 2020. It is available in Linux since kernel 4.9 and the default algorithm used by YouTube and Google cloud. While most algorithms above are loss-based (they rely on packet loss to detect congestion and lower transmission rates), BBR is model-based, using the maximum bandwidth and round-trip time to build a model of the capability of the network based on BDP (bandwidth-delay product). The BBR model is rate-based and delay-based. It is vaguely similar to TCP-Vegas in its partial reliance on latency to detect congestion, without the downsides. BBR limits its number of packets in flight to be a multiple of the bandwidth-delay product (BDP) and also uses pacing to control the inter-packet spacing.
The BBR model of calculating the congestion window: Max measured bandwidth (BW) x minimum latency (RTT) = BDP x 2 = congestion window (CWND, amount of data in the network)
Note: The algorithm uses the maximum measured bandwidth over last 8 RTTs for the calculation. It also adds pacing to the above, and tries to increase its sending rate by 25% for next 6 RTTs. The amount of data in flight is limited to 2 times BDP, which also dictates BBR's fraction of the bandwidth under competition with other algorithms in the same network. In essence, under competition it is not only rate-limited, it is also window-limited.
BBR is efficient and fast, however there were some issues with version 1 of the algorithm. There were some questions raised about BBR's fairness to non-BBR streams. There is potentially some "unfairness" between BBR v1 and CUBIC, reportedly dependent on the bottleneck TCP window buffer size (BBR v1 obtains more of the total bandwidth with smaller buffers, CUBIC gets bigger percentage with very large buffers and gigabit transfers). BBR v1 also causes more packet retransmissions compared to CUBIC, as it ignores packet loss. This is only apparent in the presence of packet loss.
Google has released BBR v2 in 2020 which uses both packet loss and ECN to help identify network congestion and achieve better fairness and fewer packet retransmissions than BBR v1. Below is a list of key differences between the two versions.
BBR v1: low throughput for CUBIC/Reno flows sharing some paths, does not use packet loss, does not use ECN
BBR v2: better coexistence with Reno/CUBIC, uses packet loss as a signal, uses ECN if available
C2TCP (2018)
Cellular Controlled Delay TCP (C2TCP) targets interactive applications requiring low latency in high-speed cellular networks. It is inspired by in-network active queue management (AQM) designs to adapt itself to different applications QoS requirements without modifying any client network devices. C2TCP is designed to work as an add-on to existing TCP (e.g. New Reno, CUBIC, BIC, etc.), it only needs to be installed on the server-side, and improves the average delay of packets to be bound to the QoS requirements for different applications. C2TCP aims to satisfy applications such as virtual reality, video conferencing, gaming, vehicular communication systems, etc. in a highly dynamic environment such as LTE and future 5G cellular networks. It can outperform BBR, Cubic and other TCP variants in achieving lower average delay and jitter.
Other TCP congestion control/avoidance algorithms
Below is a list of many other, less common and special use CCA algorithms not covered above, mostly targeted at improving performance of networks with large bandwidth-delay product.
DCTCP (Data Center TCP, 2011): RFC 8257. Intended for data-center traffic extending ECN processing
FAST TCP: especially targeted at long-distance, high latency links
HSTCP (HighSpeed TCP): RFC 3649
H-TCP (Hamilton TCP): targeted at high-speed high-latency networks, developed at the Hamilton Institute in Ireland
Copa: delay-sensitive algorithm that uses a Markovian packet arrival model, used by Facebook for live video uploads
ProPrate: aimed at cellular networks, rate-based algorithm to balance between delay and throughput
Scalable TCP: simple change to traditional TCP CCA to increase congestion window faster
TCP-Jersey: aimed at wireless networks, able to distinguish between wireless packet loss and congestion loss
TCP Hybla (2004): aimed to improve wireless and satellite links, Emory University paper
TCP-Illinois: targeted at high-speed long-distance networks, developed by University of Illinois
TCP Veno: enhancement of transmission over wireless networks
YeAH-TCP (Yet Another Highspeed TCP, 2007): delay-aware/state-enabled to keep a pipe at, or below a threshold.
Conclusion (TL;DR;)
CUBIC is the recommended, and currently most popular congestion control/avoidance algorithm, it is the default in Linux since kernel 2.6.19. CTCP is ok to use with Windows. BBR is a great new algorithm that is gaining popularity, it is available in Linux since kernel 4.9, not yet available with Windows. While BBR version 1 had some quirks, if your OS supports BBR version 2 it is likely even better than CUBIC. Westwood can be tried with lossy wireless networks.

## Slide 123: TCP CUBIC
K: point in time when TCP window size will reach Wmax
  K itself is tunable
increase W as a function of the cube of the distance between current time and K
  larger increases when further away from K
  smaller increases (cautious) when nearer K
3.7 TCP congestion control
TCP BBR available in Linux since kernel 4.9, most popular TCP for popular Web servers
  BBR v2: better coexistence with Reno/CUBIC, uses packet loss as a signal, uses ECN if available
TCP
sending
rate
time
TCP Reno
TCP CUBIC
Wmax
t0
t1
t2
t3
t4
https://djangocas.dev/blog/huge-improve-network-performance-by-change-tcp-congestion-control-to-bbr/
https://blog.rvich.com/2023/03/how-to-enable-tcp-bbr2-network.html
Notes: https://witestlab.poly.edu/blog/tcp-bbr-for-ultra-low-latency-networking-challenges-analysis-and-solutions/
https://djangocas.dev/blog/huge-improve-network-performance-by-change-tcp-congestion-control-to-bbr/
https://www.geeksforgeeks.org/how-to-boost-linux-server-internet-speed-with-tcp-bbr/
https://www.ietf.org/proceedings/106/slides/slides-106-iccrg-update-on-bbrv2-00
https://zhuanlan.zhihu.com/p/366392032
原理
很简单，就是例如你浏览qq.com，就需要首选发syn包，这个加速器帮你多发一个包，万一第一个包掉了就可以第二个包达到，就是这个意思。
同理服务器windows也是可以装的，就是游客访问你网站，你返回的小包都是返回给你的游客2次。游客syn你的web端口 你返回2次 相同的syn=1，ack=1应答他一个syn，只要一个达到你游客哪里即可。。。就是说如果网络绝对是非常优质不掉包的话，第二个发送就是多余的。所以对于流出带宽用不完的所有windows 64位系统都装上有好处。
大包不敢多次在还未确定网络掉包的情况下就发送多个copy。。。太浪费带宽了。。。
如有有非常变态的掉包环境，那就所有包都重发n次直到带宽占用满90%，这样的设计最好。。

## Slide 124: TCP CTCP and LEDBAT
3.7 TCP congestion control
chcp 437
netsh interface tcp show global
The output of this command should resemble the following:
Querying active state...
TCP Global Parameters
-----
Receive-Side Scaling State : enabled
Receive Window Auto-Tuning Level : normal
Add-On Congestion Control Provider : default
ECN Capability : disabled
RFC 1323 Timestamps : disabled
Initial RTO : 1000
Receive Segment Coalescing State : enabled
Non Sack Rtt Resiliency : disabled
Max SYN Retransmissions : 4
Fast Open : enabled
Fast Open Fallback : enabled
Pacing Profile : off
Notes: https://www.speedguide.net/articles/windows-8-10-2012-server-tcpip-tweaks-5077
https://techcommunity.microsoft.com/t5/networking-blog/windows-transport-converges-on-two-congestion-providers-cubic/ba-p/339819
https://docs.microsoft.com/en-us/powershell/module/nettcpip/set-nettcpsetting?view=windowsserver2022-ps

## Slide 125: TCP CTCP and LEDBAT
3.7 TCP congestion control
chcp 437
netsh interface tcp show supplemental
The output of this command should resemble the following:
The TCP global default template is internet
TCP Supplemental Parameters
----------------------------------------------
Minimum RTO (msec) : 300
Initial Congestion Window (MSS) : 10
Congestion Control Provider : cubic
Enable Congestion Window Restart : disabled
Delayed ACK timeout (msec) : 40
Delayed ACK frequency : 2
Enable RACK : enabled
Enable Tail Loss Probe : enabled
Notes: netsh int tcp set supplemental Internet congestionprovider=ctcp

## Slide 126: TCP CTCP and LEDBAT
3.7 TCP congestion control
chcp 437
netsh int tcp set supplemental Internet congestionprovider=ctcp
netsh interface tcp show supplemental
The output of this command should resemble the following:
Ok.
The TCP global default template is internet
TCP Supplemental Parameters
----------------------------------------------
Minimum RTO (msec) : 300
Initial Congestion Window (MSS) : 10
Congestion Control Provider : ctcp
Enable Congestion Window Restart : disabled
Delayed ACK timeout (msec) : 40
Delayed ACK frequency : 2
Enable RACK : enabled
Enable Tail Loss Probe : enabled

## Slide 127: TCP Futures: TCP over "long, fat pipes"
example: 1500 byte segments, 100ms RTT, want 10 Gbps throughput
requires W = 83,333 in-flight segments
throughput in terms of segment loss probability, L [Mathis 1997]:
  ➜ to achieve 10 Gbps throughput, need a loss rate of L = 2·10-10 – a very small loss rate!
new versions of TCP for high-speed
TCP throughput =
1.22
.
MSS
RTT
L
3.7 TCP congestion control

## Slide 128: TCP and the congested “bottleneck link”
TCP (classic, CUBIC) increase TCP’s sending rate until packet loss occurs at some router’s output: the bottleneck link
source
application
TCP
network
link
physical
destination
application
TCP
network
link
physical
bottleneck
link is always busy
packet queue almost never empty, sometimes overflows packet (loss)
3.7 TCP congestion control

## Slide 129: TCP and the congested “bottleneck link”
TCP (classic, CUBIC) increase TCP’s sending rate until packet loss occurs at some router’s output: the TCP bottleneck link
source
application
TCP
network
link
physical
destination
application
TCP
network
link
physical
understanding congestion: useful to focus on congested bottleneck link
insight: increasing TCP sending rate will not increase end-end throughout with congested bottleneck
insight: increasing TCP sending rate will increase measured RTT
RTT
Goal: “keep the end-end pipe just full, but not fuller”
3.7 TCP congestion control

## Slide 130: Delay-based TCP Congestion Control
Keeping sender-to-receiver pipe “just full enough, but no fuller”: keep bottleneck link busy transmitting, but avoid high delays/buffering
RTTmeasured
Delay-based approach:
RTTmin - minimum observed RTT (uncongested path)
ideal throughput with congestion window cwnd is cwnd/RTTmin
if measured throughput “very close” to ideal throughput
increase cwnd linearly /* since path not congested */
else if measured throughput “far below” ideal throughout
decrease cwnd linearly /* since path is congested */
RTTmeasured
measured
throughput
=
# bytes sent in last RTT interval
3.7 TCP congestion control
or with different pacing rate！

## Slide 131: Delay-based TCP Congestion Control
congestion control without inducing/forcing loss
maximizing throughout ("keeping the just pipe full…") while keeping delay low ("…but not fuller")
a number of deployed TCPs take a delay-based approach
  BBR deployed on Google’s (internal) backbone network
3.7 TCP congestion control
Bottleneck Bandwidth and RTT
https://github.com/google/bbr

## Slide 132: Explicit Congestion Notification (ECN)
source
application
TCP
network
link
physical
destination
application
TCP
network
link
physical
TCP deployments often implement network-assisted congestion control:
two bits in IP header (ToS field) marked by network router to indicate congestion
  policy to determine marking chosen by network operator
congestion indication carried to receiving host
  destination (seeing congestion indication in IP datagram) ) sets ECE bit on receiver-to-sender ACK segment to notify sender of congestion
ECN=00
ECN=11
ECE=1
IP datagram
TCP ACK segment
3.7 TCP congestion control
HLEN
4
RSVD
4
URG
ACK
PSH
RST
SYN
FIN
Flag field
CWR & ECE:
Explicit congestion
Notification (3.7.2)
CWR
ECE
Notes: involves both IP (IP header ECN bit marking) and TCP (TCP header C,E bit marking)

## Slide 133: TCP Fairness
fairness goal: if K TCP sessions share same bottleneck link of bandwidth R, each should have average rate of R/K
TCP connection 1
bottleneck
router
capacity R
TCP connection 2
3.7 TCP congestion control

## Slide 134: Q: Is TCP fair?
Example: two competing sessions:
additive increase gives slope of 1, as throughput increases
multiplicative decrease decreases throughput proportionally
R
R
fairness line (equal bandwidth share)
Connection 1 throughput
Connection 2 throughput
congestion avoidance: additive increase
loss: decrease window by factor of 2
congestion avoidance: additive increase
loss: decrease window by factor of 2
3.7 TCP congestion control
A: Yes, under idealized assumptions:
same RTT
fixed number of sessions only in congestion avoidance
Is TCP fair?
efficiency line

## Slide 135: Fairness: must all network apps be “fair”?
Fairness and UDP
multimedia apps often do not use TCP
  do not want rate throttled by congestion control
instead use UDP:
  send audio/video at constant rate, tolerate packet loss
there is no “Internet police” policing use of congestion control
Fairness, parallel TCP connections
application can open multiple parallel connections between two hosts
web browsers do this
e.g., link of rate R with 9 existing connections:
  new app asks for 1 TCP, gets rate R/10
  new app asks for 11 TCPs, gets R/2
3.7 TCP congestion control

## Slide 136: QUIC: Quick UDP Internet Connections
application-layer protocol, on top of UDP
  to increase performance of HTTP
  deployed on many Google servers, apps (Chrome, mobile YouTube app)
adopts approaches we’ve studied in this chapter for connection establishment, error control, congestion control
  connection establishment handshake: performs authentication, encryption key management while establishing error/congestion control state, avoiding RTT delays
  error and congestion control: “Readers familiar with TCP’s loss detection and congestion control will find algorithms here that parallel well-known TCP ones.” [from QUIC specification]
3.7 TCP congestion control

## Slide 137: QUIC: Quick UDP Internet Connections
multiple application-level “streams” multiplexed in parallel over single QUIC connection
  e.g. each stream could be an HTTP object from Web server to client (recall HTTP and TCP/HOL blocking)
IP
TCP
TLS
HTTP/2
IP
UDP
QUIC
HTTP/2 (slimmed)
Network
Transport
Application
HTTP/2 over TCP
HTTP/3
HTTP/3 over QUIC over UDP
3.7 TCP congestion control
HOL
Notes: TLS: Transportation Layer Security
head of line blocking: including HTTP head of line blocking and TCP head of line blocking

## Slide 138: QUIC: Streams: parallelism, no HOL blocking
(a) HTTP 1.1
TLS encryption
TCP RDT
TCP Cong. Contr.
transport
application
(b) HTTP/2 with QUIC: no HOL blocking
TCP RDT
TCP Cong. Contr.
TLS encryption
error!
HTTP
GET
HTTP
GET
HTTP
GET
QUIC Cong. Cont.
QUIC
encrypt
QUIC
RDT
QUIC
RDT
QUIC
RDT
QUIC
encrypt
QUIC
encrypt
UDP
UDP
QUIC Cong. Cont.
QUIC
encrypt
QUIC
RDT
QUIC
RDT
QUIC
RDT
QUIC
encrypt
QUIC
encrypt
error!
HTTP
GET
HTTP
GET
HTTP
GET
3.7 TCP congestion control

## Slide 139
3.1 transport-layer services
3.2 multiplexing and demultiplexing
3.3 connectionless transport: UDP
3.4 principles of reliable data transfer
3.5 connection-oriented transport: TCP
3.6 principles of congestion control
3.7 TCP congestion control
3.8 Evolution of Transport-Layer Functionality
Chapter 3 Transport Layer
Transport Layer

## Slide 140: Chapter 3: summary
principles behind transport layer services:
  multiplexing, demultiplexing
  reliable data transfer
  flow control
  congestion control
instantiation, implementation in the Internet
  UDP
  TCP
next:
leaving the network "edge" (application, transport layers)
into the network "core"
two network layer chapters:
  data plane
  control plane
Transport Layer

## Slide 141: Homework this week
Problems of Chapter 3:
P40
P44
Lab: https://www.github.com/network-whu/lab/
  6.Wireshark_TCP.docx
  Hand-in: add to your lab report, in a separate chapter
Transport Layer