## Slide 1: Chapter 5 Network Layer: The Control Plane
Slides are adapted from those of by J.F Kurose and K.W. Ross with copyright 1996-2020 J.F Kurose and K.W. Ross, All Rights Reserved

## Slide 2: Network Layer Control Plane: our goals
understand principles behind network control plane:
  traditional routing algorithms
  SDN controllers
  Internet Control Message Protocol
  network management
and their instantiation, implementation in the Internet
  OSPF, BGP, OpenFlow, ODL and ONOS controllers, ICMP, SNMP
network layer
global approaches

## Slide 3
5.1 Introduction
5.2 Routing algorithms
5.3 Intra-AS routing in the Internet: OSPF
5.4 Routing among the ISPs: BGP
5.5 The SDN control plane
5.6 ICMP: The Internet Control Message Protocol
5.7 Network management and SNMP, NETCONF/YANG
5.1 Introduction
Chapter 5 The Network Layer
: Control Plane
Network Layer - the control plane

## Slide 4: Network-layer functions
forwarding: move packets from router's input to appropriate router output
data plane
control plane
Two approaches to structuring network control plane:
per-router control (traditional)
logically centralized control (software defined networking)
Recall: two network-layer functions:
routing: determine route taken by packets from source to destination
5.1 introduction
end to end
hop by hop

## Slide 5
Per-router control plane
Routing
Algorithm
Individual routing algorithm components in each and every router interact with each other in control plane to compute forwarding tables
data
plane
control
plane
5.1 introduction
Local forwarding table
header output
0100 3
0110 2
0111 2
1001 1

## Slide 6
data
plane
control
plane
Logically centralized control plane
A distinct (typically remote) controller interacts with local control agents (CAs) in routers to compute forwarding tables
Remote Controller
CA
CA
CA
CA
CA
5.1 introduction
Remote controller computes, installs forwarding tables in routers

## Slide 7
5.1 Introduction
5.2 Routing algorithms
5.3 Intra-AS routing in the Internet: OSPF
5.4 Routing among the ISPs: BGP
5.5 The SDN control plane
5.6 ICMP: The Internet Control Message Protocol
5.7 Network management and SNMP, NETCONF/YANG
5.2 Routing algorithms
Chapter 5 The Network Layer
: Control Plane
Network Layer - the control plane

## Slide 8: Routing protocols
Routing protocol goal: determine "good" paths (equivalently, routes), from sending hosts to receiving host, through network of routers
path: sequence of routers packets will traverse in going from given initial source host to given final destination host
"good": least "cost", "fastest", "least congested"
routing: a "top-10" networking challenge!
5.2 routing protocols

## Slide 9: Graph abstraction of the network
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
graph: G = (N,E)
N = set of routers = { u, v, w, x, y, z }
E = set of links ={ (u,v), (u,x), (v,x), (v,w), (x,w), (x,y), (w,y), (w,z), (y,z) }
aside: graph abstraction is useful in other network contexts, e.g.,
P2P, where N is set of peers and E is set of TCP connections
5.2 routing protocols
A lot of NP-complete problems can be abstracted into a graph searching/splitting problem

## Slide 10: Graph abstraction: costs
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
c(x,x') = cost of link (x,x')
e.g., c(w,z) = 5
cost could always be 1, or
inversely related to bandwidth,
or inversely related to
congestion
cost of path (x1, x2, x3,…, xp) = c(x1,x2) + c(x2,x3) + … + c(xp-1,xp)
key question: what is the least-cost path between u and z ?
routing algorithm: algorithm that finds that least cost path
5.2 routing protocols

## Slide 11: Routing algorithm classification
global: all routers have complete topology, link cost info
"link state" algorithms
static: routes change slowly over time
5.2 routing protocols
dynamic: routes change more quickly
periodic update or in response to link cost changes
decentralized: iterative process of computation, exchange of info with neighbors
router knows physically-connected neighbors, link costs to neighbors
"distance vector" algorithms
global or decentralized information?
How fast do routes change?

## Slide 12
5.1 Introduction
5.2 Routing algorithms
5.2.1 The Link-State (LS) Routing Algorithm
5.2.2 The Distance-Vector (DV) Routing Algorithm
5.3 Intra-AS routing in the Internet: OSPF
5.4 Routing among the ISPs: BGP
5.5 The SDN control plane
5.6 ICMP: The Internet Control Message Protocol
5.7 Network management and SNMP, NETCONF/YANG
Chapter 5 The Network Layer
: Control Plane
Network Layer - the control plane

## Slide 13
5.1 Introduction
5.2 Routing algorithms
5.2.1 The Link-State (LS) Routing Algorithm
5.2.2 The Distance-Vector (DV) Routing Algorithm
5.3 Intra-AS routing in the Internet: OSPF
5.4 Routing among the ISPs: BGP
5.5 The SDN control plane
5.6 ICMP: The Internet Control Message Protocol
5.7 Network management and SNMP, NETCONF/YANG
Chapter 5 The Network Layer
: Control Plane
Network Layer - the control plane

## Slide 14: Dijkstra's link-state routing algorithm
c(x,y): link cost from node x to y; = ∞ if not direct neighbors
D(v): current value of cost of path from source to dest. v
p(v): predecessor node along path from source to v
N': set of nodes whose least cost path definitively known
centralized: net topology, link costs known to all nodes
  accomplished via "link state broadcast"
  all nodes have same info
computes least cost paths from one node ("source") to all other nodes
  gives forwarding table for that node
iterative: after k iterations, know least cost path to k dest.'s
5.2 routing protocols
5.2.1 The Link-State (LS) Routing Algorithm
notation

## Slide 15: Dijkstra's link-state routing algorithm
5.2 routing protocols
5.2.1 The Link-State (LS) Routing Algorithm
1 Initialization:
2 N' = {u} /* compute least cost path from u to all other nodes */
3 for all nodes v
4 if v adjacent to u /* u initially knows direct-path-cost only to direct neighbors */
5 then D(v) = c（u，v) /* but may not be minimum cost!*/
6 else D(v) = ∞
7
8 Loop
9
10
11
12
13
14
15 until all nodes in N'
find w not in N' such that D(w) is a minimum
add w to N'
update D(v) for all v adjacent to w and not in N' :
D(v) = min( D(v), D(w) + c(w,v))
/* new least-path-cost to v is either old least-cost-path to v or known
least-cost-path to w plus direct-cost from w to v */

## Slide 16: Dijsktra's algorithm
5.2 routing protocols
Dijkstra 最短路径算法
  G=(V,E)是一个带权有向图，V分成两组S和T，V=S U T。S为已求出最短路径的顶点集合。初始S中只有一个源点v，以后每求得一条最短路径 , 就将加入S中，直到S=V。从T中找出到v最短路径的点p依次加入S中。在加入的过程中，保持从v到S中各顶点的最短路径长度不大于从v到T的最短路径长度。每个顶点对应一个距离，S中的顶点的距离就是从v到此顶点的最短路径长度，T中顶点t的距离，是从v到t只包括S中的顶点为中间顶点的当前最短路径长度。流程：
  1) 初始时，S＝{v}，v的距离为0。T=V-{v}，若v与T中顶点u有边，则<u,v>正常有权值，若u不是v的邻接点，则<u,v>权值为∞
  2) 从T中选取一个距离v最小的顶点k加入S中(该距离就是v到k的最短路径长度)
  3) 以k为中间点，修改T中各顶点的距离；若从源点v到顶点u的距离（经过顶点k）比原来距离（不经过顶点k）短，则修改顶点u的距离值为v到k的距离加上k到u的距离(k到u的边的权)，修改后的距离值的顶点k的距离加上边上的权
  4) 重复2)和3)直到所有顶点都包含在S中
5.2.1 The Link-State (LS) Routing Algorithm

## Slide 17: Dijsktra's algorithm
5.2 routing protocols
Dijkstra 最短路径算法
  G=(V,E)是一个带权有向图，V分成两组S和T，V=S U T。S为已求出最短路径的顶点集合。初始S中只有一个源点v，以后每求得一条最短路径 , 就将加入S中，直到S=V。从T中找出到v最短路径的点p依次加入S中。在加入的过程中，保持从v到S中各顶点的最短路径长度不大于从v到T的最短路径长度。每个顶点对应一个距离，S中的顶点的距离就是从v到此顶点的最短路径长度，T中顶点t的距离，是从v到t只包括S中的顶点为中间顶点的当前最短路径长度。流程：
  1) 初始时，S＝{v}，v的距离为0。T=V-{v}，若v与T中顶点u有边，则<u,v>正常有权值，若u不是v的邻接点，则<u,v>权值为∞
  2) 从T中选取一个距离v最小的顶点k加入S中(该距离就是v到k的最短路径长度)
  3) 以k为中间点，修改T中各顶点的距离；若从源点v到顶点u的距离（经过顶点k）比原来距离（不经过顶点k）短，则修改顶点u的距离值为v到k的距离加上k到u的距离(k到u的边的权)，修改后的距离值的顶点k的距离加上边上的权
  4) 重复2)和3)直到所有顶点都包含在S中
5.2.1 The Link-State (LS) Routing Algorithm

## Slide 18
w
3
4
v
x
u
5
3
7
4
y
8
z
2
7
9
Dijkstra's algorithm: an example
Step
N'
D(v)
p(v)
0
1
2
3
4
5
D(w)
p(w)
D(x)
p(x)
D(y)
p(y)
D(z)
p(z)
u
∞
∞
7,u
3,u
5,u
uw
∞
11,w
6,w
5,u
14,x
11,w
6,w
uwx
uwxv
14,x
10,v
uwxvy
12,y
notes:
construct shortest path tree by tracing predecessor nodes
ties can exist (can be broken arbitrarily)
uwxvyz
5.2 routing protocols
5.2.1 The Link-State (LS) Routing Algorithm

## Slide 19: Dijkstra's algorithm: another example
Step
0
1
2
3
4
5
N'
u
ux
uxy
uxyv
uxyvw
uxyvwz
D(v),p(v)
2,u
2,u
2,u
D(w),p(w)
5,u
4,x
3,y
3,y
D(x),p(x)
1,u
D(y),p(y)
∞
2,x
D(z),p(z)
∞
∞
4,y
4,y
4,y
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
5.2 routing protocols
5.2.1 The Link-State (LS) Routing Algorithm
find a not in N' such that D(a) is a minimum
add a to N'
update D(b) for all b adjacent to a and not in N' :
D(b) = min ( D(b), D(a) + c(a,b) )
Initialization (step 0): For all a: if a adjacent to then D(a) = cu,a

## Slide 20: Dijkstra's algorithm: example (2)
u
y
x
w
v
z
resulting shortest-path tree from u:
v
x
y
w
z
(u,v)
(u,x)
(u,x)
(u,x)
(u,x)
destination
link
resulting forwarding table in u:
5.2 routing protocols
5.2.1 The Link-State (LS) Routing Algorithm
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
route from u to v directly
route from u to all other destinations via x
Notes: resulting least-cost-path tree from u:

## Slide 21: Dijkstra's algorithm: discussion
algorithm complexity: n nodes
each iteration: need to check all nodes, w, not in N
n(n+1)/2 comparisons: O(n2)
more efficient implementations possible: O(nlogn)
5.2 routing protocols
5.2.1 The Link-State (LS) Routing Algorithm
message complexity:
each router must broadcast its link state information to other n routers
efficient (and interesting!) broadcast algorithms: O(n) link crossings to disseminate a broadcast message from one source
each router’s message crosses O(n) links: overall message complexity: O(n2)

## Slide 22: Dijkstra's algorithm: discussion
A
D
C
B
1+e
e
0
e
1
1
0
0
initially
A
D
C
B
given these costs,
find new routing….
resulting in new costs
2+e
0
0
0
1+e
1
A
D
C
B
given these costs,
find new routing….
resulting in new costs
0
2+e
1+e
1
0
0
A
D
C
B
given these costs,
find new routing….
resulting in new costs
2+e
0
0
0
1+e
1
5.2 routing protocols
1
5.2.1 The Link-State (LS) Routing Algorithm
algorithm complexity: n nodes
each iteration: need to check all nodes, w, not in N
n(n+1)/2 comparisons: O(n2)
more efficient implementations possible: O(nlogn)
oscillations possible:
e.g., support link cost equals amount of carried traffic:
Notes: node C injects an amount of traffic equal to e destined for A
node D originates a unit of traffic destined for A
node B originates a unit of traffic destined for A

## Slide 23
5.1 Introduction
5.2 Routing algorithms
5.2.1 The Link-State (LS) Routing Algorithm
5.2.2 The Distance-Vector (DV) Routing Algorithm
5.3 Intra-AS routing in the Internet: OSPF
5.4 Routing among the ISPs: BGP
5.5 The SDN control plane
5.6 ICMP: The Internet Control Message Protocol
5.7 Network management and SNMP, NETCONF/YANG
Chapter 5 The Network Layer
: Control Plane
Network Layer - the control plane

## Slide 24: Distance vector algorithm
Bellman-Ford equation (dynamic programming)
let
dx(y) := cost of least-cost path from x to y
then
dx(y) = min {c(x,v) + dv(y) }
v
cost to neighbor v
min taken over all neighbors v of x
cost from neighbor v to destination y
5.2 routing protocols
5.2.2 The Distance-Vector (DV) Routing Algorithm

## Slide 25: Bellman-Ford example
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
clearly, dv(z) = 5, dx(z) = 3, dw(z) = 3
du(z) = min { c(u,v) + dv(z),
c(u,x) + dx(z),
c(u,w) + dw(z) }
= min {2 + 5,
1 + 3,
5 + 3} = 4
B-F equation says:
5.2 routing protocols
5.2.2 The Distance-Vector (DV) Routing Algorithm
Dv(z) = 5
Dw(z) = 3
Dx(z) = 3
node achieving minimum (x) is next hop on estimated least-cost path to destination (z)
Notes: node achieving minimum is next hop in shortest path, used in forwarding table

## Slide 26: Distance vector algorithm
Dx(y) = estimate of least cost from x to y
  x maintains distance vector Dx = [Dx(y): y є N ]
node x:
  knows cost to each neighbor v: c(x,v)
  maintains its neighbors' distance vectors. For each neighbor v, x maintains Dv = [Dv(y): y є N ]
5.2 routing protocols
5.2.2 The Distance-Vector (DV) Routing Algorithm

## Slide 27: Distance vector algorithm
key idea:
from time-to-time, each node sends its own distance vector estimate to neighbors
when x receives new DV estimate from any neighbor, it updates its own DV using B-F equation:
Dx(y) ← minv{c(x,v) + Dv(y)} for each node y ∊ N
under minor, natural conditions, the estimate Dx(y) converge to the actual least cost dx(y)
5.2 routing protocols
5.2.2 The Distance-Vector (DV) Routing Algorithm

## Slide 28: Distance vector algorithm
iterative,asynchronous: each local iteration caused by:
local link cost change
DV update message from neighbor
distributed: each node notifies neighbors only when its DV changes
neighbors then notify their neighbors – only if necessary
no notification received, no actions taken!
wait for (change in local link cost or msg from neighbor)
recompute DV estimates using DV received from neighbor
if DV to any dest has changed, notify neighbors
each node:
5.2 routing protocols
5.2.2 The Distance-Vector (DV) Routing Algorithm

## Slide 29
x y z
x
y
z
0 2 7
∞
∞
∞
∞
∞
∞
from
cost to
from
from
x y z
x
y
z
0
x y z
x
y
z
∞
∞
∞
∞
∞
cost to
x y z
x
y
z
∞
∞
∞
7
1
0
cost to
∞
2 0 1
∞ ∞ ∞
2 0 1
7 1 0
time
x
z
1
2
7
y
node x
table
Dx(y) = min{c(x,y) + Dy(y), c(x,z) + Dz(y)} = min{2+0 , 7+1} = 2
Dx(z) = min{c(x,y) + Dy(z), c(x,z) + Dz(z)}
= min{2+1 , 7+0} = 3
3
2
node y
table
node z
table
cost to
from
5.2 routing protocols
5.2.2 The Distance-Vector (DV) Routing Algorithm

## Slide 30
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
0 2 7
from
cost to
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
0 2 7
from
cost to
2 0 1
7 1 0
2 0 1
3 1 0
2 0 1
3 1 0
2 0 1
3 1 0
2 0 1
3 1 0
time
x y z
x
y
z
0 2 7
∞
∞
∞
∞
∞
∞
from
cost to
from
from
x y z
x
y
z
0
x y z
x
y
z
∞
∞
∞
∞
∞
cost to
x y z
x
y
z
∞
∞
∞
7
1
0
cost to
∞
2 0 1
∞ ∞ ∞
2 0 1
7 1 0
time
x
z
1
2
7
y
node x
table
Dx(y) = min{c(x,y) + Dy(y), c(x,z) + Dz(y)} = min{2+0 , 7+1} = 2
Dx(z) = min{c(x,y) + Dy(z), c(x,z) + Dz(z)}
= min{2+1 , 7+0} = 3
3
2
node y
table
node z
table
cost to
from
5.2 routing protocols
5.2.2 The Distance-Vector (DV) Routing Algorithm

## Slide 31: Distance vector: link cost changes
link cost changes:
node detects local link cost change
updates routing info, recalculates distance vector
if DV changes, notify neighbors
"good
news
travels
fast"
x
z
1
4
50
y
1
t0 : y detects link-cost change, updates its DV, informs its neighbors.
t1 : z receives update from y, updates its table, computes new least cost to x , sends its neighbors its DV.
t2 : y receives z's update, updates its distance table. y's least costs do not change, so y does not send a message to z.
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/
5.2 routing protocols
5.2.2 The Distance-Vector (DV) Routing Algorithm

## Slide 32: Distance vector: link cost changes
link cost changes:
node detects local link cost change
bad news travels slow - "count to infinity" problem!
44 iterations before algorithm stabilizes: see text
x
z
1
4
50
y
60
5.2 routing protocols
algorithm
continues
on!
X to Y
via
X to Z
via
X Z
4 6
X Y
50 5
time
t0
X Z
60 6
X Y
50 5
t1
X Z
60 6
X Y
50 7
t2
X Z
60 8
X Y
50 7
t3
X Z
60 8
X Y
50 9
t4
c(X,Y) change
5.2.2 The Distance-Vector (DV) Routing Algorithm

## Slide 33: Distance vector: link cost changes
x
z
1
4
50
y
60
poisoned reverse:
If Z routes through Y to get to X :
  Z tells Y its (Z's) distance to X is infinite (so Y won't route to X via Z)
will this completely solve count to infinity problem?
5.2 routing protocols
5.2.2 The Distance-Vector (DV) Routing Algorithm
algorithm
terminates
X to Y
via
X to Z
via
X Z
4 
X Y
50 5
time
t0
X Z
60 
X Y
50 5
t1
X Z
60 
X Y
50 61
t2
X Z
60 51
X Y
50 61
t3
X Z
60 51
X Y
50 
t4
c(X,Y) change
failed when containing loops involving three or more neighbors

## Slide 34: Distance vector: link cost changes
5.2 routing protocols
https://en.wikipedia.org/wiki/Distance-vector_routing_protocol#Count-to-infinity_problem
Counting to Infinity Problem Solutions
Set infinity = “some small integer” (e.g. 16). Stop when count = 16.
Split Horizon: Because C received lowest cost path from B, it does not advertise cost to B
poison reverse: C advertises infinity to B
There are many problems with (and fixes for) the Bellman-Ford algorithm.
5.2.2 The Distance-Vector (DV) Routing Algorithm

## Slide 35: Distance vector: link cost changes
link cost changes:
node detects local link cost change
bad news travels slow - "count to infinity" problem!
44 iterations before algorithm stabilizes: see text
x
z
1
4
50
y
60
poisoned reverse:
If Z routes through Y to get to X :
  Z tells Y its (Z's) distance to X is infinite (so Y won't route to X via Z)
will this completely solve count to infinity problem?
5.2 routing protocols
导致无穷计算问题的原因是把从对方获知的，但在对方已不再有效的信息当成有效信息再传送给对方，使对方当成有效信息使用。
5.2.2 The Distance-Vector (DV) Routing Algorithm

## Slide 36: Comparison of LS and DV algorithms
message complexity
LS: n nodes, O(n2) msgs sent
DV: exchange between neighbors only; convergence time varies
speed of convergence
LS: O(n2) algorithm, O(n2) msgs
  may have oscillations
DV: convergence time varies
  may be routing loops
  count-to-infinity problem
robustness: what happens if router malfunctions, or is compromised?
LS:
  node can advertise incorrect link cost
  each node computes only its own table
DV:
  DV node can advertise incorrect path cost (“I have a really low cost path to everywhere”): black-holing
  each node's table used by others: error propagate thru network
5.2 routing protocols
5.2.2 The Distance-Vector (DV) Routing Algorithm
Notes: Black hole attack is type of routing attack and can bring harm to whole network. Grey hole attack is the kind of denial of service attack. In this attack, the router which is mesh behave just not well and a subset of packets are forward and handle by receiver but leave by others.
https://www.researchgate.net/publication/273163452_Review_of_Black_Hole_and_Grey_Hole_Attack

## Slide 37
5.1 Introduction
5.2 Routing algorithms
5.3 Intra-AS routing in the Internet: OSPF
5.4 Routing among the ISPs: BGP
5.5 The SDN control plane
5.6 ICMP: The Internet Control Message Protocol
5.7 Network management and SNMP, NETCONF/YANG
5.3 Intra-AS routing in the Internet: OSPF
Chapter 5 The Network Layer
: Control Plane
Network Layer - the control plane
Notes: SDN: software defined network

## Slide 38: Making routing scalable
scale: billions of destinations:
can't store all destinations in routing tables!
routing table exchange would swamp links!
administrative autonomy
Internet: a network of networks
each network admin may want to control routing in its own network
our routing study thus far - idealized
all routers identical
network "flat"
… not true in practice
5.3 OSPF
homogeneous
Notes: heterogeneous

## Slide 39: Internet approach to scalable routing
aggregate routers into regions known as "autonomous system"s (AS’es) (a.k.a. "domain"s)
inter-AS (aka “inter-domain”):
routing among AS'es
gateways perform inter-domain routing (as well as intra-domain routing)
intra-AS (aka “intra-domain”):
routing among hosts, routers within the same AS ("network")
all routers in AS must run same intra-domain protocol
routers in different AS can run different intra-domain routing protocol
gateway router: at "edge" of its own AS, has link(s) to router(s) in other AS'es
5.3 OSPF

## Slide 40: Interconnected ASes
forwarding table configured by both intra- and inter-AS routing algorithm
  intra-AS routing determine entries for destinations within AS
  inter-AS & intra-AS determine entries for external destinations
5.3 OSPF
3b
1d
3a
1c
2a
AS3
AS1
AS2
1a
2c
2b
1b
3c
intra-AS
routing
intra-AS
routing
intra-AS
routing
inter-AS routing
forwarding
table
Intra-AS
Routing
algorithm
Inter-AS
Routing
algorithm

## Slide 41: Inter-AS routing: a role in intradomain forwarding
5.3 OSPF
3b
1d
3a
1c
2a
AS3
AS1
AS2
1a
2c
2b
1b
3c
other
networks
other
networks
suppose router in AS1 receives datagram destined outside of AS1:
AS1 inter-domain routing must:
learn which destinations reachable through AS2, which through AS3
propagate this reachability info to all routers in AS1
  router should forward packet to gateway router in AS1, but which one?
Notes: job of inter-AS routing

## Slide 42: Intra-AS routing: routing within an AS
also known as interior gateway protocols (IGP)
most common intra-AS routing protocols:
  RIP: Routing Information Protocol [RFC 1723]
    classic DV: DVs exchanged every 30 secs
    no longer widely used
  OSPF: Open Shortest Path First [RFC 2328]
    link-state routing
    IS-IS protocol (ISO standard, not RFC standard) essentially same as OSPF
  EIGRP: Enhanced Interior Gateway Routing Protocol [RFC 7868]
    DV based
    Cisco proprietary for decades, until May 2016, draft open in Feb 18, 2013
5.3 OSPF
Notes: Difference between IGRP and EIGRP
https://www.geeksforgeeks.org/difference-between-igrp-and-eigrp/
https://datatracker.ietf.org/doc/html/draft-savage-eigrp-00
https://datatracker.ietf.org/doc/html/rfc7868
https://community.cisco.com/t5/routing/eigrp-was-cisco-proprietary-is-it-an-open-standard-protocol-now/td-p/2528505

## Slide 43: OSPF (Open Shortest Path First)
"open": publicly available
uses classic link-state algorithm
  each router floods OSPF link-state advertisements (carried in OSPF messages directly over IP rather than using TCP/UDP) to all other routers in entire AS
  link state: for each attached link
  link state packet dissemination
  multiple link costs metrics possible: bandwidth, delay
  full topology map at each node
  forwarding table: route computation using Dijkstra's algorithm
security: all OSPF messages authenticated (to prevent malicious intrusion)
IS-IS routing protocol: nearly identical to OSPF
5.3 OSPF
Intermediate System to Intermediate System
https://en.wikipedia.org/wiki/IS-IS
IS-IS: Layer 2 protocol
OSPF: Layer 3 protocol

## Slide 44: OSPF "advanced" features
security: all OSPF messages authenticated (to prevent malicious intrusion)
multiple same-cost paths allowed (only one path in RIP)
for each link, multiple cost metrics for different TOS (e.g., satellite link cost set low for best effort ToS; high for real-time ToS)
integrated uni- and multi-cast support:
  Multicast OSPF (MOSPF) uses same topology data base as OSPF
hierarchical OSPF in large domains.
5.3 OSPF
Notes: Terms of Service 服务条款

## Slide 45: Hierarchical OSPF
area 1
area 2
area 3
backbone
area
border
routers
internal
routers
5.3 OSPF
two-level hierarchy: local area, backbone
  link-state advertisements flooded only in area, or backbone
  each node has detailed area topology; only knows direction to reach other destinations
area border routers: “summarize” distances to destinations in own area, advertise in backbone
backbone router: runs OSPF limited to backbone
boundary router:
connects to other ASes
local routers:
flood LS in area only
compute routing within area
forward packets to outside via area border router

## Slide 46
area border routers: "summarize" distances to nets in own area, advertise to other Area Border routers.
backbone routers: run OSPF routing limited to backbone.
boundary routers: connect to other AS'es.
5.3 OSPF
Hierarchical OSPF
two-level hierarchy: local area, backbone
  link-state advertisements flooded only in area, or backbone
  each node has detailed area topology; only knows direction to reach other destinations

## Slide 47: Homework this week
Problems of Chapter 5:
P3
P5
P9
Writing (optional):
  A short post about IGP, EGP, BGP, iBGP and eBGP, the relationship and difference of all these protocols.
Network Layer - the control plane

## Slide 48
5.1 Introduction
5.2 Routing algorithms
5.3 Intra-AS routing in the Internet: OSPF
5.4 Routing among the ISPs: BGP
5.5 The SDN control plane
5.6 ICMP: The Internet Control Message Protocol
5.7 Network management and SNMP, NETCONF/YANG
5.4 Routing among the ISPs: BGP
Chapter 5 The Network Layer
: Control Plane
Network Layer - the control plane

## Slide 49
5.1 Introduction
5.2 Routing algorithms
5.3 Intra-AS routing in the Internet: OSPF
5.4 Routing among the ISPs: BGP
5.4.1 The Role of BGP
5.4.2 Advertising BGP Route Information
5.4.3 Determining the Best Routes
5.4.4 IP-Anycast
5.4.5 Routing Policy
5.4.6 Putting the Pieces Together: Obtaining Internet Presence
5.5 The SDN control plane
5.4 Routing among the ISPs: BGP
Chapter 5 The Network Layer
: Control Plane
5.4 BGP

## Slide 50: Internet inter-AS routing: BGP
BGP (Border Gateway Protocol): the de facto inter-domain routing protocol
  "glue that holds the Internet together"
allows subnet to advertise its existence, and the destinations it can reach, to rest of Internet: "I am here, here is who I can reach, and how"
BGP provides each AS a means to:
  eBGP: obtain subnet information from neighboring ASes
  iBGP: propagate reachability information to all AS-internal routers.
  "good" routes to other networks based on reachability information and policy
5.4 BGP
1. reachability
2. determination
two tasks:
5.4.1 The Role of BGP
obsoletes EGP
Notes: EGP: https://www.tutorialspoint.com/what-is-exterior-gateway-protocol-egp

## Slide 51
5.1 Introduction
5.2 Routing algorithms
5.3 Intra-AS routing in the Internet: OSPF
5.4 Routing among the ISPs: BGP
5.4.1 The Role of BGP
5.4.2 Advertising BGP Route Information
5.4.3 Determining the Best Routes
5.4.4 IP-Anycast
5.4.5 Routing Policy
5.4.6 Putting the Pieces Together: Obtaining Internet Presence
5.5 The SDN control plane
5.4 Routing among the ISPs: BGP
Chapter 5 The Network Layer
: Control Plane
5.4 BGP

## Slide 52: eBGP, iBGP connections
eBGP connectivity
iBGP connectivity
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS 2
AS 3
AS 1
1c
∂
∂
gateway routers run both eBGP and iBGP protocols
5.4 BGP
5.4.2 Advertising BGP Route Information
internal routers

## Slide 53: BGP basics
when AS3 gateway router 3a advertises path AS3,X to AS2 gateway router 2c:
  AS3 promises to AS2 it will forward datagrams towards X
BGP session: two BGP routers ("peers") exchange BGP messages over semi-permanent TCP connection:
  advertising paths to different destination network prefixes (BGP is a "path vector" protocol)
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS 2
AS 3
AS 1
X
BGP advertisement:
AS3, X
5.4 BGP
5.4.2 Advertising BGP Route Information
Notes: permanent connection is a normal bearer channel（承载信道）, ex: Ts or E1. signaling channel and traffic channel is separate. when you borrow a traffic channel to signaling, the channel will be a semi permanent connection. you must config a connection through ST and dev.

## Slide 54: BGP path advertisement
based on AS2 policy, AS2 router 2c accepts path AS3,X, propagates (via iBGP) to all AS2 routers
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS2
AS3
AS1
X
AS3,X
AS2,AS3,X
AS2 router 2c receives path advertisement AS3,X (via eBGP) from AS3 router 3a
based on AS2 policy, AS2 router 2a advertises (via eBGP) path AS2, AS3, X to AS1 router 1c
5.4 BGP
5.4.2 Advertising BGP Route Information

## Slide 55: BGP path advertisement
AS1 gateway router 1c learns path AS2,AS3,X from 2a
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS2
AS3
AS1
X
AS3,X
AS2,AS3,X
gateway router may learn about multiple paths to destination:
AS3,X
AS1 gateway router 1c learns path AS3,X from 3a
based on policy, AS1 gateway router 1c chooses path AS3,X, and advertises path within AS1 via iBGP
5.4 BGP
5.4.2 Advertising BGP Route Information

## Slide 56
5.1 Introduction
5.2 Routing algorithms
5.3 Intra-AS routing in the Internet: OSPF
5.4 Routing among the ISPs: BGP
5.4.1 The Role of BGP
5.4.2 Advertising BGP Route Information
5.4.3 Determining the Best Routes
5.4.4 IP-Anycast
5.4.5 Routing Policy
5.4.6 Putting the Pieces Together: Obtaining Internet Presence
5.5 The SDN control plane
5.4 Routing among the ISPs: BGP
Chapter 5 The Network Layer
: Control Plane
5.4 BGP

## Slide 57: Path attributes and BGP routes
Policy-based routing:
  gateway receiving route advertisement uses import policy to accept/decline path (e.g., never route through AS Y).
  AS policy also determines whether to advertise path to other neighboring ASes
5.4 BGP
BGP advertised route: prefix + attributes
  prefix: destination being advertised
two important attributes:
  AS-PATH: list of ASes through which prefix advertisement has passed
  NEXT-HOP: indicates specific internal-AS router to next-hop AS
5.4.3 Determining the Best Routes
Notes: attribute 名词读 ˈa-trə-ˌbyüt
动词读 ə-ˈtri-ˌbyüt

## Slide 58: Path attributes and BGP routes
BGP advertised route: prefix + attributes
  prefix: destination being advertised
two important attributes:
  AS-PATH: list of ASes through which prefix advertisement has passed
  NEXT-HOP: indicates specific internal-AS router to next-hop AS
5.4 BGP
AS 2
AS 3
AS 1
2b
2a
2c
2d
3b
3a
3c
3d
1b
1a
1c
1d
next- hop
next- hop
IP address of leftmost interface for router 2a; AS2 AS3; x
IP address of leftmost interface of router 3d; AS3; x
two BGP routes to prefix x
5.4.3 Determining the Best Routes

## Slide 59: Hot Potato Routing
2d learns (via iBGP) it can route to X via 2a or 2c
hot potato routing: choose local gateway that has least intra-domain cost (e.g., 2d chooses 2a, even though more AS hops to X): don't worry about inter-domain cost!
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS2
AS3
AS1
X
AS3,X
AS1,AS3,X
OSPF link weights
201
152
112
263
5.4 BGP
5.4.3 Determining the Best Routes

## Slide 60: BGP route selection
router may learn about more than one route to destination AS, selects route based on:
  local preference value attribute: policy decision
  shortest AS-PATH
  closest NEXT-HOP router: hot potato routing
  additional criteria
5.4 BGP
5.4.3 Determining the Best Routes
Notes: BGP identifier

## Slide 61: BGP messages
BGP messages exchanged between peers over TCP connection
BGP messages:
  OPEN: opens TCP connection to remote BGP peer and authenticates sending BGP peer
  UPDATE: advertises new path (or withdraws old)
  KEEPALIVE: keeps connection alive in absence of UPDATES; also ACKs OPEN request
  NOTIFICATION: reports errors in previous msg; also used to close connection
5.4 BGP

## Slide 62: BGP, OSPF, forwarding table entries
recall: 1a, 1b, 1d learn about dest X via iBGP from 1c: "path to X goes through 1c"
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS2
AS3
AS1
X
AS3,X
AS2,AS3,X
AS3,X
1d: OSPF intra-domain routing: to get to 1c, forward over outgoing local interface 1
AS3,X
Q: how does router set forwarding table entry to distant prefix?
1
2
1
2
dest
interface
…
…
X
…
…
1
physical link
local link interfaces
at 1a, 1d
5.4 BGP

## Slide 63: BGP, OSPF, forwarding table entries
recall: 1a, 1b, 1c learn about dest X via iBGP from 1c: "path to X goes through 1c"
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS2
AS3
AS1
X
1d: OSPF intra-domain routing: to get to 1c, forward over outgoing local interface 1
Q: how does router set forwarding table entry to distant prefix?
dest
interface
…
…
X
…
…
2
1a: OSPF intra-domain routing: to get to 1c, forward over outgoing local interface 2
1
2
5.4 BGP

## Slide 64
5.1 Introduction
5.2 Routing algorithms
5.3 Intra-AS routing in the Internet: OSPF
5.4 Routing among the ISPs: BGP
5.4.1 The Role of BGP
5.4.2 Advertising BGP Route Information
5.4.3 Determining the Best Routes
5.4.4 IP-Anycast
5.4.5 Routing Policy
5.4.6 Putting the Pieces Together: Obtaining Internet Presence
5.5 The SDN control plane
5.4 Routing among the ISPs: BGP
Chapter 5 The Network Layer
: Control Plane
5.4 BGP

## Slide 65: IP-Anycast
5.4 BGP
5.4.4 IP-Anycast
replicating the same content on different servers in many different dispersed geographical locations
  Multiple instances of a service share the same IP address
  assigns this same IP address to each of its servers
  uses standard BGP to advertise this shared IP address
having each user access the content from the server that is closest
  The routing infrastructure directs any packet to the topologically nearest instance of the service
Failover is handled by removing the route for the failed instance
Requires nothing special for the clients
Makes use of standard routing topology

## Slide 66
5.1 Introduction
5.2 Routing algorithms
5.3 Intra-AS routing in the Internet: OSPF
5.4 Routing among the ISPs: BGP
5.4.1 The Role of BGP
5.4.2 Advertising BGP Route Information
5.4.3 Determining the Best Routes
5.4.4 IP-Anycast
5.4.5 Routing Policy
5.4.6 Putting the Pieces Together: Obtaining Internet Presence
5.5 The SDN control plane
5.4 Routing among the ISPs: BGP
Chapter 5 The Network Layer
: Control Plane
5.4 BGP

## Slide 67: BGP: achieving policy via advertisements
A advertises path Aw to B and to C
B chooses not to advertise BAw to C:
  B gets no "revenue" for routing CBAw, since none of C, A, w are B's customers
  C does not learn about CBAw path
C will route CAw (not using B) to get to w
A
B
C
W
X
Y
legend:
customer
network:
provider
network
Suppose an ISP only wants to route traffic to/from its customer networks (does not want to carry transit traffic between other ISPs)
5.4 BGP
5.4.5 Routing Policy

## Slide 68: BGP: achieving policy via advertisements
A,B,C are provider networks
X,W,Y are customer (of provider networks)
X is dual-homed: attached to two networks
policy to enforce: X does not want to route from B to C via X
  .. so X will not advertise to B a route to C
A
B
C
W
X
Y
legend:
customer
network:
provider
network
Suppose an ISP only wants to route traffic to/from its customer networks (does not want to carry transit traffic between other ISPs)
5.4 BGP
5.4.5 Routing Policy

## Slide 69: Why different Intra-, Inter-AS routing ?
policy:
inter-AS: admin wants control over how its traffic routed, who routes through its net.
intra-AS: single admin, so no policy decisions needed
scale:
hierarchical routing saves table size, reduced update traffic
performance:
intra-AS: can focus on performance
inter-AS: policy may dominate over performance
5.4 BGP
5.4.5 Routing Policy

## Slide 70
5.1 Introduction
5.2 Routing algorithms
5.3 Intra-AS routing in the Internet: OSPF
5.4 Routing among the ISPs: BGP
5.4.1 The Role of BGP
5.4.2 Advertising BGP Route Information
5.4.3 Determining the Best Routes
5.4.4 IP-Anycast
5.4.5 Routing Policy
5.4.6 Putting the Pieces Together: Obtaining Internet Presence
5.5 The SDN control plane
5.4 Routing among the ISPs: BGP
Chapter 5 The Network Layer
: Control Plane
5.4 BGP

## Slide 71: Putting the Pieces Together: Obtaining Internet Presence
Read the text!
5.4 BGP
5.4.6 Putting the Pieces Together: Obtaining Internet Presence

## Slide 72
5.1 Introduction
5.2 Routing algorithms
5.3 Intra-AS routing in the Internet: OSPF
5.4 Routing among the ISPs: BGP
5.5 The SDN control plane
5.6 ICMP: The Internet Control Message Protocol
5.7 Network management and SNMP, NETCONF/YANG
5.5 The SDN control plane
Chapter 5 The Network Layer
: Control Plane
Network Layer - the control plane
Notes: SDN: software defined network

## Slide 73
Software defined networking (SDN)
Internet network layer: historically has been implemented via distributed, per-router approach
  monolithic router contains switching hardware, runs proprietary implementation of Internet standard protocols (IP, RIP, IS-IS, OSPF, BGP) in proprietary router OS (e.g., Cisco IOS)
  different "middleboxes" for different network layer functions: firewalls, load balancers, NAT boxes, ..
~2005: renewed interest in rethinking network control plane
5.5 The SDN control plane

## Slide 74
Recall: per-router control plane
Routing
Algorithm
Individual routing algorithm components in each and every router interact with each other in control plane to compute forwarding tables
data
plane
control
plane
5.5 The SDN control plane

## Slide 75
data
plane
control
plane
Recall: logically centralized control plane
A distinct (typically remote) controller interacts with local control agents (CAs) in routers to compute forwarding tables
Remote Controller
CA
CA
CA
CA
CA
5.5 The SDN control plane

## Slide 76
Software defined networking (SDN)
Why a logically centralized control plane?
easier network management: avoid router misconfigurations, greater flexibility of traffic flows
table-based forwarding (recall OpenFlow API) allows "programming" routers
  centralized "programming" easier: compute tables centrally and distribute
  distributed "programming" more difficult: compute tables as result of distributed algorithm (protocol) implemented in each and every router
open (non-proprietary) implementation of control plane
5.5 The SDN control plane

## Slide 77: Analogy: mainframe to PC evolution
Vertically integrated
Closed, proprietary
Slow innovation
Small industry
Horizontal
Open interfaces
Rapid innovation
Huge industry
5.5 The SDN control plane
Specialized
Operating
System
Specialized
Hardware
Specialized
Applications
Microprocessor
Open Interface
or
or
Open Interface
Windows
Linux
MAC OS
App
App
App
App
App
App
App
App
App
App
App

## Slide 78: Traffic engineering: difficult with traditional routing
Q: what if network operator wants u-to-z traffic to flow along uvwz, x-to-z traffic to flow xwyz?
A: need to define link weights so traffic routing algorithm computes routes accordingly (or need a new routing algorithm)!
Link weights are only control "knobs": wrong!
2
2
1
3
1
1
2
5
3
5
v
w
u
z
y
x
5.5 The SDN control plane
Notes: Note: implicit assumption here: destination based forwarding

## Slide 79: Traffic engineering: difficult traditional routing
Q: what if network operator wants to split u-to-z traffic along uvwz and uxyz (load balancing)?
A: can't do it (or need a new routing algorithm)
2
2
1
3
1
1
2
5
3
5
v
w
u
z
y
x
5.5 The SDN control plane
Notes: Note: implicit assumption here: destination based forwarding

## Slide 80: Traffic engineering: difficult traditional routing
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
u
v
x
w
y
z
Q: what if w wants to route orange and red traffic differently?
A: can't do it (with destination based forwarding, and LS, DV routing)
5.5 The SDN control plane
Notes: Note: implicit assumption here: destination based forwarding

## Slide 81
Software defined networking (SDN)
data
plane
control
plane
Remote Controller
CA
CA
CA
CA
CA
1: generalized" flow-based" forwarding (e.g., OpenFlow)
2. control, data plane separation
3. control plane functions external to data-plane switches
…
4. programmable control applications
routing
access control
load
balance
5.5 The SDN control plane

## Slide 82
5.1 Introduction
5.2 Routing algorithms
5.3 Intra-AS routing in the Internet: OSPF
5.4 Routing among the ISPs: BGP
5.5 The SDN control plane
5.5.1 SDN Controller and SDN Network-control Applications
5.5.2 OpenFlow Protocol
5.5.3 Data and Control Plane Interaction: An Example
5.5.4 SDN: Past and Future
5.6 ICMP: The Internet Control Message Protocol
5.7 Network management and SNMP, NETCONF/YANG
5.5 The SDN control plane
Chapter 5 The Network Layer
: Control Plane
5.5 The SDN control plane

## Slide 83
SDN perspective: data plane switches
Data plane switches
fast, simple, commodity switches implementing generalized data-plane forwarding (Section 4.4) in hardware
switch flow table computed, installed by controller
API for table-based switch control (e.g., OpenFlow)
  defines what is controllable and what is not
protocol for communicating with controller (e.g., OpenFlow)
data
plane
control
plane
SDN Controller
(network operating system)
…
routing
access
control
load
balance
southbound API
northbound API
SDN-controlled switches
network-control applications
5.5 The SDN control plane
5.5.1 SDN Controller and SDN Network-control Applications

## Slide 84
SDN perspective: SDN controller
SDN controller (network OS):
maintain network state information
interacts with network control applications "above" via northbound API
interacts with network switches "below" via southbound API
implemented as distributed system for performance, scalability, fault-tolerance, robustness
data
plane
control
plane
SDN Controller
(network operating system)
…
routing
access
control
load
balance
southbound API
northbound API
SDN-controlled switches
network-control applications
5.5 The SDN control plane
5.5.1 SDN Controller and SDN Network-control Applications

## Slide 85
SDN perspective: control applications
network-control apps:
"brains" of control: implement control functions using lower-level services, API provided by SDN controller
unbundled: can be provided by 3rd party: distinct from routing vendor, or SDN controller
data
plane
control
plane
SDN Controller
(network operating system)
…
routing
access
control
load
balance
southbound API
northbound API
SDN-controlled switches
network-control applications
5.5 The SDN control plane
5.5.1 SDN Controller and SDN Network-control Applications

## Slide 86
Network-wide distributed, robust state management
Communication to/from controlled devices
Link-state info
switch info
host info
statistics
flow tables
…
…
OpenFlow
SNMP
…
network graph
intent
RESTful
API
…
Interface, abstractions for network control apps
SDN
controller
routing
access
control
load
balance
Components of SDN controller
communication layer: communicate between SDN controller and controlled switches
Network-wide state management layer: state of networks links, switches, services: a distributed database
Interface layer to network control apps: abstractions API
5.5 The SDN control plane
5.5.1 SDN Controller and SDN Network-control Applications
Notes: REST: Representational State Transfer
Key to RESTful: resources
Key to RPC: methods

## Slide 87
5.1 Introduction
5.2 Routing algorithms
5.3 Intra-AS routing in the Internet: OSPF
5.4 Routing among the ISPs: BGP
5.5 The SDN control plane
5.5.1 SDN Controller and SDN Network-control Applications
5.5.2 OpenFlow Protocol
5.5.3 Data and Control Plane Interaction: An Example
5.5.4 SDN: Past and Future
5.6 ICMP: The Internet Control Message Protocol
5.7 Network management and SNMP, NETCONF/YANG
5.5 The SDN control plane
Chapter 5 The Network Layer
: Control Plane
5.5 The SDN control plane

## Slide 88: OpenFlow protocol
operates between controller, switch
TCP used to exchange messages
  optional encryption
three classes of OpenFlow messages:
  controller-to-switch
  asynchronous (switch to controller)
  symmetric (misc)
distinct from OpenFlow API
  API used to specify generalized forwarding actions
OpenFlow Controller
5.5 The SDN control plane
port # 6653
https://www.doit.com.cn/p/96731.html

## Slide 89: OpenFlow: controller-to-switch messages
Key controller-to-switch messages
features: controller queries switch features, switch replies
configure: controller queries/sets switch configuration parameters
modify-state: add, delete, modify flow entries in the OpenFlow tables
packet-out: controller can send this packet out of specific switch port
OpenFlow Controller
5.5 The SDN control plane

## Slide 90: OpenFlow: switch-to-controller messages
Key switch-to-controller messages
packet-in: transfer packet (and its control) to controller. See packet-out message from controller
flow-removed: flow table entry deleted at switch
port status: inform controller of a change on a port.
Fortunately, network operators don't "program" switches by creating/sending OpenFlow messages directly. Instead use higher-level abstraction at controller
OpenFlow Controller
5.5 The SDN control plane

## Slide 91
5.1 Introduction
5.2 Routing algorithms
5.3 Intra-AS routing in the Internet: OSPF
5.4 Routing among the ISPs: BGP
5.5 The SDN control plane
5.5.1 SDN Controller and SDN Network-control Applications
5.5.2 OpenFlow Protocol
5.5.3 Data and Control Plane Interaction: An Example
5.5.4 SDN: Past and Future
5.6 ICMP: The Internet Control Message Protocol
5.7 Network management and SNMP, NETCONF/YANG
5.5 The SDN control plane
Chapter 5 The Network Layer
: Control Plane
5.5 The SDN control plane

## Slide 92
Link-state info
switch info
host info
statistics
flow tables
…
…
OpenFlow
SNMP
…
network graph
intent
RESTful
API
…
1
2
3
4
6
5
Dijkstra's link-state
Routing
s1
s2
s3
s4
SDN: control/data plane interaction example
S1, experiencing link failure using OpenFlow port status message to notify controller
1
SDN controller receives OpenFlow message, updates link status info
2
Dijkstra's routing algorithm application has previously registered to be called when ever link status changes. It is called.
3
Dijkstra's routing algorithm access network graph info, link state info in controller, computes new routes
4
5.5 The SDN control plane

## Slide 93
Link-state info
switch info
host info
statistics
flow tables
…
…
OpenFlow
SNMP
…
network graph
intent
RESTful
API
…
1
2
3
4
6
5
Dijkstra's link-state
Routing
s1
s2
s3
s4
SDN: control/data plane interaction example
link state routing app interacts with flow-table-computation component in SDN controller, which computes new flow tables needed
5
Controller uses OpenFlow to install new tables in switches that need updating
6
5.5 The SDN control plane

## Slide 94
5.1 Introduction
5.2 Routing algorithms
5.3 Intra-AS routing in the Internet: OSPF
5.4 Routing among the ISPs: BGP
5.5 The SDN control plane
5.5.1 SDN Controller and SDN Network-control Applications
5.5.2 OpenFlow Protocol
5.5.3 Data and Control Plane Interaction: An Example
5.5.4 SDN: Past and Future
5.6 ICMP: The Internet Control Message Protocol
5.7 Network management and SNMP, NETCONF/YANG
5.5 The SDN control plane
Chapter 5 The Network Layer
: Control Plane
5.5 The SDN control plane

## Slide 95
topology
manager
Basic Network Service Functions
REST API
OpenFlow 1.0
…
SNMP
OVSDB
forwarding
manager
switch
manager
host
manager
stats
manager
Network service apps
Service Abstraction Layer (SAL)
Access
Control
Traffic
Engineering
…
OpenDaylight (ODL) controller
ODL Phosphorus controller (ODL 15.0)
network apps may be contained within, or be external to SDN controller
Service Abstraction Layer: interconnects internal, external applications and services
5.5 The SDN control plane
https://readthedocs.org/projects/opendaylight/
lithium -> neon -> magnesium -> phosphorus
Notes: https://www.opendaylight.org/
Lithium 锂
Neon 氖
Magnesium 镁 120
phosphorus 磷 15.0

## Slide 96
Network
control apps
…
REST API
ONOS
distributed core
southbound abstractions,
protocols
OpenFlow
Netconf
OVSDB
device
link
host
flow
packet
northbound abstractions,
protocols
Intent
statistics
devices
hosts
links
paths
flow rules
topology
ONOS controller
control apps separate from controller
intent framework: high-level specification of service: what rather than how
considerable emphasis on distributed core: service reliability, replication performance scaling
5.5 The SDN control plane
Notes: https://opennetworking.org/onos

## Slide 97
SDN: selected challenges
hardening the control plane: dependable, reliable, performance-scalable, secure distributed system
  robustness to failures: leverage strong theory of reliable distributed system for control plane
  dependability, security: "baked in" from day one?
networks, protocols meeting mission-specific requirements
  e.g., real-time, ultra-reliable, ultra-secure
Internet-scaling
SDN critical in 5G cellular networks
5.5 The SDN control plane
Notes: Internet-scaling: from intra-AS to inter-AS

## Slide 98: SDN and the future of traditional network protocols
SDN-computed versus router-computer forwarding tables:
  just one example of logically-centralized-computed versus protocol computed
one could imagine SDN-computed congestion control:
  controller sets sender rates based on router-reported (to controller) congestion levels
How will implementation of network functionality (SDN versus protocols) evolve?
5.5 The SDN control plane

## Slide 99
5.1 Introduction
5.2 Routing algorithms
5.3 Intra-AS routing in the Internet: OSPF
5.4 Routing among the ISPs: BGP
5.5 The SDN control plane
5.6 ICMP: The Internet Control Message Protocol
5.7 Network management and SNMP, NETCONF/YANG
5.6 ICMP: The Internet Control Message Protocol
Chapter 5 The Network Layer
: Control Plane
Network Layer - the control plane
Notes: SDN: software defined network

## Slide 100: ICMP: internet control message protocol
used by hosts & routers to communicate network-level information
  error reporting: unreachable host, network, port, protocol
  echo request/reply (used by ping)
network-layer "above" IP:
  ICMP msgs carried in IP datagrams
ICMP message: type, code plus first 8 bytes of IP datagram causing error
Type Code description
0 0 echo reply (ping)
3 0 dest. network unreachable
3 1 dest host unreachable
3 2 dest protocol unreachable
3 3 dest port unreachable
3 6 dest network unknown
3 7 dest host unknown
4 0 source quench (congestion
control - not used)
8 0 echo request (ping)
9 0 route advertisement
10 0 router discovery
11 0 TTL expired
12 0 bad IP header
5.6 ICMP
Notes: source quench: 源抑制

## Slide 101: Traceroute and ICMP
source sends series of UDP segments to destination
  first set has TTL =1
  second set has TTL=2, etc.
  unlikely port number (e.g. 80)
when datagram in nth set arrives to nth router:
  router discards datagram and sends source ICMP message (type 11, code 0)
  ICMP message include name of router & IP address
when ICMP message arrives, source records RTTs
stopping criteria:
UDP segment eventually arrives at destination host
destination returns ICMP "port unreachable" message (type 3, code 3)
source stops
3 probes
3 probes
3 probes
5.6 ICMP
80 is an HTTP port number, based on TCP,
this is unlikely to UDP

## Slide 102
5.1 Introduction
5.2 Routing algorithms
5.3 Intra-AS routing in the Internet: OSPF
5.4 Routing among the ISPs: BGP
5.5 The SDN control plane
5.6 ICMP: The Internet Control Message Protocol
5.7 Network management and SNMP, NETCONF/YANG
5.7 Network management and SNMP, NETCONF/YANG
Chapter 5 The Network Layer
: Control Plane
Network Layer - the control plane
Notes: SDN: software defined network

## Slide 103
5.1 Introduction
5.2 Routing algorithms
5.3 Intra-AS routing in the Internet: OSPF
5.4 Routing among the ISPs: BGP
5.5 The SDN control plane
5.6 ICMP: The Internet Control Message Protocol
5.7 Network management and SNMP, NETCONF/YANG
5.7.1 The Network Management Framework
5.7.2 SNMP and the Management Information Base (MIB)
5.7.3 NETCONF and YANG
Chapter 5 The Network Layer
: Control Plane
5.7 SNMP

## Slide 104: What is network management?
autonomous systems (aka "network"): 1000s of interacting hardware/software components
other complex systems requiring monitoring, control:
  jet airplane
  nuclear power plant
  others?
"Network management includes the deployment, integration
and coordination of the hardware, software, and human
elements to monitor, test, poll, configure, analyze, evaluate,
and control the network and element resources to meet the
real-time, operational performance, and Quality of Service
requirements at a reasonable cost."
5.7 SNMP
Tuncay Saydam
1996
5.7.1 Network Management Framework
Notes: poll: 轮询、挂起到队列

## Slide 105: Infrastructure for network management
managed device
managed device
managed device
managed device
definitions:
managed devices contain managed objects whose data is gathered into a Management Information Base (MIB)
managing
entity
data
managing entity
agent
data
agent
data
network
management
protocol
managed device
agent
data
agent
data
agent
data
5.7 SNMP
5.7.1 Network Management Framework

## Slide 106: SNMP protocol
Two ways to convey MIB info, commands:
agent
data
managed device
managing
entity
agent
data
managed device
managing
entity
trap msg
request
request/response mode
trap mode
response
5.7 SNMP
5.7.1 Network Management Framework
Notes: trap message: 陷阱报文，例如链路接口的启动与关闭时发送非请求报文

## Slide 107
5.1 Introduction
5.2 Routing algorithms
5.3 Intra-AS routing in the Internet: OSPF
5.4 Routing among the ISPs: BGP
5.5 The SDN control plane
5.6 ICMP: The Internet Control Message Protocol
5.7 Network management and SNMP, NETCONF/YANG
5.7.1 The Network Management Framework
5.7.2 SNMP and the Management Information Base (MIB)
5.7.3 NETCONF and YANG
Chapter 5 The Network Layer
: Control Plane
5.7 SNMP

## Slide 108: SNMP protocol: message types
GetRequest
GetNextRequest
GetBulkRequest
manager-to-agent: "get me data"
(data instance, next data in list, block of data)
Message type
Function
InformRequest
manager-to-manager: here's MIB value
SetRequest
manager-to-agent: set MIB value
Response
Agent-to-manager: value, response to
Request
Trap
Agent-to-manager: inform manager
of exceptional event
5.7 SNMP
SNMP operates in the application layer
SNMP messages are transported via UDP
protocol data unit — PDU
unsolicited message
Request
/
Response
message
5.7.2 SNMP and Management Information Base (MIB)

## Slide 109: SNMP protocol: message formats
….
PDU
type
(0-3)
Request
ID
Error
Status
(0-5)
Error
Index
Name
Value
Name
Value
….
PDU
type
4
Enterprise
Agent
Addr
Trap
Type
(0-7)
Specific
code
Time
stamp
Name
Value
Get/set header
Variables to get/set
Trap header
Trap info
SNMP PDU
More on network management: see earlier editions of text!
5.7 SNMP
PDU format
5.7.2 SNMP and Management Information Base (MIB)
https://www.rfc-editor.org/rfc/rfc3416 page 6
Notes: PDU: Protocol Data Unit
Each SNMP message contains a protocol data unit (PDU). These SNMP PDUs are used for communication between SNMP managers and SNMP agents. The SNMP Version 1 architecture defines the following types of PDUs that flow between SNMP managers and SNMP agents:
GETREQUEST PDU
Sent by the SNMP manager to retrieve one or more requested MIB variables specified in the PDU.
GETNEXTREQUEST PDU
Sent by the SNMP manager to retrieve the next MIB variable that is specified in the PDU. You can have multiple requests in the PDU. This PDU is primarily used by the SNMP manager to walk through the SNMP agent MIB.
SETREQUEST PDU
Sent by the SNMP manager to set one or more MIB variables specified in the PDU with the value specified in the PDU.
GETRESPONSE PDU
Sent by the SNMP agent in response to a GETREQUEST, GETNEXTREQUEST, or SETREQUEST PDU.
TRAP PDU
- An unsolicited message sent by the SNMP agent to notify the SNMP manager about a significant event that occurred in the agent.

## Slide 110: SNMP: Management Information Base (MIB)
managed device’s operational (and some configuration) data
gathered into device MIB module
  400 MIB modules defined in RFC’s; many more vendor-specific MIBs
Object ID Name Type Comments
1.3.6.1.2.1.7.1 UDPInDatagrams 32-bit counter total # datagrams delivered
1.3.6.1.2.1.7.2 UDPNoPorts 32-bit counter # undeliverable datagrams (no application at port)
1.3.6.1.2.1.7.3 UDInErrors 32-bit counter # undeliverable datagrams (all other reasons)
1.3.6.1.2.1.7.4 UDPOutDatagrams 32-bit counter total # datagrams sent
1.3.6.1.2.1.7.5 udpTable SEQUENCE one entry for each port currently in use
agent
data
Structure of Management Information (SMI): data definition language
example MIB variables for UDP protocol:
5.7 SNMP
5.7.2 SNMP and Management Information Base (MIB)

## Slide 111
5.1 Introduction
5.2 Routing algorithms
5.3 Intra-AS routing in the Internet: OSPF
5.4 Routing among the ISPs: BGP
5.5 The SDN control plane
5.6 ICMP: The Internet Control Message Protocol
5.7 Network management and SNMP, NETCONF/YANG
5.7.1 The Network Management Framework
5.7.2 SNMP and the Management Information Base (MIB)
5.7.3 NETCONF and YANG
Chapter 5 The Network Layer
: Control Plane
5.7 SNMP

## Slide 112: NETCONF overview
goal: actively manage/configure devices network-wide
operates between managing server and managed network devices
  actions: retrieve, set, modify, activate configurations
  atomic-commit actions over multiple devices
  query operational data and statistics
  subscribe to notifications from devices
remote procedure call (RPC) paradigm
  NETCONF protocol messages encoded in XML
  exchanged over secure, reliable transport (e.g., TLS) protocol
5.7 SNMP
5.7.3 NETCONF and YANG

## Slide 113: NETCONF initialization, exchange, close
Session initiation,
capabilities exchange: <hello>
Session close: <close-session>
<rpc>
<rpc-reply>
<rpc>
<rpc-reply>
<rpc>
<rpc-reply>
<notification>
…
…
…
…
…
…
…
…
…
managing
server/controller
data
agent
data
5.7 SNMP
5.7.3 NETCONF and YANG

## Slide 114: Selected NETCONF Operations
NETCONF Operation Description
<get-config> Retrieve all or part of a given configuration. A device may have multiple configurations.
<get> Retrieve all or part of both configuration state and operational state data.
<edit-config> Change specified (possibly running) configuration at managed device. Managed device <rpc-reply> contains <ok> or <rpcerror> with rollback.
<lock>, <unlock> Lock (unlock) configuration datastore at managed device (to lock out NETCONF, SNMP, or CLIs commands from other sources).
<create-subscription>, Enable event notification subscription from managed device
<notification>
5.7 SNMP
5.7.3 NETCONF and YANG

## Slide 115: Sample NETCONF RPC message
note message id
change the running configuration
change MTU of Ethernet 0/0 interface to 1500
change a configuration
5.7 SNMP
5.7.3 NETCONF and YANG

## Slide 116: YANG
data modeling language used to specify structure, syntax, semantics of NETCONF network management data
  built-in data types, like SMI
XML document describing device, capabilities can be generated from YANG description
can express constraints among data that must be satisfied by a valid NETCONF configuration
  ensure NETCONF configurations satisfy correctness, consistency constraints
agent
data
managing
server/controller
data
NETCONF RPC message
<edit-config>
YANG-generated XML
</edit-config>
YANG
generated
5.7 SNMP
5.7.3 NETCONF and YANG

## Slide 117
Chapter 5 summary
Network Layer - the control plane
we've learned a lot!
approaches to network control plane
  per-router control (traditional)
  logically centralized control (software defined networking)
traditional routing algorithms
  implementation in Internet: OSPF, BGP
SDN controllers
  implementation in practice: ODL, ONOS
Internet Control Message Protocol
network management
next stop: link layer!

## Slide 118
TELNET
HTTP
FTP
SMTP
DNS
RIP
SNMP
DHCP
TCP
UDP
IP
ICMP
OSPF
ARP
RARP
application layer
transport
layer
network
layer
The Internet Hourglass
link
layer
ethernet
802.11
SONET
ATM
Network Layer - the control plane

## Slide 119: Homework this week
Problems of Chapter 5:
P12
P16
P20
P22
Lab: https://www.github.com/network-whu/lab/
  3.Wireshark_ICMP.docx
  Hand-in: add to your lab report, in a separate chapter
Network Layer - the control plane