## Slide 1: Chapter 6 The Link Layer & LANs
Slides are adapted from those of by J.F Kurose and K.W. Ross with copyright 1996-2020 J.F Kurose and K.W. Ross, All Rights Reserved

## Slide 2: Chapter 6 The Link layer and LANs
our goals:
understand principles behind link layer services:
  error detection, correction
  sharing a broadcast channel: multiple access
  link layer addressing
  local area networks: Ethernet, VLANs
instantiation, implementation of various link layer technologies
The Link layer and LANs

## Slide 3
6.1 Introduction
6.2 Error-Detection and -Correction Techniques
6.3 Multiple Access Links and Protocols
6.4 Switched Local Area Networks
6.5 Link Virtualization: A Network as a Link Layer
6.6 Data Center Networking
6.7 Retrospective: A Day in the Life of a Web Page Request
6.1 Introduction
Chapter 6 The Link layer and LANs
The Link layer and LANs

## Slide 4: Link layer: introduction
terminology:
hosts and routers: nodes
communication channels that connect adjacent nodes along communication path: links
  wired links
  wireless links
  LANs
layer-2 packet: frame, encapsulates datagram
data-link layer has responsibility of
transferring datagram from one node
to physically adjacent node over a link
6.1 introduction
mobile network
enterprise
network
national or global ISP
datacenter
network
point-to-point
broadcast

## Slide 5: Link layer: context
datagram transferred by different link protocols over different links:
  e.g., Ethernet on first link, frame relay on intermediate links, 802.11 on last link
each link protocol provides different services
  e.g., may or may not provide rdt over link
transportation analogy:
trip from whu to Stanford
  limo: whu campus to WUH
  plane: WUH to SFO
  caltrain: SFO to Palo Alto
  Marguerite Shuttle: to oval loop
tourist = datagram
transport segment = communication link
transportation mode = link layer protocol
travel agent = routing algorithm
6.1 introduction

## Slide 6
6.1 Introduction
  6.1.1 The Services Provided by the Link Layer
  6.1.2 Where Is the Link Layer Implemented?
6.2 Error-Detection and -Correction Techniques
6.3 Multiple Access Links and Protocols
6.4 Switched Local Area Networks
6.5 Link Virtualization: A Network as a Link Layer
6.6 Data Center Networking
6.7 Retrospective: A Day in the Life of a Web Page Request
Chapter 6 The Link layer and LANs
The Link layer and LANs

## Slide 7
6.1 Introduction
  6.1.1 The Services Provided by the Link Layer
  6.1.2 Where Is the Link Layer Implemented?
6.2 Error-Detection and -Correction Techniques
6.3 Multiple Access Links and Protocols
6.4 Switched Local Area Networks
6.5 Link Virtualization: A Network as a Link Layer
6.6 Data Center Networking
6.7 Retrospective: A Day in the Life of a Web Page Request
Chapter 6 The Link layer and LANs
The Link layer and LANs

## Slide 8: Link layer services
framing, link access:
  encapsulate datagram into frame, adding header, trailer and escape character for transparent transfer
  "MAC" addresses used in frame headers to identify source, destination
    different from IP address!
  channel access if shared medium
reliable delivery between adjacent nodes
  we learned how to do this already (chapter 3)!
  seldom used on low bit-error link (fiber, some twisted pair)
  wireless links: high error rates
    Q: why both link-level and end-end reliability?
6.1 introduction
6.1.1 The Services Provided by the Link Layer
Notes: Packet may get lost, end-2-end reliability can deal with such problem

## Slide 9: Link layer services (more)
flow control:
  pacing between adjacent sending and receiving nodes
error detection:
  errors caused by signal attenuation, noise.
  receiver detects presence of errors:
    signals sender for retransmission or drops frame
error correction:
  receiver identifies and corrects bit error(s) without resorting to retransmission
half-duplex and full-duplex
  with half duplex, nodes at both ends of link can transmit, but not at same time
6.1 introduction
6.1.1 The Services Provided by the Link Layer

## Slide 10
6.1 Introduction
  6.1.1 The Services Provided by the Link Layer
  6.1.2 Where Is the Link Layer Implemented?
6.2 Error-Detection and -Correction Techniques
6.3 Multiple Access Links and Protocols
6.4 Switched Local Area Networks
6.5 Link Virtualization: A Network as a Link Layer
6.6 Data Center Networking
6.7 Retrospective: A Day in the Life of a Web Page Request
Chapter 6 The Link layer and LANs
The Link layer and LANs

## Slide 11: Where is the link layer implemented?
in each and every host
link layer implemented in "adaptor" (aka network interface card NIC) or on a chip
  Ethernet card, 802.11 card; Ethernet chipset
  implements link, physical layer
attaches into host's system buses
combination of hardware, software, firmware
controller
physical
transmission
cpu
memory
host
bus
(e.g., PCI)
network adapter
card
application
transport
network
link
link
physical
6.1 introduction
6.1.2 Where Is the Link Layer Implemented?

## Slide 12: Adaptor interfaces communicating
sending side:
  encapsulates datagram in frame
  adds error checking bits, rdt, flow control, etc.
receiving side
  looks for errors, rdt, flow control, etc.
  extracts datagram, passes to upper layer at receiving side
6.1 introduction
6.1.2 Where Is the Link Layer Implemented?
controller
physical
memory
CPU
controller
physical
cpu
memory
application
transport
network
link
link
physical
application
transport
network
link
link
physical
linkh
linkh
datagram
datagram
datagram

## Slide 13
6.1 Introduction
6.2 Error-Detection and -Correction Techniques
6.3 Multiple Access Links and Protocols
6.4 Switched Local Area Networks
6.5 Link Virtualization: A Network as a Link Layer
6.6 Data Center Networking
6.7 Retrospective: A Day in the Life of a Web Page Request
6.2 Error-Detection and -Correction Techniques
Chapter 6 The Link layer and LANs
The Link layer and LANs

## Slide 14: Error detection
EDC = Error Detection and Correction bits (redundancy)
D = Data protected by error checking, may include header fields
6.2 error detection, correction
Error detection not 100% reliable!
  protocol may miss some errors, but rarely
  larger EDC field yields better detection and correction
datagram
D
EDC
d data bits
bit-error prone link
D’
EDC’
all
bits in D’
OK
?
N
detected
error
otherwise
datagram

## Slide 15
6.1 Introduction
6.2 Error-Detection and -Correction Techniques
  6.2.1 Parity Checks
  6.2.2 Checksumming Methods
  6.2.3 Cyclic Redundancy Check (CRC)
6.3 Multiple Access Links and Protocols
6.4 Switched Local Area Networks
6.5 Link Virtualization: A Network as a Link Layer
6.6 Data Center Networking
6.7 Retrospective: A Day in the Life of a Web Page Request
Chapter 6 The Link layer and LANs
The Link layer and LANs

## Slide 16
6.1 Introduction
6.2 Error-Detection and -Correction Techniques
  6.2.1 Parity Checks
  6.2.2 Checksumming Methods
  6.2.3 Cyclic Redundancy Check (CRC)
6.3 Multiple Access Links and Protocols
6.4 Switched Local Area Networks
6.5 Link Virtualization: A Network as a Link Layer
6.6 Data Center Networking
6.7 Retrospective: A Day in the Life of a Web Page Request
Chapter 6 The Link layer and LANs
The Link layer and LANs

## Slide 17: Parity checking
single bit parity:
detect single bit errors
two-dimensional bit parity:
detect and correct single bit errors
6.2 error detection, correction
0111000110101011
1
parity
bit
d data bits
Even parity: set parity bit so there is an even number of 1’s
d1,1
d2,1
di,1
. . .
d1,j+1
d2,j+1
di,j+1
. . .
. . .
d1,j
d2,j
di,j
. . .
di+1,1
di+1,j+1
di+1,j
. . .
. . .
. . .
. . .
row parity
column
parity
0 1 1 1 0 1
1 0 1 0 1 1
1 1 1 1 0 0
0 0 1 0 1 0
no errors:
0 1 1 1 0 1
1 0 1 0 1 1
1 0 1 1 0 0
0 0 1 0 1 0
parity
error
parity
error
detected
and
correctable
single-bit
error:

## Slide 18
6.1 Introduction
6.2 Error-Detection and -Correction Techniques
  6.2.1 Parity Checks
  6.2.2 Checksumming Methods
  6.2.3 Cyclic Redundancy Check (CRC)
6.3 Multiple Access Links and Protocols
6.4 Switched Local Area Networks
6.5 Link Virtualization: A Network as a Link Layer
6.6 Data Center Networking
6.7 Retrospective: A Day in the Life of a Web Page Request
Chapter 6 The Link layer and LANs
The Link layer and LANs

## Slide 19: Internet checksum (review)
sender:
treat segment contents as sequence of 16-bit integers
checksum: addition (1's complement sum) of segment contents
sender puts checksum value into UDP checksum field
receiver:
compute checksum of received segment
check if computed checksum equals checksum field value:
  NO - error detected
  YES - no error detected. But maybe errors nonetheless?
goal: detect "errors" (e.g., flipped bits) in transmitted packet (note: used at transport layer only)
6.2 error detection, correction

## Slide 20
6.1 Introduction
6.2 Error-Detection and -Correction Techniques
  6.2.1 Parity Checks
  6.2.2 Checksumming Methods
  6.2.3 Cyclic Redundancy Check (CRC)
6.3 Multiple Access Links and Protocols
6.4 Switched Local Area Networks
6.5 Link Virtualization: A Network as a Link Layer
6.6 Data Center Networking
6.7 Retrospective: A Day in the Life of a Web Page Request
Chapter 6 The Link layer and LANs
The Link layer and LANs

## Slide 21: Cyclic redundancy check
goal: choose CRC bits, , such that
  <D,R> exactly divisible by G (modulo 2)
  receiver knows G, divides <D,R> by G. If non-zero remainder: error detected!
  can detect all burst errors less than r+1 bits
widely used in practice (Ethernet, 802.11 WiFi, ATM)
6.2 error detection, correction
r CRC bits
data bits
bit pattern
formula for bit pattern
more powerful error-detection coding
view data bits, , as a binary number
choose bit pattern (generator),

## Slide 22: CRC example
want:
  D.2r XOR R = nG
equivalently:
  D.2r = nG XOR R
equivalently:
if we divide D.2r by G, want remainder R to satisfy:
6.2 error detection, correction
R = remainder [ ]
D.2r
G
1 0 0 1
1 0
1 0
1 0 0 1
1 0 0 1
1 0 0 1
0 0
1 1
0
1 0 1
0 1 1
1
1
0
D
R
1 0 0 1
G
1 0 1 1 1 0
0 0 0
2r
*
1
0
1
Transmitted data: 101110 011

## Slide 23: Cyclic Redundancy Check
Powerful error detection scheme
Rather than addition, binary division is used  Finite Algebra Theory (Galois Fields)
Can be easily implemented with small amount of hardware
  Shift registers
  XOR (for addition and subtraction)

## Slide 24
6.1 Introduction
6.2 Error-Detection and -Correction Techniques
6.3 Multiple Access Links and Protocols
6.4 Switched Local Area Networks
6.5 Link Virtualization: A Network as a Link Layer
6.6 Data Center Networking
6.7 Retrospective: A Day in the Life of a Web Page Request
6.3 Multiple Access Links and Protocols
Chapter 6 The Link layer and LANs
The Link layer and LANs

## Slide 25: Multiple access links, protocols
two types of "links":
point-to-point
  PPP for dial-up access
  point-to-point link between Ethernet switch, host
broadcast (shared wire or medium)
  old-fashioned Ethernet hub
  upstream HFC
  802.11 wireless LAN
shared wire (e.g.,
cabled Ethernet)
shared RF
(e.g., 802.11 WiFi)
shared RF
(satellite)
humans at a
cocktail party
(shared air, acoustical)
6.3 multiple access protocols
Notes: https://techdifferences.com/difference-between-hdlc-and-ppp.html
hybrid fiber-coaxial cable

## Slide 26: Multiple access protocols
single shared broadcast channel
two or more simultaneous transmissions by nodes: interference
  collision if node receives two or more signals at the same time
multiple access protocol
distributed algorithm that determines how nodes share channel, i.e., determine when node can transmit
communication about channel sharing must use channel itself!
  no out-of-band channel for coordination
6.3 multiple access protocols

## Slide 27: An ideal multiple access protocol
given: broadcast channel of rate R bps
desiderata:
  1. when one node wants to transmit, it can send at rate R.
  2. when M nodes want to transmit, each can send at average rate R/M
  3. fully decentralized:
    no special node to coordinate transmissions
    no synchronization of clocks, slots
  4. simple
6.3 multiple access protocols

## Slide 28
6.1 Introduction
6.2 Error-Detection and -Correction Techniques
6.3 Multiple Access Links and Protocols
  6.3.1 Channel Partitioning Protocols
  6.3.2 Random Access Protocols
  6.3.3 Taking-Turns Protocols
  6.3.4 DOCSIS: The Link-Layer Protocol for Cable Internet Access
6.4 Switched Local Area Networks
6.5 Link Virtualization: A Network as a Link Layer
6.6 Data Center Networking
6.7 Retrospective: A Day in the Life of a Web Page Request
Chapter 6 The Link layer and LANs
The Link layer and LANs

## Slide 29
6.1 Introduction
6.2 Error-Detection and -Correction Techniques
6.3 Multiple Access Links and Protocols
  6.3.1 Channel Partitioning Protocols
  6.3.2 Random Access Protocols
  6.3.3 Taking-Turns Protocols
  6.3.4 DOCSIS: The Link-Layer Protocol for Cable Internet Access
6.4 Switched Local Area Networks
6.5 Link Virtualization: A Network as a Link Layer
6.6 Data Center Networking
6.7 Retrospective: A Day in the Life of a Web Page Request
Chapter 6 The Link layer and LANs
The Link layer and LANs

## Slide 30: MAC protocols: taxonomy
three broad classes:
channel partitioning
  divide channel into smaller "pieces" (time slots, frequency, code)
  allocate piece to node for exclusive use
random access
  channel not divided, allow collisions
  "recover" from collisions
"taking turns"
  nodes take turns, but nodes with more to send can take longer turns
6.3 multiple access protocols
6.3.1 Channel Partitioning Protocols

## Slide 31: Channel partitioning MAC protocols: TDMA
TDMA: time division multiple access
access to channel in "rounds"
each station gets fixed length slot (length = packet transmission time) in each round
unused slots go idle
example: 6-station LAN, 1,3,4 have packets to send, slots 2,5,6 idle
1
3
4
1
3
4
6-slot
frame
6-slot
frame
6.3 multiple access protocols
6.3.1 Channel Partitioning Protocols

## Slide 32: Channel partitioning MAC protocols: FDMA
FDMA: frequency division multiple access
channel spectrum divided into frequency bands
each station assigned fixed frequency band
unused transmission time in frequency bands go idle
example: 6-station LAN, 1,3,4 have packet to send, frequency bands 2,5,6 idle
frequency bands
time
FDM cable
6.3 multiple access protocols
6.3.1 Channel Partitioning Protocols

## Slide 33
6.1 Introduction
6.2 Error-Detection and -Correction Techniques
6.3 Multiple Access Links and Protocols
  6.3.1 Channel Partitioning Protocols
  6.3.2 Random Access Protocols
  6.3.3 Taking-Turns Protocols
  6.3.4 DOCSIS: The Link-Layer Protocol for Cable Internet Access
6.4 Switched Local Area Networks
6.5 Link Virtualization: A Network as a Link Layer
6.6 Data Center Networking
6.7 Retrospective: A Day in the Life of a Web Page Request
Chapter 6 The Link layer and LANs
The Link layer and LANs

## Slide 34: Random access protocols
when node has packet to send
  transmit at full channel data rate R.
  no a priori coordination among nodes
two or more transmitting nodes ➜ "collision",
random access MAC protocol specifies:
  how to detect collisions
  how to recover from collisions (e.g., via delayed retransmissions)
examples of random access MAC protocols:
  slotted ALOHA
  ALOHA
  CSMA, CSMA/CD, CSMA/CA
6.3 multiple access protocols
6.3.2 Random Access Protocols

## Slide 35: Slotted ALOHA
assumptions:
all frames same size
time divided into equal size slots (time to transmit 1 frame)
nodes start to transmit only slot beginning
nodes are synchronized
if 2 or more nodes transmit in slot, all nodes detect collision
operation:
when node obtains fresh frame, transmits in next slot
  if no collision: node can send new frame in next slot
  if collision: node retransmits frame in each subsequent slot with prob. p until success
6.3 multiple access protocols
6.3.2 Random Access Protocols

## Slide 36: Slotted ALOHA
Pros:
single active node can continuously transmit at full rate of channel
highly decentralized: only slots in nodes need to be in sync
simple
Cons:
collisions, wasting slots
idle slots
nodes may be able to detect collision in less than time to transmit packet
clock synchronization
1
1
1
1
2
3
2
2
3
3
node 1
node 2
node 3
C
C
C
S
S
S
E
E
E
6.3 multiple access protocols
6.3.2 Random Access Protocols
Notes: Pros 利
Cons 弊
pros and cons 利弊

## Slide 37: Slotted ALOHA: efficiency
suppose: N nodes with many frames to send, each transmits in slot with probability p
prob that given node has success in a slot = p(1-p)N-1
prob that any node has a success = Np(1-p)N-1
max efficiency: find p* that maximizes Np(1-p)N-1
for many nodes, take limit of Np*(1-p*)N-1 as N goes to infinity, gives:
max efficiency = 1/e = .37
efficiency: long-run fraction of successful slots (many nodes, all with many frames to send)
at best: channel used for useful transmissions 37% of time!
!
6.3 multiple access protocols
6.3.2 Random Access Protocols

## Slide 38: Pure (unslotted) ALOHA
unslotted Aloha: simpler, no synchronization
when frame first arrives
  transmit immediately
collision probability increases:
  frame sent at t0 collides with other frames sent in [t0-1,t0+1]
6.3 multiple access protocols
6.3.2 Random Access Protocols

## Slide 39: Pure ALOHA efficiency
P(success by given node) = P(node transmits) .
P(no other node transmits in [t0-1,t0] .
P(no other node transmits in [t0,t0+1]
= p . (1-p)N-1 . (1-p)N-1
= p . (1-p)2(N-1)
… choosing optimum p and then letting N
= 1/(2e) = .18
even worse than slotted Aloha!
6.3 multiple access protocols
6.3.2 Random Access Protocols

## Slide 40: CSMA (carrier sense multiple access)
CSMA: listen before transmit:
if channel sensed idle, transmit entire frame
if channel sensed busy, defer transmission
human analogy: don't interrupt others!
6.3 multiple access protocols
6.3.2 Random Access Protocols
Notes: 载波侦听多路访问

## Slide 41: CSMA collisions
collisions can still occur: propagation delay means two nodes may not hear each other's transmission
collision: entire packet transmission time wasted
  distance & propagation delay play role in in determining collision probability
spatial layout of nodes
6.3 multiple access protocols
6.3.2 Random Access Protocols
D
B
A
C

## Slide 42: CSMA/CD (collision detection)
CSMA/CD: carrier sensing, deferral as in CSMA
  collisions detected within short time
  colliding transmissions aborted, reducing channel wastage
collision detection:
  easy in wired LANs: measure signal strengths, compare transmitted, received signals
  difficult in wireless LANs: received signal strength overwhelmed by local transmission strength
human analogy: the polite conversationalist
6.3 multiple access protocols
6.3.2 Random Access Protocols
Notes: 冲突检测

## Slide 43: CSMA/CD (collision detection)
spatial layout of nodes
6.3 multiple access protocols
6.3.2 Random Access Protocols
collision detected,
abort transmission

## Slide 44: Ethernet CSMA/CD algorithm
1. NIC receives datagram from network layer, creates frame
2. If NIC senses channel idle, starts frame transmission. If NIC senses channel busy, waits until channel idle, then transmits.
3. If NIC transmits entire frame without detecting another transmission, NIC is done with frame !
4. If NIC detects another transmission while transmitting, aborts and sends jam signal
5. After aborting, NIC enters binary (exponential) backoff:
  after mth collision, NIC chooses K at random from {0,1,2, …, 2m-1}. NIC waits K·512 bit times, returns to Step 2
  longer backoff interval with more collisions
6.3 multiple access protocols
6.3.2 Random Access Protocols
Notes: truncated binary exponential backoff: 截断二进指数退避
NIC: Network interface card

## Slide 45: CSMA/CD efficiency
tprop = max prop delay between 2 nodes in LAN
ttrans = time to transmit max-size frame
6.3 multiple access protocols
efficiency goes to 1
  as tprop goes to 0
  as ttrans goes to infinity
better performance than ALOHA: and simple, cheap, decentralized!
6.3.2 Random Access Protocols

## Slide 46
6.1 Introduction
6.2 Error-Detection and -Correction Techniques
6.3 Multiple Access Links and Protocols
  6.3.1 Channel Partitioning Protocols
  6.3.2 Random Access Protocols
  6.3.3 Taking-Turns Protocols
  6.3.4 DOCSIS: The Link-Layer Protocol for Cable Internet Access
6.4 Switched Local Area Networks
6.5 Link Virtualization: A Network as a Link Layer
6.6 Data Center Networking
6.7 Retrospective: A Day in the Life of a Web Page Request
Chapter 6 The Link layer and LANs
The Link layer and LANs

## Slide 47: "Taking turns" MAC protocols
channel partitioning MAC protocols:
    share channel efficiently and fairly at high load
    inefficient at low load: delay in channel access, 1/N bandwidth allocated even if only 1 active node!
random access MAC protocols
    efficient at low load: single node can fully utilize channel
    high load: collision overhead
"taking turns" protocols
  look for best of both worlds!
6.3 multiple access protocols
6.3.3 Taking-Turns Protocols
Notes: overhead: 开销, 费用

## Slide 48: "Taking turns" MAC protocols
polling:
master node "invites" slave nodes to transmit in turn
typically used with "dumb" slave devices
concerns:
  polling overhead
  latency
  single point of failure (master)
master
slaves
poll
data
data
6.3 multiple access protocols
6.3.3 Taking-Turns Protocols
Notes: Polling: 轮询
dumb slave devices are devices that wait for their turn to transmit data as directed by the master node. They do not have the capability to sense the network status or make decisions on when to transmit on their own. This setup is often used in scenarios where simplicity and centralized control are more important than individual device intelligence.
Overall, a dumb slave device is a network device that lacks autonomy and relies on external commands or instructions for its operation, making it a passive participant in the network communication process.

## Slide 49: "Taking turns" MAC protocols
token passing:
control token passed from one node to next sequentially.
token message
concerns:
  token overhead
  latency
  single point of failure (token)
T
data
(nothing
to send)
T
6.3 multiple access protocols
6.3.3 Taking-Turns Protocols

## Slide 50
6.1 Introduction
6.2 Error-Detection and -Correction Techniques
6.3 Multiple Access Links and Protocols
  6.3.1 Channel Partitioning Protocols
  6.3.2 Random Access Protocols
  6.3.3 Taking-Turns Protocols
  6.3.4 DOCSIS: The Link-Layer Protocol for Cable Internet Access
6.4 Switched Local Area Networks
6.5 Link Virtualization: A Network as a Link Layer
6.6 Data Center Networking
6.7 Retrospective: A Day in the Life of a Web Page Request
Chapter 6 The Link layer and LANs
The Link layer and LANs

## Slide 51: Cable access network
cable headend
CMTS
ISP
cable modem
termination system
multiple downstream (broadcast) FDM channels: up to 1.6 Gbps/channel
  single CMTS transmits into channels
multiple upstream channels (up to 1 Gbps/channel)
  multiple access: all users contend (random access) for certain upstream channel time slots; others assigned TDM
cable
modem
splitter
…
…
Internet frames, TV channels, control transmitted
downstream at different frequencies
upstream Internet frames, TV control, transmitted
upstream at different frequencies in time slots
6.3 multiple access protocols
6.3.4 DOCSIS: The Link-Layer Protocol for Cable Internet Access

## Slide 52: Cable access network
DOCSIS: data over cable service interface spec
FDM over upstream, downstream frequency channels
TDM upstream: some slots assigned, some have contention
  downstream MAP frame: assigns upstream slots
  request for upstream slots (and data) transmitted random access (binary backoff) in selected slots
MAP frame for
Interval [t1, t2]
Residences with cable modems
Downstream channel i
Upstream channel j
t1
t2
Assigned minislots containing cable modem
upstream data frames
Minislots containing
minislots request frames
cable headend
CMTS
6.3 multiple access protocols
6.3.4 DOCSIS: The Link-Layer Protocol for Cable Internet Access
Notes: truncated binary exponential backoff: 截断二进制指数退避

## Slide 53: Summary of MAC protocols
channel partitioning, by time, frequency or code
  Time Division, Frequency Division
random access (dynamic),
  ALOHA, S-ALOHA, CSMA, CSMA/CD
  carrier sensing: easy in some technologies (wire), hard in others (wireless)
  CSMA/CD used in Ethernet
  CSMA/CA used in 802.11
taking turns
  polling from central site, token passing
  Bluetooth, FDDI, token ring
6.3 multiple access protocols
Notes: the fiber distributed data interface (FDDI)
CSMA/CA(Carrier Sense Multiple Access with Collision Avoidance)：带有冲突避免的载波监听多路访问

## Slide 54: Homework this week
Problems of Chapter 6:
P1
P5
P17
P19
Network Layer - the control plane

## Slide 55
6.1 Introduction
6.2 Error-Detection and -Correction Techniques
6.3 Multiple Access Links and Protocols
6.4 Switched Local Area Networks
6.5 Link Virtualization: A Network as a Link Layer
6.6 Data Center Networking
6.7 Retrospective: A Day in the Life of a Web Page Request
6.4 Switched Local Area Networks
Chapter 6 The Link layer and LANs
The Link layer and LANs

## Slide 56
6.1 Introduction
6.2 Error-Detection and -Correction Techniques
6.3 Multiple Access Links and Protocols
6.4 Switched Local Area Networks
  6.4.1 Link-Layer Addressing and ARP
  6.4.2 Ethernet
  6.4.3 Link-Layer Switches
  6.4.4 Virtual Local Area Networks (VLANs)
6.5 Link Virtualization: A Network as a Link Layer
6.6 Data Center Networking
6.7 Retrospective: A Day in the Life of a Web Page Request
Chapter 6 The Link layer and LANs
The Link layer and LANs

## Slide 57
6.1 Introduction
6.2 Error-Detection and -Correction Techniques
6.3 Multiple Access Links and Protocols
6.4 Switched Local Area Networks
  6.4.1 Link-Layer Addressing and ARP
  6.4.2 Ethernet
  6.4.3 Link-Layer Switches
  6.4.4 Virtual Local Area Networks (VLANs)
6.5 Link Virtualization: A Network as a Link Layer
6.6 Data Center Networking
6.7 Retrospective: A Day in the Life of a Web Page Request
Chapter 6 The Link layer and LANs
The Link layer and LANs

## Slide 58: MAC addresses
32-bit IP address:
  network-layer address for interface
  used for layer 3 (network layer) forwarding
MAC (or LAN or physical or Ethernet) address:
  function: used "locally" to get frame from one interface to another physically-connected interface (same network, in IP-addressing sense)
  48 bit MAC address (for most LANs) burned in NIC ROM, also sometimes software settable
  e.g.: 1A-2F-BB-76-09-AD
hexadecimal (base 16) notation
(each "numeral" represents 4 bits)
6.4 LANs
6.4.1 Link-Layer Addressing and ARP

## Slide 59: MAC addresses
each adapter interface on LAN
has unique 48-bit MAC address
has a locally unique 32-bit IP address (as we’ve seen)
adapter interface
1A-2F-BB-76-09-AD
58-23-D7-FA-20-B0
0C-C4-11-6F-E3-98
71-65-F7-2B-08-53
LAN
(wired or
wireless)
6.4 LANs
137.196.7.78
137.196.7.14
137.196.7.88
137.196.7.23
6.4.1 Link-Layer Addressing and ARP

## Slide 60: MAC addresses
MAC address allocation administered by IEEE
manufacturer buys portion of MAC address space (to assure uniqueness)
analogy:
  MAC address: like Social Security Number
  IP address: like postal address, zip code
MAC flat address ➜ portability
  can move LAN card from one LAN to another
IP hierarchical address not portable
  address depends on IP subnet to which node is attached
6.4 LANs
6.4.1 Link-Layer Addressing and ARP

## Slide 61: ARP: address resolution protocol
ARP table: each IP node (host, router) on LAN has table
  IP/MAC address mappings for some LAN nodes:
< IP address; MAC address; TTL>
  TTL (Time To Live): time after which address mapping will be forgotten (typically 20 min)
Question: how to determine
interface's MAC address, knowing its IP address?
1A-2F-BB-76-09-AD
58-23-D7-FA-20-B0
0C-C4-11-6F-E3-98
71-65-F7-2B-08-53
LAN
137.196.7.23
137.196.7.78
137.196.7.14
137.196.7.88
6.4 LANs
6.4.1 Link-Layer Addressing and ARP

## Slide 62: ARP protocol in action
58-23-D7-FA-20-B0
137.196.7.14
B
C
D
TTL
71-65-F7-2B-08-53
137.196.7.23
A
ARP table in A
IP addr
MAC addr
TTL
example: A wants to send datagram to B
  B’s MAC address not in A’s ARP table, so A uses ARP to find B’s MAC address
A broadcasts ARP query, containing B's IP addr
  destination MAC address = FF-FF-FF-FF-FF-FF
  all nodes on LAN receive ARP query
1
Source MAC: 71-65-F7-2B-08-53
Source IP: 137.196.7.23
Target IP address: 137.196.7.14
…
1
Ethernet frame (sent to FF-FF-FF-FF-FF-FF)
6.4.1 Link-Layer Addressing and ARP

## Slide 63: ARP protocol in action
58-23-D7-FA-20-B0
137.196.7.14
B
C
D
TTL
71-65-F7-2B-08-53
137.196.7.23
A
ARP table in A
IP addr
MAC addr
TTL
B replies to A with ARP response, giving its MAC address
2
Target IP address: 137.196.7.14
Target MAC address:
58-23-D7-FA-20-B0
…
2
ARP message into Ethernet frame (sent to 71-65-F7-2B-08-53)
example: A wants to send datagram to B
  B’s MAC address not in A’s ARP table, so A uses ARP to find B’s MAC address
6.4.1 Link-Layer Addressing and ARP

## Slide 64: ARP protocol in action
58-23-D7-FA-20-B0
137.196.7.14
B
C
D
TTL
71-65-F7-2B-08-53
137.196.7.23
A
ARP table in A
IP addr
MAC addr
TTL
A receives B’s reply, adds B entry into its local ARP table
3
137.196.
7.14
58-23-D7-FA-20-B0
500
example: A wants to send datagram to B
  B’s MAC address not in A’s ARP table, so A uses ARP to find B’s MAC address
6.4.1 Link-Layer Addressing and ARP

## Slide 65: ARP protocol in action
A wants to send datagram to B
  B's MAC address not in A's ARP table.
A broadcasts ARP query packet, containing B's IP address
  destination MAC address = FF-FF-FF-FF-FF-FF
  all nodes on LAN receive ARP query
B receives ARP packet, replies to A with its (B's) MAC address
  frame sent to A's MAC address (unicast)
A caches (saves) IP-to-MAC address pair in its ARP table until information becomes old (times out)
  soft state: information that times out (goes away) unless refreshed
ARP is "plug-and-play":
  nodes create their ARP tables without intervention from net administrator
6.4 LANs
6.4.1 Link-Layer Addressing and ARP

## Slide 66
TELNET
HTTP
FTP
SMTP
DNS
RIP
SNMP
DHCP
TCP
UDP
IP
ICMP
OSPF
ARP
RARP
application layer
transport
layer
network
layer
The Internet Hourglass
link
layer
ethernet
802.11
SONET
ATM
6.4 LANs
6.4.1 Link-Layer Addressing and ARP

## Slide 67: Routing to another subnet: addressing
walkthrough: send datagram from A to B via R
  focus on addressing – at IP (datagram) and MAC layer (frame) levels
  assume A knows B's IP address
  assume A knows IP address of first hop router, R (how?)
  assume A knows R's MAC address (how?)
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
6.4 LANs
6.4.1 Link-Layer Addressing and ARP

## Slide 68: Routing to another subnet: addressing
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP
Eth
Phy
IP src: 111.111.111.111
IP dest: 222.222.222.222
  A creates IP datagram with IP source A, destination B
  A creates link-layer frame with R's MAC address as destination address, frame contains A-to-B IP datagram
MAC src: 74-29-9C-E8-FF-55
MAC dest: E6-E9-00-17-BB-4B
6.4 LANs
6.4.1 Link-Layer Addressing and ARP

## Slide 69: Routing to another subnet: addressing
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP
Eth
Phy
  frame sent from A to R
IP
Eth
Phy
  frame received at R, datagram removed, passed up to IP
MAC src: 74-29-9C-E8-FF-55
MAC dest: E6-E9-00-17-BB-4B
IP src: 111.111.111.111
IP dest: 222.222.222.222
IP src: 111.111.111.111
IP dest: 222.222.222.222
6.4 LANs
6.4.1 Link-Layer Addressing and ARP

## Slide 70: Routing to another subnet: addressing
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP src: 111.111.111.111
IP dest: 222.222.222.222
  R forwards datagram with IP source A, destination B
  R creates link-layer frame with B's MAC address as destination address, frame contains A-to-B IP datagram
MAC src: 1A-23-F9-CD-06-9B
MAC dest: 49-BD-D2-C7-56-2A
IP
Eth
Phy
IP
Eth
Phy
6.4 LANs
6.4.1 Link-Layer Addressing and ARP

## Slide 71: Routing to another subnet: addressing
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
  R forwards datagram with IP source A, destination B
  R creates link-layer frame with B's MAC address as destination address, frame contains A-to-B IP datagram
IP src: 111.111.111.111
IP dest: 222.222.222.222
MAC src: 1A-23-F9-CD-06-9B
MAC dest: 49-BD-D2-C7-56-2A
IP
Eth
Phy
IP
Eth
Phy
6.4 LANs
6.4.1 Link-Layer Addressing and ARP

## Slide 72: Routing to another subnet: addressing
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
  R forwards datagram with IP source A, destination B
  R creates link-layer frame with B's MAC address as dest, frame contains A-to-B IP datagram
IP src: 111.111.111.111
IP dest: 222.222.222.222
MAC src: 1A-23-F9-CD-06-9B
MAC dest: 49-BD-D2-C7-56-2A
IP
Eth
Phy
6.4 LANs
6.4.1 Link-Layer Addressing and ARP

## Slide 73
6.1 Introduction
6.2 Error-Detection and -Correction Techniques
6.3 Multiple Access Links and Protocols
6.4 Switched Local Area Networks
  6.4.1 Link-Layer Addressing and ARP
  6.4.2 Ethernet
  6.4.3 Link-Layer Switches
  6.4.4 Virtual Local Area Networks (VLANs)
6.5 Link Virtualization: A Network as a Link Layer
6.6 Data Center Networking
6.7 Retrospective: A Day in the Life of a Web Page Request
Chapter 6 The Link layer and LANs
The Link layer and LANs

## Slide 74: Ethernet
"dominant" wired LAN technology:
single chip, multiple speeds (e.g., Broadcom BCM5761)
first widely used LAN technology
simpler, cheap
kept up with speed race: 10 Mbps – 400 Gbps
Metcalfe's Ethernet sketch
6.4 LANs
Novell
6.4.2 Ethernet
Notes: https://blog.csdn.net/weixin_42229404/article/details/81227377

## Slide 75: Ethernet: physical topology
bus: popular through mid 90s
  all nodes in same collision domain (can collide with each other)
star: prevails today
  active switch in center
  each "spoke" runs a (separate) Ethernet protocol (nodes do not collide with each other)
switch
bus: coaxial cable
star
6.4 LANs
6.4.2 Ethernet

## Slide 76: Ethernet frame structure
sending adapter encapsulates IP datagram (or other network layer protocol packet) in Ethernet frame
preamble:
7 bytes with pattern 10101010 followed by one byte with pattern 10101011
used to synchronize receiver, sender clock rates
dest.
address
source
address
data (payload)
CRC
preamble
type
6.4 LANs
6.4.2 Ethernet

## Slide 77: Ethernet frame structure (more)
addresses: 6 byte source, destination MAC addresses
  if adapter receives frame with matching destination address, or with broadcast address (e.g. ARP packet), it passes data in frame to network layer protocol
  otherwise, adapter discards frame
type: indicates higher layer protocol (mostly IP but others possible, e.g., Novell IPX, AppleTalk)
CRC: cyclic redundancy check at receiver
  error detected: frame is dropped
dest.
address
source
address
data (payload)
CRC
preamble
type
6.4 LANs
6.4.2 Ethernet

## Slide 78: Ethernet: unreliable, connectionless
connectionless: no handshaking between sending and receiving NICs
unreliable: receiving NIC doesn't send acks or nacks to sending NIC
  data in dropped frames recovered only if initial sender uses higher layer rdt (e.g., TCP), otherwise dropped data lost
Ethernet's MAC protocol: unslotted CSMA/CD with binary backoff
6.4 LANs
6.4.2 Ethernet

## Slide 79: 802.3 Ethernet standards: link & physical layers
many different Ethernet standards
  common MAC protocol and frame format
  different speeds: 2 Mbps, 10 Mbps, 100 Mbps, 1Gbps, 10 Gbps, 40 Gbps
  different physical layer media: fiber, cable
application
transport
network
link
physical
MAC protocol
and frame format
100BASE-TX
100BASE-T4
100BASE-FX
100BASE-T2
100BASE-SX
100BASE-BX
fiber physical layer
copper (twister
pair) physical layer
6.4 LANs
6.4.2 Ethernet

## Slide 80
6.1 Introduction
6.2 Error-Detection and -Correction Techniques
6.3 Multiple Access Links and Protocols
6.4 Switched Local Area Networks
  6.4.1 Link-Layer Addressing and ARP
  6.4.2 Ethernet
  6.4.3 Link-Layer Switches
  6.4.4 Virtual Local Area Networks (VLANs)
6.5 Link Virtualization: A Network as a Link Layer
6.6 Data Center Networking
6.7 Retrospective: A Day in the Life of a Web Page Request
Chapter 6 The Link layer and LANs
The Link layer and LANs

## Slide 81: Ethernet switch
link-layer device: takes an active role
  store, forward Ethernet frames
  examine incoming frame's MAC address, selectively forward frame to one-or-more outgoing links when frame is to be forwarded on segment
  uses CSMA/CD to access segment
transparent
  hosts are unaware of presence of switches
plug-and-play, self-learning
  switches do not need to be configured
6.4 LANs
6.4.3 Link-Layer Switches
Notes: segment = network segment

## Slide 82: Switch: multiple simultaneous transmissions
switching: A-to-A' and B-to-B' can transmit simultaneously, without collisions
switch with six interfaces
(1,2,3,4,5,6)
A
A'
B
B'
C
C'
1
2
3
4
5
6
6.4 LANs
hosts have dedicated, direct connection to switch
switches buffer packets
Ethernet protocol used on each incoming link
  no collisions; full duplex
  each link is its own collision domain
6.4.3 Link-Layer Switches

## Slide 83: Switch: multiple simultaneous transmissions
but A-to-A’ and C to A’ can not happen simultaneously
switch with six interfaces
(1,2,3,4,5,6)
A
A'
B
B'
C
C'
1
2
3
4
5
6
6.4 LANs
hosts have dedicated, direct connection to switch
switches buffer packets
Ethernet protocol used on each incoming link
  no collisions; full duplex
  each link is its own collision domain
6.4.3 Link-Layer Switches

## Slide 84: Switch forwarding table
Q: how does switch know A' reachable via interface 4, B' reachable via interface 5?
switch with six interfaces
(1,2,3,4,5,6)
A
A'
B
B'
C
C'
1
2
3
4
5
6
A: each switch has a switch table, each entry:
  (MAC address of host, interface to reach host, time stamp)
  looks like a routing table!
Q: how are entries created, maintained in switch table?
  something like a routing protocol? No!
6.4 LANs
6.4.3 Link-Layer Switches

## Slide 85: Switch: self-learning
A
A'
B
B'
C
C'
1
2
3
4
5
6
switch learns which hosts can be reached through which interfaces
  when frame received, switch "learns" location of sender: incoming LAN segment
  records sender/location pair in switch table
A A'
Source: A
Dest: A'
MAC addr interface TTL
Switch table
(initially empty)
A
1
60
6.4 LANs
6.4.3 Link-Layer Switches

## Slide 86: Switch: frame filtering/forwarding
when frame received at switch:
  1. record incoming link, MAC address of sending host
  2. index switch table using MAC destination address
  3. if entry found for destination then {
  if destination on segment from which frame arrived then drop frame
  else forward frame on interface indicated by entry
  }
  else flood /* forward on all interfaces except arriving
  interface */
6.4 LANs
6.4.3 Link-Layer Switches

## Slide 87: Self-learning, forwarding: example
A
A'
B
B'
C
C'
1
2
3
4
5
6
A A'
Source: A
Dest: A'
MAC addr interface TTL
switch table
(initially empty)
A
1
60
A A'
A A'
A A'
A A'
A A'
frame destination, A', location unknown:
flood
A' A
destination A location known:
A'
4
60
selectively send
on just one link
6.4 LANs
6.4.3 Link-Layer Switches

## Slide 88: Interconnecting switches
self-learning switches can be connected together:
Q: sending from A to G - how does S1 know to forward frame destined to G via S4 and S3?
A: self learning! (works exactly the same as in single-switch case!)
A
B
S1
C
D
E
F
S2
S4
S3
H
I
G
6.4 LANs
6.4.3 Link-Layer Switches

## Slide 89: Self-learning multi-switch example
Suppose A sends frame to G, G responds to A
Q: show switch tables and packet forwarding in S1, S2, S3, S4
A
B
S1
C
D
E
F
S2
S4
S3
H
I
G
6.4 LANs
6.4.3 Link-Layer Switches

## Slide 90: Institutional network
to external
network
router
IP subnet
mail server
web server
6.4 LANs
6.4.3 Link-Layer Switches

## Slide 91: Switches vs. routers
both are store-and-forward:
routers: network-layer devices (examine network-layer headers)
switches: link-layer devices (examine link-layer headers)
both have forwarding tables:
routers: compute tables using routing algorithms, IP addresses
switches: learn forwarding table using flooding, learning, MAC addresses
application
transport
network
link
physical
network
link
physical
link
physical
switch
datagram
application
transport
network
link
physical
frame
frame
frame
datagram
6.4 LANs
6.4.3 Link-Layer Switches

## Slide 92
6.1 Introduction
6.2 Error-Detection and -Correction Techniques
6.3 Multiple Access Links and Protocols
6.4 Switched Local Area Networks
  6.4.1 Link-Layer Addressing and ARP
  6.4.2 Ethernet
  6.4.3 Link-Layer Switches
  6.4.4 Virtual Local Area Networks (VLANs)
6.5 Link Virtualization: A Network as a Link Layer
6.6 Data Center Networking
6.7 Retrospective: A Day in the Life of a Web Page Request
Chapter 6 The Link layer and LANs
The Link layer and LANs

## Slide 93: VLANs: motivation
6.4 LANs
6.4.4 Virtual Local Area Networks (VLANs)
EE
single broadcast domain:
  scaling: all layer-2 broadcast traffic (ARP, DHCP, unknown MAC) must cross entire LAN
  efficiency, security, privacy issues
Q: what happens as LAN sizes scale, users change point of attachment?
Computer
Science

## Slide 94: VLANs: motivation
6.4 LANs
6.4.4 Virtual Local Area Networks (VLANs)
administrative issues:
  CS user moves office to EE - physically attached to EE switch, but wants to remain logically attached to CS switch
EE
single broadcast domain:
  scaling: all layer-2 broadcast traffic (ARP, DHCP, unknown MAC) must cross entire LAN
  efficiency, security, privacy, efficiency issues
Q: what happens as LAN sizes scale, users change point of attachment?
Computer
Science

## Slide 95: Port-based VLANs
port-based VLAN: switch ports grouped (by switch management software) so that single physical switch ……
switch(es) supporting VLAN capabilities can be configured to define multiple virtual LANS over single physical LAN infrastructure.
Virtual Local
Area Network
1
8
9
16
10
2
7
…
Electrical Engineering
(VLAN ports 1-8)
Computer Science
(VLAN ports 9-15)
15
…
Electrical Engineering
(VLAN ports 1-8)
…
1
8
2
7
9
16
10
15
…
Computer Science
(VLAN ports 9-16)
… operates as multiple virtual switches
6.4 LANs
6.4.4 Virtual Local Area Networks (VLANs)

## Slide 96: Port-based VLANs
1
8
9
16
10
2
7
…
Electrical Engineering
(VLAN ports 1-8)
Computer Science
(VLAN ports 9-15)
15
…
traffic isolation: frames to/from ports 1-8 can only reach ports 1-8
  can also define VLAN based on MAC addresses of endpoints, rather than switch port
dynamic membership: ports can be dynamically assigned among VLANs
router
forwarding between VLANS: done via routing (just as with separate switches)
  in practice vendors sell combined switches plus routers
6.4 LANs
6.4.4 Virtual Local Area Networks (VLANs)

## Slide 97: VLANS spanning multiple switches
trunk port: carries frames between VLANS defined over multiple physical switches
  frames forwarded within VLAN between switches can't be vanilla 802.1 frames (must carry VLAN ID info)
  802.1q protocol adds/removed additional header fields for frames forwarded between trunk ports
1
8
9
10
2
7
…
Electrical Engineering
(VLAN ports 1-8)
Computer Science
(VLAN ports 9-15)
15
…
2
7
3
Ports 2,3,5 belong to EE VLAN
Ports 4,6,7,8 belong to CS VLAN
5
4
6
8
16
1
6.4 LANs
6.4.4 Virtual Local Area Networks (VLANs)
Notes: In information technology, vanilla (pronounced vah-NIHL-uh ) is an adjective meaning plain or basic. The unfeatured version of a product is sometimes referred to as the vanilla version. The term is based on the fact that vanilla is the most popular or at least the most commonly served flavor of ice cream. Or, as Eric Raymond, editor of The New Hacker's Dictionary , puts it, the default ice cream.
IBM's Book Master product, a text publishing system used in mainframe environments, provides a default way, called vanilla , to specify which parts of the book to publish, and another fancier way to specify it, called mocha .
Some Web sites with frames call the simpler version of their site the vanilla version.

## Slide 98: 802.1Q VLAN frame format
type
2-byte Tag Protocol Identifier
(value: 81-00)
Tag Control Information (12 bit VLAN ID field,
3 bit priority field like IP TOS)
Recomputed
CRC
802.1 frame
802.1Q frame
dest.
address
source
address
data (payload)
CRC
preamble
dest.
address
source
address
preamble
data (payload)
CRC
type
6.4 LANs
6.4.4 Virtual Local Area Networks (VLANs)
Notes: ToS: Terms of Service

## Slide 99
6.1 Introduction
6.2 Error-Detection and -Correction Techniques
6.3 Multiple Access Links and Protocols
6.4 Switched Local Area Networks
6.5 Link Virtualization: A Network as a Link Layer
6.6 Data Center Networking
6.7 Retrospective: A Day in the Life of a Web Page Request
6.5 Link Virtualization: A Network as a Link Layer
Chapter 6 The Link layer and LANs
The Link layer and LANs

## Slide 100
6.1 Introduction
6.2 Error-Detection and -Correction Techniques
6.3 Multiple Access Links and Protocols
6.4 Switched Local Area Networks
6.5 Link Virtualization: A Network as a Link Layer
  6.5.1 Multiprotocol Label Switching (MPLS)
6.6 Data Center Networking
6.7 Retrospective: A Day in the Life of a Web Page Request
Chapter 6 The Link layer and LANs
The Link layer and LANs

## Slide 101
6.1 Introduction
6.2 Error-Detection and -Correction Techniques
6.3 Multiple Access Links and Protocols
6.4 Switched Local Area Networks
6.5 Link Virtualization: A Network as a Link Layer
  6.5.1 Multiprotocol Label Switching (MPLS)
6.6 Data Center Networking
6.7 Retrospective: A Day in the Life of a Web Page Request
Chapter 6 The Link layer and LANs
The Link layer and LANs

## Slide 102: Multiprotocol label switching (MPLS)
initial goal: high-speed IP forwarding using fixed length label (instead of IP address)
  fast lookup using fixed length identifier (rather than longest prefix matching)
  borrowing ideas from Virtual Circuit (VC) approach
  but IP datagram still keeps IP address!
6.5 link virtualization: MPLS
RFC 3031
RFC 3032
6.5.1 Multiprotocol Label Switching (MPLS)
label
Exp
S
TTL
20
3
1
5
remainder of Ethernet frame, including IP header with IP source, destination addresses
MPLS header
Ethernet
header
remainder of Ethernet frame, including IP header with IP source, destination addresses

## Slide 103: MPLS capable routers
a.k.a. label-switched router
forward packets to outgoing interface based only on label value (don't inspect IP address)
  MPLS forwarding table distinct from IP forwarding tables
flexibility: MPLS forwarding decisions can differ from those of IP
  use destination and source addresses to route flows to same destination differently (traffic engineering)
  re-route flows quickly if link fails: pre-computed backup paths (useful for VoIP)
6.5 link virtualization: MPLS
6.5.1 Multiprotocol Label Switching (MPLS)

## Slide 104: MPLS versus IP paths
R2
D
R3
R5
A
R6
IP router
IP routing: path to destination determined by destination address alone
R4
6.5 link virtualization: MPLS
6.5.1 Multiprotocol Label Switching (MPLS)

## Slide 105: MPLS versus IP paths
R2
D
R3
R4
R5
A
R6
IP-only
router
IP routing: path to destination determined by destination address alone
MPLS and
IP router
MPLS routing: path to destination can be based on source and destination address
  fast reroute: precompute backup routes in case of link failure
entry router (R4) can use different MPLS routes to A based, e.g., on source address
6.5 link virtualization: MPLS
6.5.1 Multiprotocol Label Switching (MPLS)

## Slide 106: MPLS signaling
modify OSPF, IS-IS link-state flooding protocols to carry info used by MPLS routing,
  e.g., link bandwidth, amount of “reserved” link bandwidth
D
R4
R5
A
R6
entry MPLS router uses RSVP-TE signaling protocol to set up MPLS forwarding at downstream routers
modified
link state
flooding
RSVP-TE
6.5 link virtualization: MPLS
RFC 3468 memo
RFC 3209 Proposed Standard
6.5.1 Multiprotocol Label Switching (MPLS)

## Slide 107: MPLS forwarding tables
6.5 link virtualization: MPLS
in out out
label label dest interface
6 - A 0
in out out
label label dest interface
10 6 A 1
12 9 D 0
in out out
label label dest interface
8 6 A 0
in out out
label label dest interface
10 A 0
12 D 0
8 A 1
R2
D
R3
R5
A
R6
R4
R1
0
1
0
0
1
0
6.5.1 Multiprotocol Label Switching (MPLS)

## Slide 108
6.1 Introduction
6.2 Error-Detection and -Correction Techniques
6.3 Multiple Access Links and Protocols
6.4 Switched Local Area Networks
6.5 Link Virtualization: A Network as a Link Layer
6.6 Data Center Networking
6.7 Retrospective: A Day in the Life of a Web Page Request
6.6 Data Center Networking
Chapter 6 The Link layer and LANs
The Link layer and LANs

## Slide 109
6.1 Introduction
6.2 Error-Detection and -Correction Techniques
6.3 Multiple Access Links and Protocols
6.4 Switched Local Area Networks
6.5 Link Virtualization: A Network as a Link Layer
6.6 Data Center Networking
  6.6.1 Data Center Architectures
  6.6.2 Trends in Data Center Networking
6.7 Retrospective: A Day in the Life of a Web Page Request
Chapter 6 The Link layer and LANs
The Link layer and LANs

## Slide 110
6.1 Introduction
6.2 Error-Detection and -Correction Techniques
6.3 Multiple Access Links and Protocols
6.4 Switched Local Area Networks
6.5 Link Virtualization: A Network as a Link Layer
6.6 Data Center Networking
  6.6.1 Data Center Architectures
  6.6.2 Trends in Data Center Networking
6.7 Retrospective: A Day in the Life of a Web Page Request
Chapter 6 The Link layer and LANs
The Link layer and LANs

## Slide 111: Data center networks
10's to 100's of thousands of hosts, often closely coupled, in close proximity:
  e-business (e.g. Amazon)
  content-servers (e.g., YouTube, TikTok, Apple, Microsoft)
  search engines, data mining (e.g., Google, Baidu)
challenges:
  multiple applications, each serving massive numbers of clients
  reliability
  managing/balancing load, avoiding processing, networking, data bottlenecks
Inside a 40-ft Microsoft container,
Chicago data center
6.6 data center networking
6.6.1 Data Center Architectures

## Slide 112: Datacenter networks: network elements
6.6 data center networking
Server racks
20- 40 server blades: hosts
Top of Rack (TOR) switch
one per rack
40-100Gbps Ethernet to blades
Tier-2 switches
connecting to ~16 TORs below
Tier-1 switches
connecting to ~16 T-2s below
Border routers
connections outside datacenter
…
…
…
…
…
…
…
…
6.6.1 Data Center Architectures
Notes: TOR(Top of Rack): 机架顶部
blade: 刀片机

## Slide 113: Datacenter networks: network elements
6.6 data center networking
Facebook F16 data center network topology:
6.6.1 Data Center Architectures

## Slide 114: Datacenter networks: multipath
9
10
11
12
13
14
15
16
two disjoint paths highlighted between racks 1 and 11
rich interconnection among switches, racks:
  increased throughput between racks (multiple routing paths possible)
  increased reliability via redundancy
6.6 data center networking
6.6.1 Data Center Architectures

## Slide 115: Datacenter networks: application-layer routing
…
…
…
…
…
…
…
…
Load
balancer
Internet
load balancer: application-layer routing
receives external client requests
directs workload within data center
returns results to external client (hiding data center internals from client)
6.6 data center networking
6.6.1 Data Center Architectures

## Slide 116
6.1 Introduction
6.2 Error-Detection and -Correction Techniques
6.3 Multiple Access Links and Protocols
6.4 Switched Local Area Networks
6.5 Link Virtualization: A Network as a Link Layer
6.6 Data Center Networking
  6.6.1 Data Center Architectures
  6.6.2 Trends in Data Center Networking
6.7 Retrospective: A Day in the Life of a Web Page Request
Chapter 6 The Link layer and LANs
The Link layer and LANs

## Slide 117: Datacenter networks: protocol innovations
link layer:
  RoCE: remote DMA (RDMA) over Converged Ethernet
transport layer:
  ECN (explicit congestion notification) used in transport-layer congestion control (DCTCP, DCQCN)
  experimentation with hop-by-hop (backpressure) congestion control
routing, management:
  SDN widely used within/among organizations’ datacenters
  place related services, data as close as possible (e.g., in same rack or nearby rack) to minimize tier-2, tier-1 communication
6.6 data center networking
6.6.2 Trends in Data Center Networking

## Slide 118
6.1 Introduction
6.2 Error-Detection and -Correction Techniques
6.3 Multiple Access Links and Protocols
6.4 Switched Local Area Networks
6.5 Link Virtualization: A Network as a Link Layer
6.6 Data Center Networking
6.7 Retrospective: A Day in the Life of a Web Page Request
6.7 Retrospective: A Day in the Life of a Web Page Request
Chapter 6 The Link layer and LANs
The Link layer and LANs

## Slide 119
6.1 Introduction
6.2 Error-Detection and -Correction Techniques
6.3 Multiple Access Links and Protocols
6.4 Switched Local Area Networks
6.5 Link Virtualization: A Network as a Link Layer
6.6 Data Center Networking
6.7 Retrospective: A Day in the Life of a Web Page Request
  6.7.1 Getting Started: DHCP, UDP, IP, and Ethernet
  6.7.2 Still Getting Started: DNS and ARP
  6.7.3 Still Getting Started: Intra-Domain Routing to the DNS Server
  6.7.4 Web Client-Server Interaction: TCP and HTTP
Chapter 6 The Link layer and LANs
The Link layer and LANs

## Slide 120
6.1 Introduction
6.2 Error-Detection and -Correction Techniques
6.3 Multiple Access Links and Protocols
6.4 Switched Local Area Networks
6.5 Link Virtualization: A Network as a Link Layer
6.6 Data Center Networking
6.7 Retrospective: A Day in the Life of a Web Page Request
  6.7.1 Getting Started: DHCP, UDP, IP, and Ethernet
  6.7.2 Still Getting Started: DNS and ARP
  6.7.3 Still Getting Started: Intra-Domain Routing to the DNS Server
  6.7.4 Web Client-Server Interaction: TCP and HTTP
Chapter 6 The Link layer and LANs
The Link layer and LANs

## Slide 121
6.1 Introduction
6.2 Error-Detection and -Correction Techniques
6.3 Multiple Access Links and Protocols
6.4 Switched Local Area Networks
6.5 Link Virtualization: A Network as a Link Layer
6.6 Data Center Networking
6.7 Retrospective: A Day in the Life of a Web Page Request
  6.7.1 Getting Started: DHCP, UDP, IP, and Ethernet
  6.7.2 Still Getting Started: DNS and ARP
  6.7.3 Still Getting Started: Intra-Domain Routing to the DNS Server
  6.7.4 Web Client-Server Interaction: TCP and HTTP
Chapter 6 The Link layer and LANs
The Link layer and LANs

## Slide 122
6.1 Introduction
6.2 Error-Detection and -Correction Techniques
6.3 Multiple Access Links and Protocols
6.4 Switched Local Area Networks
6.5 Link Virtualization: A Network as a Link Layer
6.6 Data Center Networking
6.7 Retrospective: A Day in the Life of a Web Page Request
  6.7.1 Getting Started: DHCP, UDP, IP, and Ethernet
  6.7.2 Still Getting Started: DNS and ARP
  6.7.3 Still Getting Started: Intra-Domain Routing to the DNS Server
  6.7.4 Web Client-Server Interaction: TCP and HTTP
Chapter 6 The Link layer and LANs
The Link layer and LANs

## Slide 123
6.1 Introduction
6.2 Error-Detection and -Correction Techniques
6.3 Multiple Access Links and Protocols
6.4 Switched Local Area Networks
6.5 Link Virtualization: A Network as a Link Layer
6.6 Data Center Networking
6.7 Retrospective: A Day in the Life of a Web Page Request
  6.7.1 Getting Started: DHCP, UDP, IP, and Ethernet
  6.7.2 Still Getting Started: DNS and ARP
  6.7.3 Still Getting Started: Intra-Domain Routing to the DNS Server
  6.7.4 Web Client-Server Interaction: TCP and HTTP
Chapter 6 The Link layer and LANs
The Link layer and LANs

## Slide 124: Synthesis: a day in the life of a web request
journey down protocol stack complete!
  application, transport, network, link
putting-it-all-together: synthesis!
  goal: identify, review, understand protocols (at all layers) involved in seemingly simple scenario: requesting www page
  scenario: student attaches laptop to campus network, requests/receives www.google.com
6.7 a day in the life of a web request

## Slide 125: A day in the life: scenario
Comcast network
68.80.0.0/13
Google's network
64.233.160.0/19
64.233.169.105
web server
DNS server
school network
68.80.2.0/24
web page
browser
6.7 a day in the life of a web request

## Slide 126: A day in the life… connecting to the Internet
router
(runs DHCP)
connecting laptop needs to get its own IP address, addr of first-hop router, addr of DNS server: use DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP request encapsulated in UDP, encapsulated in IP, encapsulated in 802.3 Ethernet
Ethernet frame broadcast (dest: FFFFFFFFFFFF) on LAN, received at router running DHCP server
Ethernet demuxed to IP demuxed, UDP demuxed to DHCP
6.7 a day in the life of a web request

## Slide 127: A day in the life… connecting to the Internet
router
(runs DHCP)
DHCP server formulates DHCP ACK containing client's IP address, IP address of first-hop router for client, name & IP address of DNS server
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
encapsulation at DHCP server, frame forwarded (switch learning) through LAN, demultiplexing at client
Client now has IP address, knows name & addr of DNS
server, IP address of its first-hop router
DHCP client receives DHCP ACK reply
6.7 a day in the life of a web request

## Slide 128: A day in the life… ARP (before DNS, before HTTP)
router
(runs DHCP)
before sending HTTP request, need IP address of www.google.com: DNS
DNS
UDP
IP
Eth
Phy
DNS
DNS
DNS
DNS query created, encapsulated in UDP, encapsulated in IP, encapsulated in Eth. To send frame to router, need MAC address of router interface: ARP
ARP query broadcast, received by router, which replies with ARP reply giving MAC address of router interface
client now knows MAC address of first hop router, so can now send frame containing DNS query
ARP query
Eth
Phy
ARP
ARP
ARP reply
6.7 a day in the life of a web request

## Slide 129: A day in the life… using DNS
router
(runs DHCP)
DNS
UDP
IP
Eth
Phy
DNS
DNS
DNS
DNS
DNS
IP datagram containing DNS query forwarded via LAN switch from client to 1st hop router
IP datagram forwarded from campus network into Comcast network, routed (tables created by RIP, OSPF, IS-IS and/or BGP routing protocols) to DNS server
demuxed to DNS server
DNS server replies to client with IP address of www.google.com
Comcast network
68.80.0.0/13
DNS server
DNS
UDP
IP
Eth
Phy
DNS
DNS
DNS
DNS
6.7 a day in the life of a web request

## Slide 130: A day in the life…TCP connection carrying HTTP
router
(runs DHCP)
HTTP
TCP
IP
Eth
Phy
HTTP
to send HTTP request, client first opens TCP socket to web server
TCP SYN segment (step 1 in 3-way handshake) inter-domain routed to web server
TCP connection established!
64.233.169.105
web server
SYN
SYN
SYN
SYN
TCP
IP
Eth
Phy
SYN
SYN
SYN
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
web server responds with TCP SYNACK (step 2 in 3-way handshake)
6.7 a day in the life of a web request

## Slide 131: A day in the life… HTTP request/reply
router
(runs DHCP)
HTTP
TCP
IP
Eth
Phy
HTTP
HTTP request sent into TCP socket
IP datagram containing HTTP request routed to www.google.com
IP datagram containing HTTP reply routed back to client
64.233.169.105
web server
HTTP
TCP
IP
Eth
Phy
web server responds with HTTP reply (containing web page)
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
web page finally (!!!) displayed
6.7 a day in the life of a web request

## Slide 132: Chapter 6: summary
The Link layer and LANs
principles behind data link layer services:
  error detection, correction
  sharing a broadcast channel: multiple access
  link layer addressing
instantiation and implementation of various link layer technologies
  Ethernet
  switched LANS, VLANs
  virtualized networks as a link layer: MPLS
synthesis: a day in the life of a web request

## Slide 133: Chapter 6: let's take a breath
journey down protocol stack complete (except PHY)
solid understanding of networking principles, practice
….. course stops here …. but lots of interesting topics remain to be explored !
  wireless
  multimedia
  security
The Link layer and LANs

## Slide 134: Homework this week
Lab: https://www.github.com/network-whu/lab/
  8.Wireshark_Ethernet_ARP.docx
  Hand-in: add to your lab report, in a separate chapter
Network Layer - the control plane

## Slide 135: IEEE 802.11: multiple access
avoid collisions: 2+ nodes transmitting at same time
802.11: CSMA - sense before transmitting
  don’t collide with detected ongoing transmission by another node
802.11: no collision detection!
  difficult to sense collisions: high transmitting signal, weak received signal due to fading
  can’t sense all collisions in any case: hidden terminal, fading
  goal: avoid collisions: CSMA/CollisionAvoidance
space
A
B
C
A
B
C
A’s signal
strength
C’s signal
strength

## Slide 136: IEEE 802.11 MAC Protocol: CSMA/CA
802.11 sender
1 if sense channel idle for DIFS then
  transmit entire frame (no CD)
sender
receiver
DIFS
data
SIFS
ACK
802.11 receiver
if frame received OK
return ACK after SIFS (ACK needed due to hidden terminal problem)
2 if sense channel busy then
  start random backoff time
  timer counts down while channel idle
  transmit when timer expires
  if no ACK, increase random backoff interval, repeat 2
Notes: Short Inter-frame Spacing (SIFS)
Distributed Inter-frame Space (DIFS)

## Slide 137: Avoiding collisions (more)
idea: sender “reserves” channel use for data frames using small reservation packets
sender first transmits small request-to-send (RTS) packet to BS using CSMA
  RTSs may still collide with each other (but they’re short)
BS broadcasts clear-to-send CTS in response to RTS
CTS heard by all nodes
  sender transmits data frame
  other stations defer transmissions